## Slide 1: Data and Computer Communications
Tenth Edition
by William Stallings
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 7 “Data Link Control Protocols”.

## Slide 2: Data Link Control Protocols
Chapter 7
Notes: Our discussion so far has concerned sending signals over a transmission link .
For effective digital data communications, much more is needed to control
and manage the exchange. In this chapter, we shift our emphasis to that of
sending data over a data communications link . To achieve the necessary control,
a layer of logic is added above the physical layer discussed in Chapter 6;
this logic is referred to as data link control or a data link control protocol .
When a data link control protocol is used, the transmission medium between
systems is referred to as a data link .

## Slide 3
“A conversation forms a two-way communication link; there is a measure of symmetry between the two parties, and messages pass to and fro. There is a continual stimulus-response, cyclic action; remarks call up other remarks, and the behavior of the two individuals becomes concerted, co-operative, and directed toward some goal. This is true communication.”
—On Human Communication,
Colin Cherry
Notes: Opening quote.

## Slide 4: Data Link Control Protocols
Requirements and objectives for effective data communication between two directly connected transmitting-receiving stations:
Frame synchronization
Flow control
Error control
Addressing
Control and data
Link management
Notes: To see the need for data link control, we list some of the requirements
and objectives for effective data communication between two directly connected
transmitting-receiving stations:
• Frame synchronization: Data are sent in blocks called frames. The beginning
and end of each frame must be recognizable. We briefly introduced
this topic with the discussion of synchronous frames (Figure 6.2).
• Flow control: The sending station must not send frames at a rate faster
than the receiving station can absorb them.
• Error control: Bit errors introduced by the transmission system should
be corrected.
• Addressing: On a shared link, such as a local area network (LAN), the
identity of the two stations involved in a transmission must be specified.
• Control and data on same link: It is usually not desirable to have a
physically separate communications path for control information.
Accordingly, the receiver must be able to distinguish control information
from the data being transmitted.
• Link management: The initiation, maintenance, and termination of a
sustained data exchange require a fair amount of coordination and cooperation
among stations. Procedures for the management of this exchange
are required.

## Slide 5: Flow Control
Technique for assuring that a transmitting entity does not over-whelm a receiving entity with data
  The receiving entity typically allocates a data buffer of some maximum length for a transfer
  When data are received, the receiver must do a certain amount of processing before passing the data to the higher-level software
In the absence of flow control, the receiver’s buffer may fill up and overflow while it is processing old data
Notes: Flow control is a technique for assuring that a transmitting entity does not overwhelm a receiving entity with data. The receiving entity typically allocates a data buffer of some maximum length for a transfer. When data are received, the receiver must do a certain amount of processing before passing the data to the higher-level software. In the absence of flow control, the receiver's buffer may fill up and overflow while it is processing old data.

## Slide 6
Notes: To begin, we examine mechanisms for flow control in the absence of errors.
The model we will use is depicted in Figure 7.1a, which is a vertical time sequence
diagram. It has the advantages of showing time dependencies and illustrating the
correct send–receive relationship. Each arrow represents a single frame transiting a
data link between two stations. The data are sent in a sequence of frames, with each
frame containing a portion of the data and some control information. The time it
takes for a station to emit all of the bits of a frame onto the medium is the transmission
time ; this is proportional to the length of the frame. The propagation time is the
time it takes for a bit to traverse the link between source and destination. For this
section, we assume that all frames that are transmitted are successfully received; no
frames are lost and none arrive with errors. Furthermore, frames arrive in the same
order in which they are sent. However, each transmitted frame suffers an arbitrary
and variable amount of delay before reception.

## Slide 7: Stop-and-Wait Flow Control
Simplest form of flow control
It is often the case that a source will break up a large block of data into smaller blocks and transmit the data in many frames
  The buffer size of the receiver may be limited
  The longer the transmission, the more likely that there will be an error, necessitating retransmission of the entire frame
  On a shared medium it is usually desirable not to permit one station to use the medium for an extended period, thus causing long delays at the other sending station
Source transmits frame
Destination receives frame and replies with acknowledgement (ACK)
Source waits for ACK before sending next frame
Destination can stop flow by not sending ACK
Notes: The simplest form of flow control, known as stop-and-wait flow control, works as
follows. A source entity transmits a frame. After the destination entity receives
the frame, it indicates its willingness to accept another frame by sending back an
acknowledgment to the frame just received. The source must wait until it receives
the acknowledgment before sending the next frame. The destination can thus stop
the flow of data simply by withholding acknowledgment. This procedure works fine
and, indeed, can hardly be improved upon when a message is sent in a few large
frames. However, it is often the case that a source will break up a large block of
data into smaller blocks and transmit the data in many frames. This is done for the
following reasons:
• The buffer size of the receiver may be limited.
• The longer the transmission, the more likely that there will be an error, necessitating
retransmission of the entire frame. With smaller frames, errors are
detected sooner, and a smaller amount of data needs to be retransmitted.
• On a shared medium, such as a LAN, it is usually desirable not to permit one
station to occupy the medium for an extended period, thus causing long delays
at the other sending stations.

## Slide 8
Notes: In situations where the bit length of the link is greater than the frame length,
serious inefficiencies result. This is illustrated in Figure 7.2.
In the figure, the transmission
time is normalized to one, and the propagation delay is expressed as the
variable a .
When a is less than 1, the propagation time is less than the transmission time.
In this case, the frame is sufficiently long that the first bits of the frame have arrived
When a is greater than 1, the propagation time is greater than the transmission
time. In this case, the sender completes transmission of the entire frame before the
leading bits of that frame arrive at the receiver. Put another way, larger values of
a are consistent with higher data rates and/or longer distances between stations.
Chapter 16 discusses a and data link performance.
Both parts of Figure 7.2 (a and b) consist of a sequence of snapshots of the
transmission process over time. In both cases, the first four snapshots show the process
of transmitting a frame containing data, and the last snapshot shows the return
of a small acknowledgment frame. Note that for a >1, the line is always underutilized
and even for a<1, the line is inefficiently utilized. In essence, for very high
data rates, for very long distances between sender and receiver, stop-and-wait flow
control provides inefficient line utilization.

## Slide 9: Sliding Windows Flow Control
Allows multiple numbered frames to be in transit
  Receiver has buffer W long
  Transmitter sends up to W frames without ACK
  ACK includes number of next frame expected
  Sequence number is bounded by size of field (k)
    Frames are numbered modulo 2k
    Giving max window size of up to 2k – 1
  Receiver can ACK frames without permitting further transmission (Receive Not Ready)
  Must send a normal acknowledge to resume
If have full-duplex link, can piggyback ACKs
Notes: The essence of the problem described so far is that only one frame at a time can be in transit. Efficiency can be greatly improved by allowing multiple frames to be in transit at the same time.
Consider two stations, A and B, connected via a full-duplex link. Station B allocates buffer space for W frames. Thus, B can accept W frames, and A is allowed to send W frames without waiting for any acknowledgments. To keep track of which frames have been acknowledged, each is labeled with a a k-bit sequence number. This gives a range of sequence numbers of 0 through 2k – 1, and frames are numbered modulo 2k, with a maximum window size of 2k – 1. The window size need not be the maximum possible size for a given sequence number length k. B acknowledges a frame by sending an acknowledgment that includes the sequence number of the next frame expected. This scheme can also be used to acknowledge multiple frames, and is referred to as sliding-window flow control. Most data link control protocols also allow a station to cut off the flow of frames from the other side by sending a Receive Not Ready (RNR) message, which acknowledges former frames but forbids transfer of future frames. At some subsequent point, the station must send a normal acknowledgment to reopen the window. If two stations exchange data, each needs to maintain two windows, one for transmit and one for receive, and each side needs to send the data and acknowledgments to the other. To provide efficient support for this requirement, a feature known as piggybacking is typically provided. Each data frame includes a field that holds the sequence number of that frame plus a field that holds the sequence number used for acknowledgment.

## Slide 10
W= 7 frames
Notes: Figure 7.3 is a useful way of depicting the sliding-window process. It assumes
the use of a 3-bit sequence number, so that frames are numbered sequentially from
0 through 7, and then the same numbers are reused for subsequent frames. The
shaded rectangle indicates the frames that may be sent; in this figure, the sender
may transmit five frames, beginning with frame 0. Each time a frame is sent, the
shaded window shrinks; each time an acknowledgment is received, the shaded window
grows. Frames between the vertical bar and the shaded window have been sent
but not yet acknowledged. As we shall see, the sender must buffer these frames in
case they need to be retransmitted.
The window size need not be the maximum possible size for a given sequence
number length. For example, using a 3-bit sequence number, a window size of
5 could be configured for the stations using the sliding-window flow control
protocol.

## Slide 11
Notes: An example is shown in Figure 7.4. The example assumes a 3-bit sequence number field and a maximum window size of seven frames. Initially, A and B have windows indicating that A may transmit seven frames, beginning with frame 0 (F0). After transmitting three frames (F0, F1, F2) without acknowledgment, A has shrunk its window to four frames and maintains a copy of the three transmitted frames. The window indicates that A may transmit four frames, beginning with frame number 3. B then transmits an RR (receive ready) 3, which means "I have received all frames up through frame number 2 and am ready to receive frame number 3; in fact, I am prepared to receive seven frames, beginning with frame number 3." With this acknowledgment, A is back up to permission to transmit seven frames, still beginning with frame 3; also A may discard the buffered frames that have now been acknowledged. A proceeds to transmit frames 3, 4, 5, and 6. B returns RR 4, which acknowledges F3, and allows transmission of F4 through the next instance of F2. By the time this RR reaches A, it has already transmitted F4, F5, and F6, and therefore A may only open its window to permit sending four frames beginning with F7.
Sliding-window flow control is potentially much more efficient than stop-and-
wait flow control. The reason is that, with sliding-window flow control, the
transmission link is treated as a pipeline that may be filled with frames in transit.
By contrast, with stop-and-wait flow control, only one frame may be in the pipe at a
time. Chapter 16 quantifies the improvement in efficiency.

## Slide 12: Error Control Techniques
Error detection
Positive acknowledgment
Retransmission after timeout
Negative acknowledgment and retransmission
  Lost frames
  - a frame fails to arrive at the other side
  Damaged frames
    - frame arrives but some of the bits are in error
Notes: Error control refers to mechanisms to detect and correct errors that occur in the
transmission of frames. The model that we will use, which covers the typical case, is
illustrated in Figure 7.1b. As before, data are sent as a sequence of frames; frames
arrive in the same order in which they are sent; and each transmitted frame suffers
an arbitrary and potentially variable amount of delay before reception. In addition,
we admit the possibility of two types of errors:
• Lost frame: A frame fails to arrive at the other side. In the case of a network,
the network may simply fail to deliver a frame. In the case of a direct point-to-
point data link, a noise burst may damage a frame to the extent that the
receiver is not aware that a frame has been transmitted.
• Damaged frame: A recognizable frame does arrive, but some of the bits are in
error (have been altered during transmission).
The most common techniques for error control are based on some or all of the
following ingredients:
• Error detection: The destination detects frames that are in error, using the
techniques described in the preceding chapter, and discards those frames.
• Positive acknowledgment: The destination returns a positive acknowledgment
to successfully received, error-free frames.
• Retransmission after timeout: The source retransmits a frame that has not
been acknowledged after a predetermined amount of time.
• Negative acknowledgment and retransmission: The destination returns a
negative acknowledgment to frames in which an error is detected. The source
retransmits such frames.

## Slide 13: Automatic Repeat Request (ARQ)
Collective name for error control mechanisms
Effect of ARQ is to turn an unreliable data link into a reliable one
Versions of ARQ
Stop-and-wait
Go-back-N
Selective-reject
Notes: Collectively, these mechanisms are all referred to as automatic repeat request
(ARQ) . The effect of ARQ is to turn a potentially unreliable data link into a reliable
one. Three versions of ARQ have been standardized:
• Stop-and-wait ARQ
• Go-back-N ARQ
• Selective-reject ARQ
All of these forms are based on the use of the flow control techniques discussed
in Section 7.1. We examine each in turn.

## Slide 14: Stop and Wait ARQ
Source transmits single frame
Waits for ACK
No other data can be sent until destination’s reply arrives
If frame received is damaged, discard it
Transmitter has timeout
If no ACK within timeout, retransmit
If ACK is damaged, transmitter will not recognize
Transmitter will retransmit
Receiver gets two copies of frame
Use alternate numbering and ACK0 / ACK1
Notes: Stop-and-wait ARQ is based on the stop-and-wait flow control technique outlined previously. The source station transmits a single frame and then must await an acknowledgment (ACK). No other data frames can be sent until the destination station's reply arrives at the source station.
Two sorts of errors could occur. First, the frame that arrives at the destination could be damaged. The receiver detects this by using the error-detection technique referred to earlier and simply discards the frame. To account for this possibility, the source station is equipped with a timer. After a frame is transmitted, the source station waits for an acknowledgment. If no acknowledgment is received by the time that the timer expires, then the same frame is sent again. Note that this method requires that the transmitter maintain a copy of a transmitted frame until an acknowledgment is received for that frame.
The second sort of error is a damaged acknowledgment, which is not recognizable by A, which will therefore time out and resend the same frame. This duplicate frame arrives and is accepted by B. B has therefore accepted two copies of the same frame as if they were separate. To avoid this problem, frames are alternately labeled with 0 or 1, and positive acknowledgments are of the form ACK0 and ACK1. In keeping with the sliding-window convention, an ACK0 acknowledges receipt of a frame numbered 1 and indicates that the receiver is ready for a frame numbered 0.

## Slide 15
Notes: Figure 7.5 gives an example of the use of stop-and-wait ARQ, showing the
transmission of a sequence of frames from source A to destination B.2 The figure
shows the two types of errors just described. The third frame transmitted by A is lost
or damaged and therefore B does not return an ACK. A times out and retransmits
the frame. Later, A transmits a frame labeled 1 but the ACK0 for that frame is lost.
A times out and retransmits the same frame. When B receives two frames in a row
with the same label, it discards the second frame but sends back an ACK0 to each.
The principal advantage of stop-and-wait ARQ is its simplicity. Its principal
disadvantage, as discussed in Section 7.1, is that stop-and-wait is an inefficient mechanism.
The sliding-window flow control technique can be adapted to provide more
efficient line use; in this context, it is sometimes referred to as continuous ARQ .

## Slide 16: Go-Back-N ARQ
Most commonly used error control
Based on sliding-window
Use window size to control number of outstanding frames
While no errors occur, the destination will acknowledge incoming frames as usual
  RR=receive ready, or piggybacked acknowledgment
If the destination station detects an error in a frame, it may send a negative acknowledgment
  REJ=reject
  Destination will discard that frame and all future frames until the frame in error is received correctly
  Transmitter must go back and retransmit that frame and all subsequent frames
Notes: The form of error control based on sliding-window flow control that is most commonly
used is called go-back-N ARQ. In this method, a station may send a series
of frames sequentially numbered modulo some maximum value. The number of
unacknowledged frames outstanding is determined by window size, using the
sliding-window flow control technique. While no errors occur, the destination
will acknowledge incoming frames as usual (RR = receive ready, or piggybacked
acknowledgment). If the destination station detects an error in a frame, it may send
a negative acknowledgment (REJ = reject) for that frame, as explained in the following
rules. The destination station will discard that frame and all future incoming
frames until the frame in error is correctly received. Thus, the source station, when
it receives a REJ, must retransmit the frame in error plus all succeeding frames that
were transmitted in the interim.

## Slide 17: Selective-Reject (ARQ)
Also called selective retransmission
Only rejected frames are retransmitted
Subsequent frames are accepted by the receiver and buffered
Minimizes retransmission
Receiver must maintain large enough buffer
More complex logic in transmitter
  Less widely used
Useful for satellite links with long propagation delays
Notes: With selective-reject ARQ, the only frames retransmitted are those that receive a negative acknowledgment, in this case called SREJ, or those that time out. Selective reject would appear to be more efficient than go-back-N, because it minimizes the amount of retransmission. On the other hand, the receiver must maintain a buffer large enough to save post-SREJ frames until the frame in error is retransmitted and must contain logic for reinserting that frame in the proper sequence. The transmitter, too, requires more complex logic to be able to send a frame out of sequence. Because of such complications, select-reject ARQ is much less widely used than go-back-N ARQ. Selective reject is a useful choice for a satellite link because of the long propagation delay involved.

## Slide 18: Selective-Reject (ARQ)
Window Size Limitation
  For a k-bit sequence number, the maximum window size is limited to 2k-1.
0 1 2 3 4 5 6 7 0 1 2 3 4 5 ...
S
R
RR7 lost
retx
Ö
0 1 2 3 4 5 6 7 0 1 2 ...
S
R
RR4 lost
retx
x
k=3, W=7
k=3, W=4
Notes: With selective-reject ARQ, the only frames retransmitted are those that receive a negative acknowledgment, in this case called SREJ, or those that time out. Selective reject would appear to be more efficient than go-back-N, because it minimizes the amount of retransmission. On the other hand, the receiver must maintain a buffer large enough to save post-SREJ frames until the frame in error is retransmitted and must contain logic for reinserting that frame in the proper sequence. The transmitter, too, requires more complex logic to be able to send a frame out of sequence. Because of such complications, select-reject ARQ is much less widely used than go-back-N ARQ. Selective reject is a useful choice for a satellite link because of the long propagation delay involved.

## Slide 19
Notes: Figure 7.6a is an example of the frame flow for go-back-N ARQ.
Because of the propagation delay on the line, by the time that an acknowledgment
(positive or negative) arrives back at the sending station, it has already
sent at least one additional frame beyond the one being acknowledged. In this
example, frame 4 is damaged. Frames 5 and 6 are received out of order and are
discarded by B. When frame 5 arrives, B immediately sends a REJ 4. When the
REJ to frame 4 is received, not only frame 4 but frames 5 and 6 must be retransmitted.
Note that the transmitter must keep a copy of all unacknowledged
frames. Figure 7.6a also shows an example of retransmission after timeout. No
acknowledgment is received for frame 5 within the timeout period, so A issues
an RR to determine the status of B.
Figure 7.6b illustrates Selective-Reject ARQ. When frame 5 is received
out of order, B sends a SREJ 4, indicating that frame 4 has not been received.
However, B continues to accept incoming frames and buffers them until a valid
frame 4 is received. At that point, B can place the frames in the proper order for
delivery to higher-layer software.

## Slide 20: High Level Data Link Control (HDLC)
Most important data link control protocol
Specified as ISO 3009, ISO 4335
Basis for other data link control protocols
Station types
Primary - controls operation of link
Secondary - under control of primary station
Combined - issues commands and responses
Link configurations
Unbalanced - 1 primary, multiple secondary
Balanced - 2 combined stations
Notes: The most important data link control protocol is HDLC (ISO 3009, ISO 4335). Not only is HDLC widely used, but it is the basis for many other important data link control protocols, which use the same or similar formats and the same mechanisms as employed in HDLC.
To satisfy a variety of applications, HDLC defines: three station types:
• Primary station: Responsible for controlling the operation of the link. Frames issued by the primary are called commands.
• Secondary station: Operates under the control of the primary station. Frames issued by a secondary are called responses. The primary maintains a separate logical link with each secondary station on the line.
• Combined station: Combines the features of primary and secondary. A combined station may issue both commands and responses.
It also defines two link configurations:
• Unbalanced configuration: Consists of one primary and one or more secondary stations and supports both full-duplex and half-duplex transmission.
• Balanced configuration: Consists of two combined stations and supports both full-duplex and half-duplex transmission.

## Slide 21: HDLC Data Transfer Modes
Normal Response Mode (NRM)
Used with an unbalanced configuration
Primary initiates transfer
Asynchronous Balanced Mode (ABM)
Used with a balanced configuration
Either station initiates transmission
Has no polling overhead
Most widely used
Asynchronous Response Mode (ARM)
Used with unbalanced configuration
Secondary may transmit without permission from primary
Rarely used
Notes: HDLC defines three data transfer modes:
•Normal response mode (NRM): Used with an unbalanced configuration. The primary may initiate data transfer to a secondary, but a secondary may only transmit data in response to a command from the primary. NRM is used on multi-drop lines, in which a number of terminals are connected to a host computer.
•Asynchronous balanced mode (ABM): Used with a balanced configuration. Either combined station may initiate transmission without receiving permission from the other combined station. ABM is the most widely used of the three modes; it makes more efficient use of a full-duplex point-to-point link because there is no polling overhead.
•Asynchronous response mode (ARM): Used with an unbalanced configuration. The secondary may initiate transmission without explicit permission of the primary. The primary still retains responsibility for the line, including initialization, error recovery, and logical disconnection. ARM is rarely used; it is applicable to some special situations in which a secondary may need to initiate transmission.

## Slide 22
Notes: HDLC uses synchronous transmission. All transmissions are in the form of frames,
and a single frame format suffices for all types of data and control exchanges.
Figure 7.7 depicts the structure of the HDLC frame. The flag, address, and
control fields that precede the information field are known as a header . The frame
check sequence and flag fields following the data field are referred to as a trailer .

## Slide 23
Notes: Flag fields delimit the frame at both ends with the unique pattern
01111110. A single flag may be used as the closing flag for one frame and the opening
flag for the next. On both sides of the user-network interface, receivers are continuously
hunting for the flag sequence to synchronize on the start of a frame. While
receiving a frame, a station continues to hunt for that sequence to determine the
end of the frame. Because the protocol allows the presence of arbitrary bit patterns
(i.e., there are no restrictions on the content of the various fields imposed by the
link protocol), there is no assurance that the pattern 01111110 will not appear somewhere
inside the frame, thus destroying synchronization. To avoid this problem, a
procedure known as bit stuffing is used. For all bits between the starting and ending
flags, the transmitter inserts an extra 0 bit after each occurrence of five 1s in the
frame. After detecting a starting flag, the receiver monitors the bit stream. When a
pattern of five 1s appears, the sixth bit is examined. If this bit is 0, it is deleted. If the
sixth bit is a 1 and the seventh bit is a 0, the combination is accepted as a flag. If the
sixth and seventh bits are both 1, the sender is indicating an abort condition.
With the use of bit stuffing, arbitrary bit patterns can be inserted into the data
field of the frame. This property is known as data transparency .
Figure 7.8 shows an example of bit stuffing. Note that in the first two cases, the
extra 0 is not strictly necessary for avoiding a flag pattern but is necessary for the
operation of the algorithm.

## Slide 24: Address Field
Identifies secondary station that transmitted or will receive frame
Usually 8 bits long
May be extended to multiples of 7 bits
  Leftmost bit indicates if is the last octet (1) or not (0)
Address 11111111 allows a primary to broadcast a frame for reception by all secondaries
This field is not needed for point-to-point links
Notes: The address field identifies the secondary station that transmitted or is to receive the frame. This field is not needed for point-to-point links but is always included for the sake of uniformity. The address field is usually 8 bits long but, by prior agreement, an extended format may be used in which the actual address length is a multiple of 7 bits. The leftmost bit of each octet is 1 or 0 according as it is or is not the last octet of the address field. The remaining 7 bits of each octet form part of the address. The single-octet address of 11111111 is interpreted as the all-stations address in both basic and extended formats. It is used to allow the primary to broadcast a frame for reception by all secondaries.

## Slide 25
HDLC defines three types of frames, each with a different control field format
  Information frames (I-frames)
    Carry the data to be transmitted for the user
    Flow and error control data, using the ARQ mechanism, are piggybacked on an information frame
  Supervisory frames (S-frames)
    Provide the ARQ mechanism when piggybacking is not used
  Unnumbered frames (U-frames)
    Provide supplemental link control functions
Notes: HDLC defines three types of frames, each with a different control
field format. Information frames (I-frames) carry the data to be transmitted for
the user (the logic above HDLC that is using HDLC). Additionally, flow and
error control data, using the ARQ mechanism, are piggybacked on an information
frame. Supervisory frames (S-frames) provide the ARQ mechanism when piggybacking
is not used. Unnumbered frames (U-frames) provide supplemental link
control functions. The first one or two bits of the control field serves to identify the
frame type. The remaining bit positions are organized into subfields as indicated in
Figures 7.7c and d. Their use is explained in the discussion of HDLC operation later
in this chapter.

## Slide 26: Control Field
Use of poll/final (P/F) bit depends on context
In command frames P bit is set to 1 to solicit (poll) a response from the peer HDLC entity
In response frames F bit is set to 1 to indicate the response frame transmitted as a result of a soliciting command
The basic control field for S- and I-frames uses 3 bit sequence numbers
  An extended control field can be used that employs 7-bit sequence numbers
  U-frames always contain an 8-bit control field
Notes: All of the control field formats contain the poll/final (P/F) bit. Its use depends
on context. Typically, in command frames, it is referred to as the P bit and is set to
1 to solicit (poll) a response frame from the peer HDLC entity. In response frames,
it is referred to as the F bit and is set to 1 to indicate the response frame transmitted
as a result of a soliciting command.
Note that the basic control field for S- and I-frames uses 3-bit sequence
numbers. With the appropriate set-mode command, an extended control field can
be used for S- and I-frames that employs 7-bit sequence numbers. U-frames always
contain an 8-bit control field.

## Slide 27: Information and Frame Check Sequence (FCS) Fields
Information Field
Present only in I-frames and some U-frames
Must contain an integral number of octets
Variable length
Frame Check Sequence Field (FCS)
Error detecting code calculated from the remaining bits of the frame, exclusive of flags
The normal code is the 16 bit CRC-CCITT
Optional 32-bit FCS, using CRC-32, may be employed if the frame length or the line reliability dictates this choice
Notes: The information field is present only in I-frames and some U-frames. The field can contain any sequence of bits but must consist of an integral number of octets. The length of the information field is variable up to some system-defined maximum.
The frame check sequence (FCS) is an error-detecting code calculated from the remaining bits of the frame, exclusive of flags. The normal code is the 16-bit CRC-CCITT defined in Section 6.3. An optional 32-bit FCS, using CRC-32, may be employed if the frame length or the line reliability dictates this choice.

## Slide 28
Table 7.1
HDLC Commands
and Responses
(Table can be found on page 254 in the textbook)
Notes: HDLC operation consists of the exchange of I-frames, S-frames, and U-frames
between two stations. The various commands and responses defined for these frame
types are listed in Table 7.1.

## Slide 29: HDLC Operation
Initialization
Signals the other side that initialization is requested
Data Transfer
The N(S) and N(R) fields of the I-frame are sequence numbers that support flow control and error control
Disconnect
Either module can initiate
Specifies which of the three modes (NRM, ABM, ARM) is requested
Specifies whether 3- or 7-bit sequence numbers are to be used
An HDLC module will number them sequentially
Receive Ready (RR) is used when there is no reverse user data traffic
Sends disconnect (DISC) frame
Remote entity replies with a UA
Any outstanding unacknowledged
I-frames may be lost
Either on its own initiative if there is some sort of fault, or at the request of its higher-layer user
Recovery is the responsibility of higher layers
Consists of the exchange of I-frames, S-frames and U-frames
Involves three phases:
Notes: The operation of HDLC involves three phases. First, one side or another
initializes the data link so that frames may be exchanged in an orderly fashion.
During this phase, the options that are to be used are agreed upon. After initialization,
the two sides exchange user data and the control information to exercise
flow and error control. Finally, one of the two sides signals the termination of the
operation.
Either side may request initialization by issuing one of the six set-mode
commands. This command serves three purposes:
1. It signals the other side that initialization is requested.
2. It specifies which of the three modes (NRM, ABM, ARM) is requested.
3. It specifies whether 3- or 7-bit sequence numbers are to be used.
If the other side accepts this request, then the HDLC module on that end
transmits an unnumbered acknowledged (UA) frame back to the initiating side. If
the request is rejected, then a disconnected mode (DM) frame is sent.
When the initialization has been requested and accepted, then
a logical connection is established. Both sides may begin to send user data in
I-frames, starting with sequence number 0. The N(S) and N(R) fields of the I-frame
are sequence numbers that support flow control and error control. An HDLC
module sending a sequence of I-frames will number them sequentially, modulo 8
or 128, depending on whether 3- or 7-bit sequence numbers are used, and place
the sequence number in N(S). N(R) is the acknowledgment for I-frames received;
it enables the HDLC module to indicate which number I-frame it expects to
receive next.
S-frames are also used for flow control and error control. The receive ready
(RR) frame acknowledges the last I-frame received by indicating the next I-frame
expected. The RR is used when there is no reverse user data traffic (I-frames) to
carry an acknowledgment. Receive not ready (RNR) acknowledges an I-frame, as
with RR, but also asks the peer entity to suspend transmission of I-frames. When the
entity that issued RNR is again ready, it sends an RR. REJ initiates the go-
back-N ARQ. It indicates that the last I-frame received has been rejected and that retransmission
of all I-frames beginning with number N(R) is required. Selective reject
(SREJ) is used to request retransmission of just a single frame.
Either HDLC module can initiate a disconnect, either on its own initiative
if there is some sort of fault, or at the request of its higher-layer user. HDLC
issues a disconnect by sending a disconnect (DISC) frame. The remote entity must
accept the disconnect by replying with a UA and informing its layer 3 user that the
connection has been terminated. Any outstanding unacknowledged I-frames may
be lost, and their recovery is the responsibility of higher layers.

## Slide 30
Notes: To better understand HDLC operation, several examples
are presented in Figure 7.9. In the example diagrams, each arrow includes a
legend that specifies the frame name, the setting of the P/F bit, and, where appropriate,
the values of N(R) and N(S). The setting of the P or F bit is 1 if the designation
is present and 0 if absent.
Figure 7.9a shows the frames involved in link setup and disconnect. The HDLC
protocol entity for one side issues an SABM command to the other side and starts
a timer. The other side, upon receiving the SABM, returns a UA response and sets
local variables and counters to their initial values. The initiating entity receives the
UA response, sets its variables and counters, and stops the timer. The logical connection
is now active, and both sides may begin transmitting frames. Should the
timer expire without a response to an SABM, the originator will repeat the SABM,
as illustrated. This would be repeated until a UA or DM is received or until, after
a given number of tries, the entity attempting initiation gives up and reports failure
to a management entity. In such a case, higher-layer intervention is necessary. The
same figure (Figure 7.9a) shows the disconnect procedure. One side issues a DISC
command, and the other responds with a UA response.
Figure 7.9b illustrates the full-duplex exchange of I-frames. When an entity
sends a number of I-frames in a row with no incoming data, then the receive
sequence number is simply repeated (e.g., I,1,1; I,2,1 in the A-to-B direction). When
an entity receives a number of I-frames in a row with no outgoing frames, then the
receive sequence number in the next outgoing frame must reflect the cumulative
activity (e.g., I,1,3 in the B-to-A direction). Note that, in addition to I-frames, data
exchange may involve supervisory frames.
Figure 7.9c shows an operation involving a busy condition. Such a condition
may arise because an HDLC entity is not able to process I-frames as fast as they
are arriving, or the intended user is not able to accept data as fast as they arrive
in I-frames. In either case, the entity’s receive buffer fills up and it must halt the
incoming flow of I-frames, using an RNR command. In this example, A issues an
RNR, which requires B to halt transmission of I-frames. The station receiving the
RNR will usually poll the busy station at some periodic interval by sending an RR
with the P bit set. This requires the other side to respond with either an RR or an
RNR. When the busy condition has cleared, A returns an RR, and I-frame transmission
from B can resume.
An example of error recovery using the REJ command is shown in Figure 7.9d.
In this example, A transmits I-frames numbered 3, 4, and 5. Number 4 suffers an
error and is lost. When B receives I-frame number 5, it discards this frame because it
is out of order and sends an REJ with an N(R) of 4. This causes A to initiate retransmission
of I-frames previously sent, beginning with frame 4. A may continue to send
additional frames after the retransmitted frames.
An example of error recovery using a timeout is shown in Figure 7.9e. In
this example, A transmits I-frame number 3 as the last in a sequence of I-frames.
The frame suffers an error. B detects the error and discards it. However, B cannot
send an REJ, because there is no way to know if this was an I-frame. If an error is
detected in a frame, all of the bits of that frame are suspect, and the receiver has no
way to act upon it. A, however, would have started a timer as the frame was transmitted.
This timer has a duration long enough to span the expected response time.
When the timer expires, A initiates recovery action. This is usually done by polling
the other side with an RR command with the P bit set to determine the status of
the other side. Because the poll demands a response, the entity will receive a frame
containing an N(R) field and be able to proceed. In this case, the response indicates
that frame 3 was lost, which A retransmits.
These examples are not exhaustive. However, they should give the reader a
good feel for the behavior of HDLC.

## Slide 31: Summary
Flow control
  Stop-and-wait flow control
  Sliding-window flow control
Error control
  Stop-and-wait ARQ
  Go-back-N ARQ
  Selective-reject ARQ
High-level data link control (HDLC)
  Basic characteristics
  Frame structure
  Operation
Notes: Chapter 7summary.