## Slide 1: Data and Computer Communications
Tenth Edition
by William Stallings
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 8 “Multiplexing”.

## Slide 2: Multiplexing
Chapter 8
Notes: In Chapter 7, we described efficient techniques for utilizing a data link under
heavy load. Specifically, with two devices connected by a point-to-point link,
it is generally desirable to have multiple frames outstanding so that the data
link does not become a bottleneck between the stations. Now consider the
opposite problem. Typically, two communicating stations will not utilize the
full capacity of a data link. For efficiency, it should be possible to share that
capacity. A generic term for such sharing is multiplexing.
A common application of multiplexing is in long-haul communications.
Trunks on long-haul networks are high-capacity fiber, coaxial, or microwave
links. These links can carry large numbers of voice and data transmissions
simultaneously using multiplexing.

## Slide 3
“It was impossible to get a conversation going, everybody was talking too much.”
- Yogi Berra
Notes: The widespread use of multiplexing in data communications can be
explained by the following:
• The higher the data rate, the more cost-effective the transmission facility.
That is, for a given application and over a given distance, the cost
per kbps declines with an increase in the data rate of the transmission
facility. Similarly, the cost of transmission and receiving equipment, per
kbps, declines with increasing data rate.
• Most individual data communicating devices require relatively modest
data rate support. For example, for many terminal and personal computer
applications that do not involve Web access or intensive graphics,
a data rate of between 9600 bps and 64 kbps is generally adequate.
The preceding statements were phrased in terms of data communicating
devices. Similar statements apply to voice communications. That is, the
greater the capacity of a transmission facility, in terms of voice channels, the
less the cost per individual voice channel, and the capacity required for a single
voice channel is modest.
This chapter presents two types of multiplexing techniques. The first,
frequency-division multiplexing (FDM), is the most heavily used and is
familiar to anyone who has ever used a radio or television set. The second
is a particular case of time-division multiplexing (TDM) known as synchronous
TDM. This is commonly used for multiplexing digitized voice streams
and data streams. We then look at two schemes that combine both types of
multiplexing, cable modems and digital subscriber lines.

## Slide 4
Notes: Figure 8.1 depicts the multiplexing function in its simplest form. There
are n inputs to a multiplexer. The multiplexer is connected by a single data link
to a demultiplexer. The link is able to carry n separate channels of data. The
multiplexer over a higher-capacity data link. The demultiplexer accepts the multiplexed
data stream, separates (demultiplexes) the data according to channel, and
delivers data to the appropriate output lines.combines (multiplexes) data from the n input lines and transmits
over a higher-capacity data link. The demultiplexer accepts the multiplexed
data stream, separates (demultiplexes) the data according to channel, and
delivers data to the appropriate output lines.

## Slide 5
Notes: FDM is possible when the useful bandwidth of the transmission medium exceeds the
required bandwidth of signals to be transmitted. A number of signals can be carried
simultaneously if each signal is modulated onto a different carrier frequency and
the carrier frequencies are sufficiently separated that the bandwidths of the signals
do not significantly overlap. A general case of FDM is shown in Figure 8.2a. Six signal
sources are fed into a multiplexer, which modulates each signal onto a different
frequency (f1 , . . . , f6 ). Each modulated signal requires a certain bandwidth centered
on its carrier frequency, referred to as a channel . To prevent interference, the channels
are separated by guard bands, which are unused portions of the spectrum.
The composite signal transmitted across the medium is analog. Note, however,
that the input signals may be either digital or analog. In the case of digital
input, the input signals must be passed through modems to be converted to analog.
In either case, each input analog signal must then be modulated to move it to the
appropriate frequency band.

## Slide 6
Notes: A generic depiction of an FDM system is shown in Figure 8.3. A number of analog or digital signals [mi(t), i = 1, n] are to be multiplexed onto the same transmission medium. Modulation equipment is needed to move each signal to the required frequency band, and multiplexing equipment is needed to combine the modulated signals. Each signal mi(t) is modulated onto a carrier fi; because multiple carriers are to be used, each is referred to as a subcarrier. Any type of modulation may be used. The resulting analog, modulated signals are then summed to produce a composite baseband signal mb(t). Figure 8.3b shows the result. The spectrum of signal mi(t) is shifted to be centered on fi. For this scheme to work, fi must be chosen so that the bandwidths of the various signals do not significantly overlap. Otherwise, it will be impossible to recover the original signals.
The composite signal may then be shifted as a whole to another carrier frequency by an additional modulation step.
The FDM signal s(t) has a total bandwidth B = Sum Bi . This analog signal may be transmitted over a suitable medium. At the receiving end, the FDM signal is demodulated to retrieve mb(t), which is then passed through n bandpass filters, each filter centered on fi and having a bandwidth Bi, for 1 ≤ i ≤ n. In this way, the signal is again split into its component parts. Each component is then demodulated to recover the original signal.

## Slide 7
Notes: Let us consider a simple example of transmitting three voice
signals simultaneously over a medium. As was mentioned, the bandwidth of a
voice signal is generally taken to be 4 kHz, with an effective spectrum of 300 to
3400 Hz (Figure 8.4a). If such a signal is used to amplitude-modulate a 64-kHz
carrier, the spectrum of Figure 8.4b results. The modulated signal has a bandwidth
of 8 kHz, extending from 60 to 68 kHz. To make efficient use of bandwidth,
we elect to transmit only the lower sideband. If three voice signals are
used to modulate carriers at 64 kHz, 68 kHz, and 72 kHz, and only the lower
sideband of each is taken, the spectrum of Figure 8.4c results.
Figure 8.4 points out two problems that an FDM system must cope with. The
first is crosstalk, which may occur if the spectra of adjacent component signals
overlap significantly. In the case of voice signals, with an effective bandwidth of
only 3100 Hz (300 to 3400), a 4-kHz bandwidth is adequate. The spectra of signals
produced by modems for voiceband transmission also fit well in this bandwidth.
Another potential problem is intermodulation noise, which was discussed
in Chapter 3. On a long link, the nonlinear effects of amplifiers on a signal in one
channel could produce frequency components in other channels.

## Slide 8: Analog Carrier Systems
Long-distance links use an FDM hierarchy
AT&T (USA) and ITU-T (International) variants
Original signal can be modulated many times
Group
12 voice channels (4kHz each) = 48kHz
Range 60kHz to 108kHz
Supergroup
FDM of 5 group signals supports 60 channels
Carriers between 420kHz and 612 kHz
Mastergroup
FDM of 10 supergroups supports 600 channels
Notes: The long-distance carrier system provided in the United States and throughout the world is designed to transmit voiceband signals over high-capacity transmission links, such as coaxial cable and microwave systems. The earliest, and still a very common, technique for utilizing high-capacity links is FDM. In the United States, AT&T has designated a hierarchy of FDM schemes to accommodate transmission systems of various capacities. A similar, but unfortunately not identical, system has been adopted internationally under the auspices of ITU-T.

## Slide 9: Table 8.1 North American and International FDM Carrier Standards
Notes: At the first level of the AT&T hierarchy, 12 voice channels are combined to produce a group signal with a bandwidth of 12  4 kHz = 48 kHz, in the range 60 to 108 kHz. The next basic building block is the 60-channel supergroup, which is formed by frequency division multiplexing five group signals. The subcarriers have frequencies from 420 to 612 kHz in increments of 48 kHz. The resulting signal occupies 312 to 552 kHz. The next level of the hierarchy is the mastergroup, which combines 10 supergroup inputs. The mastergroup has a bandwidth of 2.52 MHz and can support 600 voice frequency (VF) channels. Higher-level multiplexing is defined above the mastergroup, as shown in Table 8.1.
Note that the original voice or data signal may be modulated many times. Each stage can distort the original data; this is so, for example, if the modulator/multiplexer contains nonlinearities or introduces noise.

## Slide 10: Wavelength Division Multiplexing (WDM)
Multiple beams of light at different frequencies
Carried over optical fiber links
Commercial systems with 160 channels of 10 Gbps
Lab demo of 256 channels 39.8 Gbps
Architecture similar to other FDM systems
Multiplexer consolidates laser sources (1550nm) for transmission over single fiber
Optical amplifiers amplify all wavelengths
Demultiplexer separates channels at destination
Dense Wavelength Division Multiplexing (DWDM)
Use of more channels more closely spaced
Notes: The true potential of optical fiber is fully exploited when multiple beams of light at different frequencies are transmitted on the same fiber. This is a form of frequency division multiplexing (FDM) but is commonly called wavelength division multiplexing (WDM). With WDM, the light streaming through the fiber consists of many colors, or wavelengths, each carrying a separate channel of data. Commercial systems with 160 channels of 10 Gbps are now available. In a lab environment, Alcatel has carried 256 channels at 39.8 Gbps each, a total of 10.1 Tbps, over a 100-km span.
The term dense wavelength division multiplexing (DWDM) is often seen in the literature. There is no official or standard definition of this term. The term connotes the use of more channels, more closely spaced, than ordinary WDM. In general, a channel spacing of 200 GHz or less could be considered dense.

## Slide 11
Notes: A typical WDM system has the same general architecture as other FDM systems. A number of sources generate a laser beam at different wavelengths. Most WDM systems operate in the 1550-nm range. These are sent to a multiplexer, which consolidates the sources for transmission over a single fiber line. Optical amplifiers, typically spaced tens of kilometers apart, amplify all of the wavelengths simultaneously. Finally, the composite signal arrives at a demultiplexer, where the component channels are separated and sent to receivers at the destination point. (Figure 8.5)

## Slide 12: Table 8.2 ITU WDM Channel Spacing (G.692)
Notes: Most WDM systems operate in the 1550-nm range. In early systems, 200 GHz
was allocated to each channel, but today most WDM systems use 50-GHz spacing.
The channel spacing defined in ITU-T G.692, which accommodates 80 50-GHz
channels, is summarized in Table 8.2.

## Slide 13
Notes: A generic depiction of a synchronous TDM system is provided in Figure 8.6. A number of signals [mi(t), i = 1, n] are to be multiplexed onto the same transmission medium. The signals carry digital data and are generally digital signals. The incoming data from each source are briefly buffered. Each buffer is typically one bit or one character in length. The buffers are scanned sequentially to form a composite digital data stream mc(t). The scan operation is sufficiently rapid so that each buffer is emptied before more data can arrive. Thus, the data rate of mc(t) must at least equal the sum of the data rates of the mi(t). The digital signal mc(t) may be transmitted directly, or passed through a modem so that an analog signal is transmitted. In either case, transmission is typically synchronous.
The transmitted data may have a format something like Figure 8.6b. The data are organized into frames. Each frame contains a cycle of time slots. In each frame, one or more slots are dedicated to each data source. The sequence of slots dedicated to one source, from frame to frame, is called a channel. The slot length equals the transmitter buffer length, typically a bit or a byte (character).
The byte-interleaving technique is used with asynchronous and synchronous
sources. Each time slot contains one character of data. Typically, the start and
stop bits of each character are eliminated before transmission and reinserted by
the receiver, thus improving efficiency. The bit-interleaving technique is used with
synchronous sources and may also be used with asynchronous sources. Each time
slot contains just one bit.
At the receiver, the interleaved data are demultiplexed and routed to the appropriate destination buffer. For each input source mi(t), there is an identical output destination that will receive the output data at the same rate at which it was generated.
Synchronous TDM is called synchronous not because synchronous transmission
is used, but because the time slots are preassigned to sources and fixed. The
time slots for each source are transmitted whether or not the source has data to
send. This is, of course, also the case with FDM. In both cases, capacity is wasted
to achieve simplicity of implementation. Even when fixed assignment is used, however,
it is possible for a synchronous TDM device to handle sources of different data
rates. For example, the slowest input device could be assigned one slot per cycle,
while faster devices are assigned multiple slots per cycle.
An alternative to synchronous TDM is statistical TDM . The statistical multiplexer
dynamically allocates time slots on demand. As with a synchronous TDM,
the statistical multiplexer has a number of I/O lines on one side and a higher speed
multiplexed line on the other. Each I/O line has a buffer associated with it. In the
case of the statistical multiplexer, there are n I/O lines, but only k , where k<n ,
time slots available on the TDM frame. For input, the function of the multiplexer
is to scan the input buffers, collecting data until a frame is filled, and then send the
frame. On output, the multiplexer receives a frame and distributes the slots of data
to the appropriate output buffers. Packet switching is, in effect, a form of statistical
TDM. For a further discussion of statistical TDM, see Appendix I.

## Slide 14: TDM Link Control
No headers and trailers
Data link control protocols not needed
Flow control
  Data rate of multiplexed line is fixed
  If one channel receiver can not receive data, the others must carry on
  Corresponding source must be quenched
  Leaving empty slots
Error control
  Errors detected and handled on individual channel
Notes: The reader will note that the transmitted data stream depicted in Figure 8.6b does
not contain the headers and trailers that we have come to associate with synchronous
transmission. The reason is that the control mechanisms provided by a data
link protocol are not needed. It is instructive to ponder this point, and we do so by
considering two key data link control mechanisms: flow control and error control. It
should be clear that, as far as the multiplexer and demultiplexer (Figure 8.1) are concerned,
flow control is not needed. The data rate on the multiplexed line is fixed, and
the multiplexer and demultiplexer are designed to operate at that rate. But suppose
that one of the individual output lines attaches to a device that is temporarily unable
to accept data. Should the transmission of TDM frames cease? Clearly not, because
the remaining output lines are expecting to receive data at predetermined times.
The solution is for the saturated output device to cause the flow of data from the corresponding
input device to cease. Thus, for a while, the channel in question will carry
empty slots, but the frames as a whole will maintain the same transmission rate.
The reasoning for error control is the same. It would not do to request
retransmission of an entire TDM frame because an error occurs on one channel.
The devices using the other channels do not want a retransmission nor would they
know that a retransmission has been requested by some other device on another
channel. Again, the solution is to apply error control on a per-channel basis.
Flow control and error control can be provided on a per-channel basis by using
a data link control protocol such as HDLC on a per-channel basis.

## Slide 15
Notes: Figure 8.7 provides a simplified example. We assume two data
sources, each using HDLC. One is transmitting a stream of HDLC frames containing
three octets of data each, and the other is transmitting HDLC frames
containing four octets of data. For clarity, we assume that character-interleaved
multiplexing is used, although bit interleaving is more typical. Notice what is
happening. The octets of the HDLC frames from the two sources are shuffled
together for transmission over the multiplexed line. The reader may initially
be uncomfortable with this diagram, because the HDLC frames have lost their
integrity in some sense. For example, each frame check sequence (FCS) on the
line applies to a disjointed set of bits. Even the FCS is not in one piece. However,
the pieces are reassembled correctly before they are seen by the device on the
other end of the HDLC protocol. In this sense, the multiplexing/demultiplexing
operation is transparent to the attached stations; to each communicating pair of
stations, it appears that they have a dedicated link.
One refinement is needed in Figure 8.7. Both ends of the line need to be a
combination multiplexer/demultiplexer with a full-duplex line in between. Then
each channel consists of two sets of slots, one traveling in each direction. The individual
devices attached at each end can, in pairs, use HDLC to control their own
channel. The multiplexer/demultiplexers need not be concerned with these matters.

## Slide 16: Framing
No flag or SYNC characters bracketing TDM frames
Must still provide synchronizing mechanism between source and destination clocks
Added digit framing is most common
One control bit added to each TDM frame
Identifiable bit pattern used as control channel
Alternating pattern 101010…unlikely to be sustained on a data channel
Receivers compare incoming bits of frame position to the expected pattern
Notes: We have seen that a link control protocol is not needed to manage the
overall TDM link. There is, however, a basic requirement for framing. Because we
are not providing flag or SYNC characters to bracket TDM frames, some means is
needed to assure frame synchronization. It is clearly important to maintain framing
synchronization because, if the source and destination are out of step, data on all
channels are lost.
Perhaps the most common mechanism for framing is known as added-digit
framing. In this scheme, typically, one control bit is added to each TDM frame. An
identifiable pattern of bits, from frame to frame, is used as a “control channel.”
A typical example is the alternating bit pattern, 101010. . . . This is a pattern unlikely
to be sustained on a data channel. Thus, to synchronize, a receiver compares the
incoming bits of one frame position to the expected pattern. If the pattern does
not match, successive bit positions are searched until the pattern persists over multiple
frames. Once framing synchronization is established, the receiver continues to
monitor the framing bit channel. If the pattern breaks down, the receiver must again enter a framing search mode.

## Slide 17
Pulse Stuffing is a common solution
Have outgoing data rate (excluding framing bits) higher than sum of incoming rates
Stuff extra dummy bits or pulses into each incoming signal until it matches local clock
Stuffed pulses inserted at fixed locations in frame and removed at demultiplexer
Problem of synchronizing various data sources
Variation among clocks could cause loss of synchronization
Issue of data rates from different sources not related by a simple rational number
Notes: Perhaps the most difficult problem in the design of a synchronous time division multiplexer is that of synchronizing the various data sources. If each source has a separate clock, any variation among clocks could cause loss of synchronization. Also, in some cases, the data rates of the input data streams are not related by a simple rational number. For both these problems, a technique known as pulse stuffing is an effective remedy. With pulse stuffing, the outgoing data rate of the multiplexer, excluding framing bits, is higher than the sum of the maximum instantaneous incoming rates. The extra capacity is used by stuffing extra dummy bits or pulses into each incoming signal until its rate is raised to that of a locally generated clock signal. The stuffed pulses are inserted at fixed locations in the multiplexer frame format so that they may be identified and removed at the demultiplexer.

## Slide 18
Notes: An example, from [COUC13], illustrates the use of synchronous
TDM to multiplex digital and analog sources (Figure 8.8). Consider that
there are 11 sources to be multiplexed on a single link:
Source 1: Analog, 2-kHz bandwidth
Source 2: Analog, 4-kHz bandwidth
Source 3: Analog, 2-kHz bandwidth
Sources 4–11: Digital, 7200 bps synchronous
As a first step, the analog sources are converted to digital using pulse code
modulation (PCM). Recall from Chapter 5 that PCM is based on the sampling
theorem, which dictates that a signal be sampled at a rate equal to twice its bandwidth.
Thus, the required sampling rate is 4000 samples per second for sources
1 and 3, and 8000 samples per second for source 2. These samples, which are
analog (PAM), must then be quantized or digitized. Let us assume that 4 bits are
used for each analog sample. For convenience, these three sources will be multiplexed
first, as a unit. At a scan rate of 4 kHz, one PAM sample each is taken
from sources 1 and 3, and two PAM samples are taken from source 2 per scan.
These four samples are interleaved and converted to 4-bit PCM samples. Thus,
a total of 16 bits is generated at a rate of 4000 times per second, for a composite
bit rate of 64 kbps.
For the digital sources, pulse stuffing is used to raise each source to a rate
of 8 kbps, for an aggregate data rate of 64 kbps. A frame can consist of multiple
cycles of 32 bits, each containing 16 PCM bits and two bits from each of the eight
digital sources.

## Slide 19: Table 8.3 North American and International TDM Carrier Standards
Notes: The long-distance carrier system provided in the United States and throughout
the world was designed to transmit voice signals over high-capacity transmission
links, such as optical fiber, coaxial cable, and microwave. Part of the evolution of
these telecommunications networks to digital technology has been the adoption of
synchronous TDM transmission structures. In the United States, AT&T developed
a hierarchy of TDM structures of various capacities; this structure is used in Canada
and Japan as well as the United States. A similar, but unfortunately not identical,
hierarchy has been adopted internationally under the auspices of ITU-T (Table 8.3).

## Slide 20
Notes: The basis of the TDM hierarchy (in North America and Japan) is the DS-1
transmission format (Figure 8.9), which multiplexes 24 channels. Each frame
contains 8 bits per channel plus a framing bit for 24 * 8 + 1 = 193 bits. For voice
transmission, the following rules apply. Each channel contains one word of digitized
voice data. The original analog voice signal is digitized using pulse code modulation
at a rate of 8000 samples per second. Therefore, each channel slot and hence each
frame must repeat 8000 times per second. With a frame length of 193 bits, we have
a data rate of 8000 * 193 = 1.544 Mbps. For five of every six frames, 8-bit PCM samples
are used. For every sixth frame, each channel contains a 7-bit PCM word plus
a signaling bit . The signaling bits form a stream for each voice channel that contains
network control and routing information. For example, control signals are used to
establish a connection or terminate a call.
The same DS-1 format is used to provide digital data service. For compatibility
with voice, the same 1.544-Mbps data rate is used. In this case, 23 channels of
data are provided. The twenty-fourth channel position is reserved for a special sync
byte, which allows faster and more reliable reframing following a framing error.
Within each channel, 7 bits per frame are used for data, with the eighth bit used to
indicate whether the channel, for that frame, contains user data or system control
data. With 7 bits per channel, and because each frame is repeated 8000 times per
second, a data rate of 56 kbps can be provided per channel. Lower data rates are
provided using a technique known as subrate multiplexing. For this technique, an
additional bit is robbed from each channel to indicate which subrate multiplexing
rate is being provided. This leaves a total capacity per channel of 6 * 8000 = 48 kbps.
This capacity is used to multiplex five 9.6-kbps channels, ten 4.8-kbps channels,
or twenty 2.4-kbps channels. For example, if channel 2 is used to provide 9.6-kbps
service, then up to five data subchannels share this channel. The data for each subchannel
appear as six bits in channel 2 every fifth frame.
Finally, the DS-1 format can be used to carry a mixture of voice and data
channels. In this case, all 24 channels are utilized; no sync byte is provided.
Above the DS-1 data rate of 1.544 Mbps, higher-level multiplexing is achieved
by interleaving bits from DS-1 inputs. For example, the DS-2 transmission system
combines four DS-1 inputs into a 6.312-Mbps stream. Data from the four sources
are interleaved 12 bits at a time. Note that 1.544 * 4 = 6.176 Mbps. The remaining
capacity is used for framing and control bits.

## Slide 21: SONET/SDH
Synchronous Optical Network (ANSI)
Synchronous Digital Hierarchy (ITU-T)
High speed capability of optical fiber
Defines hierarchy of signal rates
    Synchronous Transport Signal level 1 (STS-1) or Optical Carrier level 1 (OC-1) is 51.84Mbps
    Carries one DS-3 or multiple (DS1 DS1C DS2) plus ITU-T rates (e.g., 2.048Mbps)
    Multiple STS-1 combine into STS-N signal
    ITU-T lowest rate is 155.52Mbps (STM-1)
Notes: SONET (Synchronous Optical Network) is an optical transmission interface originally proposed by BellCore and standardized by ANSI. A compatible version, referred to as Synchronous Digital Hierarchy (SDH), has been published by ITU-T in Recommendation G.707. SONET is intended to provide a specification for taking advantage of the high-speed digital transmission capability of optical fiber.

## Slide 22: Table 8.4 SONET/SDH Signal Hierarchy
Notes: The SONET specification defines a hierarchy of standardized digital data rates (Table 8.4). The lowest level, referred to as STS-1 (Synchronous Transport Signal level 1) or OC-1 (Optical Carrier level 1), is 51.84 Mbps. This rate can be used to carry a single DS-3 signal or a group of lower-rate signals, such as DS1, DS1C, DS2, plus ITU-T rates (e.g., 2.048 Mbps). An OC-N rate is the optical equivalent of an STS-N electrical signal. End user devices transmit and receive electrical signals; these must be converted to and from optical signals for transmission over optical fiber. Multiple STS-1 signals can be combined to form an STS-N signal. The signal is created by interleaving bytes from N STS-1 signals that are mutually synchronized. For the ITU-T Synchronous Digital Hierarchy, the lowest rate is 155.52 Mbps, which is designated STM-1. This corresponds to SONET STS-3.

## Slide 23
Notes: The basic SONET building block is the STS-1 frame, which consists of 810 octets and is transmitted once every 125 µs, for an overall data rate of 51.84 Mbps (Figure 8.10a). The frame can logically be viewed as a matrix of 9 rows of 90 octets each, with transmission being one row at a time, from left to right and top to bottom.
Figure 8.10b shows the general format for higher-rate frames, using the ITU-T
designation.

## Slide 24
Notes: The first three columns (3 octets * 9 rows = 27 octets) of the frame are
devoted to overhead octets. Nine octets are devoted to section-related overhead
and 18 octets are devoted to line overhead. Figure 8.11a shows the arrangement of
overhead octets.
The remainder of the frame is payload. The payload includes a column of path
overhead, which is not necessarily in the first available column position; the line overhead
contains a pointer that indicates where the path overhead starts. Figure 8.11b
shows the arrangement of path overhead octets, and Table 8.5 defines these.

## Slide 25
Table 8.5
STS-1 Overhead Bits
(Table can be found on page 277 in textbook)
Notes: Table 8.5 defines the various fields.

## Slide 26: Cable Modems
Downstream
Cable scheduler delivers data in small packets
Active subscribers share downstream capacity
Also allocates upstream time slots to subscribers
Upstream
User requests timeslots on shared upstream channel
Headend scheduler notifies subscriber of slots to use
-Dedicate two cable TV channels to data transfer
-Each channel shared by number of subscribers
using statistical TDM
Notes: A cable modem is a device that allows a user to access the Internet and other online services through a cable television network. To support data transfer to and from a cable modem, a cable TV provider dedicates two 6-MHz channels, one for transmission in each direction. Each channel is shared by a number of subscribers, and so some scheme is needed for allocating capacity on each channel for transmission. Typically, a form of statistical TDM is used, as illustrated in Figure 8.12. In the downstream direction, cable headendto subscriber, a cable scheduler delivers data in the form of small packets. Because the channel is shared by a number of subscribers, if more than one subscriber is active, each subscriber gets only a fraction of the downstream capacity. An individual cable modem subscriber may experience access speeds from 500 kbps to 1.5 Mbps or more, depending on the network architecture and traffic load. The downstream direction is also used to grant time slots to subscribers. When a subscriber has data to transmit, it must first request time slots on the shared upstream channel. Each subscriber is given dedicated time slots for this request purpose. The headend scheduler responds to a request packet by sending back an assignment of future time slots to be used by this subscriber. Thus, a number of subscribers can share the same upstream channel without conflict

## Slide 27
Notes: Figure 8.12
Cable Modem Scheme

## Slide 28: Cable Spectrum Division
To support both cable television programming and data channels, the cable spectrum is divided in to three ranges:
  User-to-network data (upstream): 5 - 40 MHz
  Television delivery (downstream): 50 - 550 MHz
  Network to user data (downstream): 550 - 750 MHz
Notes: To support both cable television programming and data channels, the cable spectrum is divided in to three ranges, each of which is further divided into 6-MHz channels. In North America, the spectrum division is as follows:
User-to-network data (upstream): 5 - 40 MHz
Television delivery (downstream): 50 - 550 MHz
Network to user data (downstream): 550 - 750 MHz

## Slide 29
Notes: Figure 8.13 shows a typical cable modem configuration at a residential or office location. At the interface to the external cable, a one-to-two splitter enables the subscriber to continue to receive cable television service through numerous FDM 6-MHz channels while simultaneously supporting data channels to one or more computers in a local area network. The inbound channel first goes through a radio frequency (RF) tuner that selects and demodulates the data channel down to a spectrum of 0 to 6 MHz. This channel provides a data stream encoded using 64-QAM (quadrature amplitude modulation) or 256-QAM. The QAM demodulator extracts the encoded data stream and converts it to a digital signal that it passes to the media access control (MAC) module. In the outbound direction, a data stream is modulated using either QPSK (quadrature phase shift keying) or 16-QAM.

## Slide 30: Asymmetrical Digital Subscriber Line (ADSL)
Link between subscriber and network
Uses currently installed twisted pair cable
Is Asymmetric - bigger downstream than up
Uses Frequency Division Multiplexing
  Reserve lowest 25kHz for voice (POTS)
  Uses echo cancellation or FDM to give two bands
Has a range of up to 5.5km
Notes: In the implementation and deployment of a high-speed wide area public digital network, the most challenging part is the link between subscriber and network: the digital subscriber line. ADSL is the most widely publicized of a family of new modem technologies designed to provide high-speed digital data transmission over ordinary telephone wire. The term asymmetric refers to the fact that ADSL provides more capacity downstream (from the carrier’s central office to the customer’s site) than upstream (from customer to carrier), being a good fit to Internet requirements. ADSL uses frequency division multiplexing (FDM) in a novel way to exploit the 1-MHz capacity of twisted pair. When echo cancellation is used, the entire frequency band for the upstream channel overlaps the lower portion of the downstream channel. The ADSL scheme provides a range of up to 5.5 km, depending on the diameter of the cable and its quality.

## Slide 31
Notes: The term asymmetric refers to the fact that ADSL provides more capacity downstream
(from the carrier’s central office to the customer’s site) than upstream
(from customer to carrier). ADSL was originally targeted at the expected need
for video on demand and related services. This application has not materialized.
However, since the introduction of ADSL technology, the demand for high-speed
access to the Internet has grown. Typically, the user requires far higher capacity
for downstream than for upstream transmission. Most user transmissions are in
the form of keyboard strokes or transmission of short e-mail messages, whereas
incoming traffic, especially Web traffic, can involve large amounts of data and
include images or even video. Thus, ADSL provides a perfect fit for the Internet
requirement.
ADSL uses frequency-division multiplexing in a novel way to exploit the
1-MHz capacity of twisted pair. There are three elements of the ADSL strategy
(Figure 8.14):
• Reserve lowest 25 kHz for voice, known as POTS (plain old telephone service).
The voice is carried only in the 0 to 4 kHz band; the additional bandwidth is to
prevent crosstalk between the voice and data channels.
• Use either echo cancellation or FDM to allocate two bands, a smaller
upstream band and a larger downstream band.
• Use FDM within the upstream and downstream bands. In this case, a single bit
stream is split into multiple parallel bit streams and each portion is carried in a
separate frequency band.
When echo cancellation is used, the entire frequency band for the upstream
channel overlaps the lower portion of the downstream channel. This has two
advantages compared to the use of distinct frequency bands for upstream and
downstream.
• The higher the frequency, the greater the attenuation. With the use of echo
cancellation, more of the downstream bandwidth is in the “good” part of the
spectrum.
• The echo cancellation design is more flexible for changing upstream capacity.
The upstream channel can be extended upward without running into the
downstream; instead, the area of overlap is extended.
The disadvantage of the use of echo cancellation is the need for echo cancellation
logic on both ends of the line.
The ADSL scheme provides a range of up to 5.5 km, depending on the diameter
of the cable and its quality. This is sufficient to cover about 95% of all U.S.
subscriber lines and should provide comparable coverage in other nations.

## Slide 32: Discrete Multitone (DMT)
Multiple carrier signals at different frequencies
Divide into 4kHz subchannels
Test and use subchannels with better SNR
256 downstream subchannels at 4kHz (60kbps)
  In theory 15.36Mbps, in practice 1.5-9Mbps
Notes: Discrete multitone (DMT) uses multiple carrier signals at different frequencies,
sending some of the bits on each channel. The available transmission band (upstream
or downstream) is divided into a number of 4-kHz subchannels. On initialization,
the DMT modem sends out test signals on each subchannel to determine the signal-to-
noise ratio. The modem then assigns more bits to channels with better signal
transmission qualities and less bits to channels with poorer signal transmission qualities.
Figure 8.15 illustrates this process. Each subchannel can carry a data rate of
from 0 to 60 kbps. The figure shows a typical situation in which there is increasing
attenuation and hence decreasing signal-to-noise ratio at higher frequencies. As a
result, the higher-frequency subchannels carry less of the load.

## Slide 33
Notes: Figure 8.16 provides a general block diagram for DMT transmission. After
initialization, the bit stream to be transmitted is divided into a number of substreams,
one for each subchannel that will carry data. The sum of the data rates of
the substreams is equal to the total data rate. Each substream is then converted to
an analog signal using quadrature amplitude modulation, described in Chapter 5.
This scheme works easily because of QAM’s ability to assign different numbers of
bits per transmitted signal. Each QAM signal occupies a distinct frequency band, so
these signals can be combined by simple addition to produce the composite signal
for transmission.
Present ADSL/DMT designs employ 256 downstream subchannels. In theory,
with each 4-kHz subchannel carrying 60 kbps, it would be possible to transmit at a
rate of 15.36 Mbps. In practice, transmission impairments prevent attainment of this
data rate. Current implementations operate at from 1.5 to 9 Mbps, depending on
line distance and quality.

## Slide 34
Notes: Figure 8.17 shows a typical configuration for broadband service using DSL. The
DSL link is between the provider central office and the residential or business
premises. On the customer side, a splitter allows simultaneous telephone and data
service. The data service makes use of a DSL modem, sometimes referred to as a
G.DMT modem, because the modem conforms to the ITU-T G.992.1 recommendation
for DMT over DSL. The DSL data signal can be further divided into a video
stream and a data stream. The latter connects the modem to either a single local
computer or to a wireless modem/router, which enables the customer to support a
wireless local area network.
On the provider side, a splitter is also used to separate the telephone service
from the Internet service. The voice traffic is connected to the public switched
telephone network (PSTN), thus providing the same service as an ordinary telephone
line to the subscriber. The data traffic connects to a DSL access multiplexer
(DSLAM), which multiplexes multiple customer DSL connections on to a single
high-speed asynchronous transfer mode line. The ATM line connects via one or
more ATM switches to a router that provides an entry point to the Internet.

## Slide 35: Table 8.6 Comparison of xDSL Alternatives
UTP = unshielded twisted pair
Notes: ADSL is one of a number of recent schemes for providing high-speed digital transmission
of the subscriber line. Table 8.6 summarizes and compares some of the most
important of these new schemes, which collectively are referred to as xDSL.

## Slide 36: xDSL
High data rate DSL (HDSL)
  2B1Q coding on dual twisted pairs
  Up to 2Mbps over 3.7km
Single line DSL
  2B1Q coding on single twisted pair (residential) with echo cancelling
  Up to 2Mbps over 3.7km
Very high data rate DSL
  DMT/QAM for very high data rates
  Separate bands for separate services
Notes: HDSL was developed in the late 1980s by BellCore to provide a more cost-effective
means of delivering a T1 data rate (1.544 Mbps). The standard T1 line uses alternate
mark inversion (AMI) coding, which occupies a bandwidth of about 1.5 MHz.
Because such high frequencies are involved, the attenuation characteristics limit the
use of T1 to a distance of about 1 km between repeaters. Thus, for many subscriber
lines one or more repeaters are required, which adds to the installation and maintenance
expense.
HDSL uses the 2B1Q coding scheme to provide a data rate of up to 2 Mbps
over two twisted-pair lines within a bandwidth that extends only up to about
196 kHz. This enables a range of about 3.7 km to be achieved.
Although HDSL is attractive for replacing existing T1 lines, it is not suitable for
residential subscribers because it requires two twisted pair, whereas the typical residential
subscriber has a single twisted pair. SDSL was developed to provide the
same type of service as HDSL but over a single twisted-pair line. As with HDSL,
2B1Q coding is used. Echo cancellation is used to achieve full-duplex transmission
over a single pair.
One of the newest xDSL schemes is VDSL. As of this writing, many of the details
of this signaling specification remain to be worked out. The objective is to provide
a scheme similar to ADSL at a much higher data rate by sacrificing distance. The
likely signaling technique is DMT/QAM.
VDSL does not use echo cancellation but provides separate bands for different
services, with the following tentative allocation:
• POTS: 0–4 kHz
• ISDN: 4–80 kHz
• Upstream: 300–700 kHz
• Downstream: ≥ 1 MHz

## Slide 37
F
Notes: FDD, by itself, is not a particularly interesting case. FDD simply means that two
stations have a full-duplex connection in which each station transmits on a separate
frequency band. The two frequency bands are separated from each other
and from other bands on the network by guard bands, to prevent interference
(Figure 8.18a). The combination of the two frequency bands is often referred to as
a subchannel , with the combination of the two subchannels viewed as a full-duplex
channel between the stations.

## Slide 38
TDMA/FDD
Notes: In TDD, also known as time-compression multiplexing (TCM) , data are transmitted
in one direction at a time, with transmission alternating between the two directions.
To achieve the desired subscriber data rate with simple TDD, the transmitter’s bit
stream is divided into equal segments, compressed in time to a higher transmission
rate, and transmitted in bursts, which are expanded at the other end to the original
rate. A short quiescent period is used between bursts going in opposite directions to
allow the channel to settle down. Thus, the actual data rate on the channel must be
greater than twice the data rate required by the two end systems.
The timing implications are shown in Figure 8.19b.
TDD is used in cordless telephones and is a building block for a number of
wireless network systems.

## Slide 39: FDMA
Frequency-Division Multiple Access
  Technique used to share the spectrum among multiple stations
  Base station assigns bandwidths to stations within the overall bandwidth available
  Key features:
Each subchannel is dedicated to a single station
If a subchannel is not in use, it is idle; the capacity is wasted
Requires fewer overhead bits because each subchannel is dedicated
Individual subchannels must be separated by guard bands to minimize interference
Notes: FDMA is a technique used to share the spectrum among multiple stations. In a
typical configuration, there is a base station that communicates with a number of
subscriber stations. Such a configuration is found in satellite networks, cellular
networks, Wi-Fi, and WiMAX. Typically, the base station assigns bandwidths to
stations within the overall bandwidth available. Figure 8.19a is an example. Three
stations are assigned separate frequency bands (subchannels) for transmission to
the base station (uplink direction), with guard bands between the assigned transmission
bands. Another frequency band, typically wider, is reserved for transmission
from the base station to the other stations (downlink direction).
Key features of FDMA include the following:
• Each subchannel is dedicated to a single station; it is not shared.
• If a subchannel is not in use, it is idle; the capacity is wasted.
• FDMA is relatively less complex than TDMA and requires fewer overhead
bits because each subchannel is dedicated.
• Individual subchannels must be separated by guard bands to minimize
interference.
As with FDMA, TDMA is typically used in a configuration that consists of a base
station and a number of subscriber stations. With TDMA there is a single, relatively
large, uplink frequency band that is used to transmit a sequence of time slots.
Repetitive time slots are assigned to an individual subscriber station to form a logical
subchannel. is an example. In this example, each station gets an equal amount
of the overall capacity of the uplink channel. Thus, each channel is assigned every
third slot. Similarly, each subscriber station listens on designated time slots on the
downlink channel, which may have the same slot assignment as the uplink channel,
or a different one. In this example, the downlink channel is also equally distributed
among the three stations.
Key features of TDMA include the following:
• Each subchannel is dedicated to a single station; it is not shared.
• For an individual station, data transmission occurs in bursts rather than
continuously.
• Guard times are needed between time slots, to account for lack of perfect synchronization
among the subscriber station.
• The downlink channel may be on a separate frequency band, as in our example.
This is referred to as TDMA/FDD. With TDMA/FDD, the time slots
assigned for subscriber station reception are typically nonoverlapping with
that station’s transmit time slots.
• The uplink and downlink transmission may be on the same frequency band,
which is referred to as TDMA/TDD.

## Slide 40: TDMA
Time-Division Multiple Access
  There is a single, relatively large, uplink frequency band that is used to transmit a sequence of time slots
  Repetitive time slots are assigned to an individual subscriber station to form a logical subchannel
  Key features:
Each subchannel is dedicated to a single station
For an individual station data transmission occurs in bursts rather than continuously
Guard times are needed between time slots, to account for lack of perfect synchronization among the subscriber station
Downlink channel may be on a separate frequency band
The uplink and downlink transmission may be on the same frequency band

## Slide 41: Summary
Frequency-division multiplexing
  Characteristics
  Analog carrier systems
  Wavelength division multiplexing
Synchronous time-division multiplexing
  Characteristics
  TDM link control
  Digital carrier systems
  SONET/SDH
Cable modems
Asymmetric digital subscriber line
  ADSL design
  Discrete multitone
  Broadband access configuration
xDSL
  High data rate digital subscriber line
  Single-line digital subscriber line
  Very high data rate digital subscriber line
Multiple channel access
  Frequency-division duplex (FDD)
  Time-division duplex (TDD)
  Frequency-division multiple access (FDMA)
  Time-division multiple access (TDMA)
Notes: Chapter 8summary.