## Slide 1: Data and Computer Communications
Tenth Edition
by William Stallings
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 9 “WAN Technology and Protocols”.

## Slide 2: WAN Technology and Protocols
Chapter 9
Notes: Part Two describes how information can be encoded and transmitted over
a communications link. We now turn to the broader discussion of networks,
which can be used to interconnect many devices. The chapter begins with a
general discussion of switched communications networks. The remainder
of the chapter focuses on wide area networks and, in particular, on traditional
approaches to wide area network design: circuit switching and packet
switching.
Since the invention of the telephone, circuit switching has been the
dominant technology for voice communications, and it has remained so well
into the digital era. This chapter looks at the key characteristics of a circuit-switching
network.
Around 1970, research began on a new form of architecture for long-distance
digital data communications: packet switching. Although the technology
of packet switching has evolved substantially since that time, it is
remarkable that (1) the basic technology of packet switching is fundamentally
the same today as it was in the early 1970s networks, and (2) packet switching
remains one of the few effective technologies for long-distance data
communications.
This chapter provides an overview of packet-switching technology. We
will see, in this chapter and later in this part, that many of the advantages
of packet switching (flexibility, resource sharing, robustness, responsiveness)
come with a cost. The packet-switching network is a distributed collection
of packet-switching nodes. Ideally, all packet-switching nodes would always
know the state of the entire network. Unfortunately, because the nodes are
distributed, there is a time delay between a change in status in one portion of
the network and knowledge of that change elsewhere. Furthermore, there is
overhead involved in communicating status information. As a result, a packet-switching
network can never perform “perfectly,” and elaborate algorithms
are used to cope with the time delay and overhead penalties of network operation.
These same issues will appear again when we discuss internetworking in
Part Five.

## Slide 3: Switched Communications Networks
Switching nodes - provide a switching facility that move data between nodes
Stations – devices attached to the network
Nodes – switching devices that provide communication
Communications network – collection of nodes
Switched communication network – data entering the network from a station are routed to the destination by being switched from node to node
Notes: For transmission of data beyond a local area, communication is typically achieved
by transmitting data from source to destination through a network of intermediate
switching nodes; this switched network design is typically used to implement LANs
as well. The switching nodes are not concerned with the content of the data; rather,
their purpose is to provide a switching facility that will move the data from node to
node until they reach their destination. Figure 9.1 illustrates a simple network. The
devices attached to the network may be referred to as stations . The stations may
be computers, terminals, telephones, or other communicating devices. We refer to
the switching devices whose purpose is to provide communication as nodes . Nodes
are connected to one another in some topology by transmission links. Each station
attaches to a node, and the collection of nodes is referred to as a communications
network .
In a switched communication network , data entering the network from a station
are routed to the destination by being switched from node to node.
Two different technologies are used in wide area switched networks: circuit
switching and packet switching. These two technologies differ in the way the
nodes switch information from one link to another on the way from source to
destination.

## Slide 4
Notes: In Figure 9.1, data from station A intended for station F are
sent to node 4. They may then be routed via nodes 5 and 6 or nodes 7 and 6 to
the destination. Several observations are in order:
1. Some nodes connect only to other nodes (e.g., 5 and 7). Their sole task is the
internal (to the network) switching of data. Other nodes have one or more
stations attached as well; in addition to their switching functions, such nodes
accept data from and deliver data to the attached stations.
2. Node–station links are generally dedicated point-to-point links. Node–node
links are usually multiplexed, using either frequency-division multiplexing
(FDM) or time-division multiplexing (TDM).
3. Usually, the network is not fully connected; that is, there is not a direct link
between every possible pair of nodes. However, it is always desirable to have
more than one possible path through the network for each pair of stations.
This enhances the reliability of the network.

## Slide 5: Circuit Switching
Uses a dedicated path between two stations
Can be inefficient
  Channel capacity dedicated for duration of connection
  If no data, capacity is wasted
Set up (connection) takes time
Once connected, transfer is transparent
Has three phases
Establish
Transfer
Disconnect
Notes: Communication via circuit switching implies that there is a dedicated communication
path between two stations. That path is a connected sequence of links between
network nodes. On each physical link, a logical channel is dedicated to the connection.
Communication via circuit switching involves three phases, which can be
explained with reference to Figure 9.1.
1. Circuit establishment . Before any signals can be transmitted, an end-to-end
(station-to-station) circuit must be established. For example, station A sends a
request to node 4 requesting a connection to station E. Typically, the link from
A to 4 is a dedicated line, so that part of the connection already exists. Node
4 must find the next leg in a route leading to E. Based on routing information
and measures of availability and perhaps cost, node 4 selects the link to node
5, allocates a free channel (using FDM or TDM) on that link, and sends a
message requesting connection to E. So far, a dedicated path has been established
from A through 4 to 5. Because a number of stations may attach to 4,
it must be able to establish internal paths from multiple stations to multiple
nodes. How this is done is discussed later in this section. The remainder of the
process proceeds similarly. Node 5 allocates a channel to node 6 and internally
ties that channel to the channel from node 4. Node 6 completes the connection
to E. In completing the connection, a test is made to determine if E is busy or
is prepared to accept the connection.
2. Data transfer . Data can now be transmitted from A through the network to E.
The transmission may be analog or digital, depending on the nature of the
network. As the carriers evolve to fully integrated digital networks, the use of
digital (binary) transmission for both voice and data is becoming the dominant
method. The path is A-4 link, internal switching through 4, 4-5 channel, internal
switching through 5, 5-6 channel, internal switching through 6, 6-E link.
Generally, the connection is full duplex.
3. Circuit disconnect . After some period of data transfer, the connection is
terminated, usually by the action of one of the two stations. Signals must be
propagated to nodes 4, 5, and 6 to deallocate the dedicated resources.
Note that the connection path is established before data transmission begins.
Thus, channel capacity must be reserved between each pair of nodes in the path, and
each node must have available internal switching capacity to handle the requested
connection. The switches must have the intelligence to make these allocations and
to devise a route through the network.
Circuit switching can be rather inefficient. Channel capacity is dedicated for
the duration of a connection, even if no data are being transferred. For a voice connection,
utilization may be rather high, but it still does not approach 100%. For a
client/server or terminal-to-computer connection, the capacity may be idle during
most of the time of the connection. In terms of performance, there is a delay prior
to signal transfer for call establishment. However, once the circuit is established, the
network is effectively transparent to the users. Information is transmitted at a fixed
data rate with no delay other than the propagation delay through the transmission
links. The delay at each node is negligible.

## Slide 6
Notes: Circuit switching was developed to handle voice traffic but is now also used
for data traffic. The best-known example of a circuit-switching network is the public
telephone network (Figure 9.2). This is actually a collection of national networks
interconnected to form the international service. Although originally designed and
implemented to service analog telephone subscribers, it handles substantial data
traffic via modem and is gradually being converted to a digital network. Another
well-known application of circuit switching is the private branch exchange (PBX),
used to interconnect telephones within a building or office. Circuit switching is
also used in private networks. Typically, such a network is set up by a corporation
or other large organization to interconnect its various sites. Such a network usually
consists of PBX systems at each site interconnected by dedicated, leased lines
obtained from one of the carriers, such as AT&T. A final common example of the
application of circuit switching is the data switch. The data switch is similar to the
PBX but is designed to interconnect digital data processing devices, such as terminals
and computers.
A public telecommunications network can be described using four generic
architectural components:
• Subscribers : The devices that attach to the network. It is still the case that most
subscriber devices to public telecommunications networks are telephones, but
the percentage of data traffic increases year by year.
• Subscriber line : The link between the subscriber and the network, also referred
to as the subscriber loop or local loop . Almost all local loop connections use
twisted-pair wire. The length of a local loop is typically in a range from a few
kilometers to a few tens of kilometers.
• Exchanges : The switching centers in the network. A switching center that
directly supports subscribers is known as an end office. Typically, an end office
will support many thousands of subscribers in a localized area. There are over
19,000 end offices in the United States, so it is clearly impractical for each end
office to have a direct link to each of the other end offices; this would require
on the order of 2 * 108 links. Rather, intermediate switching nodes are used.
• Trunks : The branches between exchanges. Trunks carry multiple voice-frequency
circuits using either FDM or synchronous TDM. We referred to
these as carrier systems in Chapter 8.

## Slide 7
Notes: Subscribers connect directly to an end office, which switches traffic between
subscribers and between a subscriber and other exchanges. The other exchanges are
responsible for routing and switching traffic between end offices. This distinction is
shown in Figure 9.3. To connect two subscribers attached to the same end office, a circuit
is set up between them in the same fashion as described before. If two subscribers
connect to different end offices, a circuit between them consists of a chain of circuits
through one or more intermediate offices. In the figure, a connection is established
between lines a and b by simply setting up the connection through the end office. The
connection between c and d is more complex. In c’s end office, a connection
is established between line c and one channel on a TDM trunk to the intermediate switch. In
the intermediate switch, that channel is connected to a channel on a TDM trunk to d’s
end office. In that end office, the channel is connected to line d.

## Slide 8: Circuit-Switching Technology
Driven by applications that handle voice traffic
  Key requirement is no transmission delay and no variation in delay
Efficient for analog transmission of voice signals
Inefficient for digital transmission
Transparent
  Once a circuit is established it appears as a direct connection; no special logic is needed
Notes: Circuit-switching technology has been driven by those applications that handle
voice traffic. One of the key requirements for voice traffic is that there must be
virtually no transmission delay and certainly no variation in delay. A constant signal
transmission rate must be maintained, because transmission and reception occur
at the same signal rate. These requirements are necessary to allow normal human
conversation. Further, the quality of the received signal must be sufficiently high to
provide, at a minimum, intelligibility.
Circuit switching achieved its widespread, dominant position because it is well
suited to the analog transmission of voice signals. In today’s digital world, its inefficiencies
are more apparent. However, despite its inefficiencies, circuit switching
will remain an attractive choice for both local area and wide area networking. One
of its key strengths is that it is transparent. Once a circuit is established, it appears
as a direct connection to the two attached stations; no special networking logic is
needed at the station.

## Slide 9
Notes: The technology of circuit switching is best approached by examining the operation of
a single circuit-switching node. A network built around a single circuit-switching node
consists of a collection of stations attached to a central switching unit. The central
switch establishes a dedicated path between any two devices that wish to communicate.
Figure 9.4 depicts the major elements of such a one-node network. The dotted
lines inside the switch symbolize the connections that are currently active.

## Slide 10: Circuit-Switching Concepts
Digital switch
Provides a transparent signal path
Must allow full-duplex transmission
Network interface
Functions and hardware needed to connect digital devices
Control unit
Establishes, maintains, and tears down the connection
Notes: The heart of a modern system is a digital switch. The function of the digital switch is to provide a transparent signal path between any pair of attached devices. The path is transparent in that it appears to the attached pair of devices that there is a direct connection between them. Typically, the connection must allow full-duplex transmission.
The network interface element represents the functions and hardware needed to connect digital devices, such as data processing devices and digital telephones, to the network. Analog telephones can also be attached if the network interface contains the logic for converting to digital signals. Trunks to other digital switches carry TDM signals and provide the links for constructing multiple-node networks.
The control unit performs three general tasks. First, it establishes connections. This is generally done on demand, that is, at the request of an attached device. Second, the control unit must maintain the connection. Because the digital switch uses time division principles, this may require ongoing manipulation of the switching elements. Third, the control unit must tear down the connection, either in response to a request from one of the parties or for its own reasons.

## Slide 11: Blocking or Non-blocking
Blocking network
  May be unable to connect stations because all paths are in use
  Used on voice systems because it is expected for phone calls to be of short duration and that only a fraction of the phones will be engaged at any one time
Non-blocking network
  Permits all stations to connect at once
  Grants all possible connection requests as long as the called party is free
  When using data connections terminals can be continuously connected for long periods of time so nonblocking configurations are required
Notes: An important characteristic of a circuit-switching device is whether it is blocking or nonblocking. Blocking occurs when the network is unable to connect two stations because all possible paths between them are already in use. A blocking network is one in which such blocking is possible. Hence a nonblocking network permits all stations to be connected (in pairs) at once and grants all possible connection requests as long as the called party is free. When a network is supporting only voice traffic, a blocking configuration is generally acceptable, because it is expected that most phone calls are of short duration and that therefore only a fraction of the telephones will be engaged at any time. However, when data processing devices are involved, these assumptions may be invalid. For example, for a data entry application, a terminal may be continuously connected to a computer for hours at a time. Hence, for data applications, there is a requirement for a nonblocking or "nearly nonblocking" (very low probability of blocking) configuration.

## Slide 12: Space Division Switching
Originally developed for analog, space division switching has been carried over into the digital realm
Signal paths are physically separate from one another
Path is dedicated solely to transfer signals
Basic building block of switch is a metallic crosspoint or semiconductor gate
Notes: Space division switching was originally developed for the analog environment and
has been carried over into the digital realm. The fundamental principles are the
same, whether the switch is used to carry analog or digital signals. As its name
implies, a space division switch is one in which the signal paths are physically
separate from one another (divided in space). Each connection requires the establishment
of a physical path through the switch that is dedicated solely to the transfer
of signals between the two endpoints. The basic building block of the switch is a
metallic crosspoint or semiconductor gate that can be enabled and disabled by a
control unit.

## Slide 13
Notes: Figure 9.5 shows a simple crossbar matrix with 10 full-duplex
I/O lines. The matrix has 10 inputs and 10 outputs; each station attaches to the
matrix via one input and one output line. Interconnection is possible between
any two lines by enabling the appropriate crosspoint. Note that a total of 100
crosspoints is required.
The crossbar switch has a number of limitations:
• The number of crosspoints grows with the square of the number of attached
stations. This is costly for a large switch.
• The loss of a crosspoint prevents connection between the two devices whose
lines intersect at that crosspoint.
• The crosspoints are inefficiently utilized; even when all of the attached devices
are active, only a small fraction of the crosspoints are engaged.
To overcome these limitations, multiple-stage switches are employed.

## Slide 14
Notes: Figure 9.6 is an example of a three-stage switch.
A multiple-stage switch has two advantages over a single-stage crossbar matrix:
• The number of crosspoints is reduced, increasing crossbar utilization. In
Examples 9.2 and 9.3, the total number of crosspoints for 10 stations is reduced
from 100 to 48.
• There is more than one path through the network to connect two endpoints,
increasing reliability.
Of course, a multistage network requires a more complex control scheme. To
establish a path in a single-stage network, it is only necessary to enable a single gate.
In a multistage network, a free path through the stages must be determined and the
appropriate gates enabled.
A consideration with a multistage space division switch is that it may be
blocking. It should be clear from Figure 9.5 that a single-stage crossbar matrix is
nonblocking; that is, a path is always available to connect an input to an output.
That this may not be the case with a multiple-stage switch can be seen in Figure 9.6.
The heavier lines indicate the lines that are already in use. In this state, input line
10, for example, cannot be connected to output line 3, 4, or 5, even though all of
these output lines are available. A multiple-stage switch can be made nonblocking
by increasing the number or size of the intermediate switches, but of course this
increases the cost.

## Slide 15: Time Division Switching
Modern digital systems use intelligent control of space & time division elements
Use digital time division techniques to set up and maintain virtual circuits
Partition low speed bit stream into pieces that share higher speed stream
Individual pieces manipulated by control logic to flow from input to output
Notes: The technology of switching has a long history, most of it covering an era when
analog signal switching predominated. With the advent of digitized voice and
synchronous
TDM techniques, both voice and data can be transmitted via digital
signals. This has led to a fundamental change in the design and technology of
switching systems. Instead of the relatively dumb space division approach, modern
digital systems rely on intelligent control of space and time-division elements.
Virtually all modern circuit switches use digital time-division techniques for
establishing and maintaining “circuits.” Time-division switching involves the partitioning
of a lower-speed bit stream into pieces that share a higher-speed stream with
other bit streams. The individual pieces, or slots, are manipulated by control logic to
route data from input to output.

## Slide 16
Notes: The basic building block of many time-division switches is the time-slot interchange
(TSI) mechanism. A TSI unit operates on a synchronous TDM stream of time
slots, or channels, by interchanging pairs of slots to achieve a full-duplex operation.
Figure 9.7a shows how the input line of device I is connected to the output line of
device J , and vice versa.
The input lines of N devices are passed through a synchronous time-division
multiplexer to produce a TDM stream with N slots. To allow the interchange of any
two slots, to create a full-duplex connection, the incoming data in a slot must be
stored until the data can be sent out on the correct channel in the next TDM frame
cycle. Hence, the TSI introduces a delay and produces output slots in the desired
order. The output stream of slots is then demultiplexed and routed to the appropriate
output line. Because each channel is provided a time slot in each TDM frame,
whether or not it transmits data, the size of the TSI unit must be chosen for the
capacity of the line, not for the actual data rate.
Figure 9.7b shows a mechanism for implementing TSI. A random access data
store whose width equals one time slot of data and whose length equals the number
of slots in a frame is used. An incoming TDM frame is written sequentially,
slot by slot, into the data store. An outgoing data frame is created by reading slots
from the memory in an order dictated by an address store that reflects the existing
connections. In the figure, the data in channels I and J are interchanged, creating a
full-duplex connection between the corresponding stations.
TSI is a simple, effective way to switch TDM data. However, the size of such
a switch, in terms of the number of connections, is limited by the amount of latency
that can be tolerated. The greater the number of channels, the greater the average
delay that each channel experiences.

## Slide 17
Notes: To overcome the latency problems of TSI, contemporary time-division switches use
multiple TSI units, each of which carries a portion of the total traffic. To connect
two channels entering a single TSI unit, their time slots can be interchanged, as just
described. However, to connect a channel on one TDM stream (going into one TSI)
to a channel on another TDM stream (going into another TSI), some form of space
division switching is needed. Naturally, we do not wish to switch all of the time slots
from one TDM stream to another; we would like to do it one slot at a time. This
technique is known as time-multiplexed switching (TMS) .
One means of implementing a TMS switch is the crossbar switch discussed
earlier. This requires the crosspoints to be manipulated at each time slot. More commonly,
the TMS switch is implemented using digital selectors. The selector (SEL)
device selects an input line based on a channel assignment provided from a store
controlled by a time-slot counter.
To reduce or eliminate blocking, multiple stage networks can be built by
concatenating TMS (S) and TSI (T) stages. Systems are generally described by an
enumeration of their stages from input to output using the symbols T and S. Figure 9.8
shows an example of a three-stage switch implemented with SEL units.

## Slide 18
Notes: The latest trend in the development of circuit-switching technology is generally
referred to as the softswitch. In essence, a softswitch is a general-purpose computer
running specialized software that turns it into a smart phone switch. Softswitches
cost significantly less than traditional circuit switches and can provide more
functionality. In particular, in addition to handling the traditional circuit-switching
functions, a softswitch can convert a stream of digitized voice bits into packets. This
opens up a number of options for transmission, including the increasingly popular
voice over IP (Internet Protocol) approach.
In any telephone network switch, the most complex element is the software
that controls call processing. This software performs call routing and implements
call-processing logic for hundreds of custom-calling features. Typically, this software
runs on a proprietary processor that is integrated with the physical circuit-switching
hardware. A more flexible approach is to physically separate the call-processing
function from the hardware-switching function. In softswitch terminology, the
physical-switching function is performed by a media gateway (MG) and the callprocessing
logic resides in a media gateway controller (MGC) .
Figure 9.9 contrasts the architecture of a traditional telephone network circuit
switch with the softswitch architecture. In the latter case, the MG and MGC are
distinct entities and may be provided by different vendors. To facilitate interoperability,
ITU-T has issued a standard for a media gateway control protocol between
the MG and MGC: H.248.1 (Gateway Control Protocol, Version 3 , 2005). RFC 2805
(Media Gateway Control Protocol Architecture and Requirements , 2000) provides
an overview of media gateway concepts.

## Slide 19: Packet Switching
Circuit switching was designed for voice
Packet switching was designed for data
Transmitted in small packets
Packets contain user data and control info
  User data may be part of a larger message
  Control information includes routing (addressing)
Packets are received, stored briefly (buffered) and passed on to the next node
Notes: The long-haul circuit-switching telecommunications network was originally designed
to handle voice traffic, and the majority of traffic on these networks continues to
be voice. A key characteristic of circuit-switching networks is that resources within
the network are dedicated to a particular call. For voice connections, the resulting
circuit
will enjoy a high percentage of utilization because, most of the time, one
party or the other is talking. However, as the circuit-switching network began to be
used increasingly for data connections, two shortcomings became apparent:
• In a typical user/host data connection (e.g., personal computer user logged on
to a database server), much of the time the line is idle. Thus, with data connections,
a circuit-switching approach is inefficient.
• In a circuit-switching network, the connection provides for transmission at
a constant data rate. Thus, each of the two devices that are connected must
transmit and receive at the same data rate as the other. This limits the utility of
the network in interconnecting a variety of host computers and workstations.

## Slide 20
Notes: To understand how packet switching addresses these problems, let us
briefly summarize packet-switching operation. Data are transmitted in short
packets. A typical upper bound on packet length is 1000 octets (bytes). If a source
has a longer message to send, the message is broken up into a series of packets
(Figure 9.10). Each packet contains a portion (or all for a short message) of the
user’s data plus some control information. The control information, at a minimum,
includes the information that the network requires to be able to route the packet
through the network and deliver it to the intended destination. At each node en
route, the packet is received, stored briefly, and passed on to the next node.

## Slide 21: Advantages
Line efficiency
  Single link shared by many packets over time
  Packets queued and transmitted as fast as possible
Data rate conversion
  Stations connect to local node at own speed
  Nodes buffer data if required to equalize rates
Packets accepted even when network is busy
Priorities can be used
Notes: Let us return to Figure 9.1, but now assume that it depicts a simple packet switching
network. Consider a packet to be sent from station A to station E. The
packet includes control information that indicates that the intended destination
is E. The packet is sent from A to node 4. Node 4 stores the packet, determines the
next leg of the route (say 5), and queues the packet to go out on that link (the 4-5
link). When the link is available, the packet is transmitted to node 5, which forwards
the packet to node 6, and finally to E. This approach has a number of advantages
over circuit switching:
• Line efficiency is greater, because a single node-to-node link can be dynamically
shared by many packets over time. The packets are queued up and
transmitted as rapidly as possible over the link. By contrast, with circuit
switching, time on a node-to-node link is preallocated using synchronous
time-division multiplexing. Much of the time, such a link may be idle because
a portion of its time is dedicated to a connection that is idle.
• A packet-switching network can perform data-rate conversion. Two stations
of different data rates can exchange packets because each connects to its node
at its proper data rate.
• When traffic becomes heavy on a circuit-switching network, some calls are
blocked; that is, the network refuses to accept additional connection requests
until the load on the network decreases. On a packet-switching network, packets
are still accepted, but delivery delay increases.
• Priorities can be used. If a node has a number of packets queued for transmission,
it can transmit the higher-priority packets first. These packets will
therefore experience less delay than lower-priority packets.

## Slide 22: Switching Techniques
Station breaks long message into packets
Packets sent one at a time to the network
Packets can be handled in two ways:
Datagram
Each packet is treated independently with no reference to previous packets
Virtual circuit
A preplanned route is established before any packets are sent
Notes: If a station has a message to send through a packet-switching network that is of length greater than the maximum packet size, it breaks the message up into packets and sends these packets, one at a time, to the network. A question arises as to how the network will handle this stream of packets as it attempts to route them through the network and deliver them to the intended destination. Two approaches are used in contemporary networks: datagram and virtual circuit.

## Slide 23
Notes: In the datagram approach, each packet is treated independently, with no reference
to packets that have gone before. This approach is illustrated in Figure 9.11,
which shows a time sequence of snapshots of the progress of three packets through
the network. Each node chooses the next node on a packet’s path, taking into account
information received from neighboring nodes on traffic, line failures, and so on. So
the packets, each with the same destination address, do not all follow the same route,
and they may arrive out of sequence at the exit point. In this example, the exit node
restores the packets to their original order before delivering them to the destination.
In some datagram networks, it is up to the destination rather than the exit node to
do the reordering. Also, it is possible for a packet to be destroyed in the network. For
example, if a packet-switching node crashes momentarily, all of its queued packets
may be lost. Again, it is up to either the exit node or the destination to detect the
loss of a packet and decide how to recover it. In this technique, each packet, treated
independently, is referred to as a datagram.

## Slide 24
Notes: In the virtual circuit approach, a preplanned route is established before any
packets are sent. Once the route is established, all the packets between a pair of communicating
parties follow this same route through the network. This is illustrated in
Figure 9.12. Because the route is fixed for the duration of the logical connection, it
is somewhat similar to a circuit in a circuit-switching network and is referred to as a
virtual circuit. Each packet contains a virtual circuit identifier as well as data. Each
node on the preestablished route knows where to direct such packets; no routing
decisions are required. At any time, each station can have more than one virtual
circuit to any other station and can have virtual circuits to more than one station.
So the main characteristic of the virtual circuit technique is that a route
between stations is set up prior to data transfer. Note that this does not mean that
this is a dedicated path, as in circuit switching. A transmitted packet is buffered at
each node, and queued for output over a line, while other packets on other virtual
circuits may share the use of the line. The difference from the datagram approach
is that, with virtual circuits, the node need not make a routing decision for each
packet. It is made only once for all packets using that virtual circuit.

## Slide 25: Virtual Circuits vs. Datagram
Virtual circuits
  Network can provide sequencing and error control
  Packets are forwarded more quickly
  Less reliable
Datagram
  No call setup phase
  More flexible
  More reliable
Notes: If two stations wish to exchange data over an extended period of time, there are certain advantages to virtual circuits. First, the network may provide services related to the virtual circuit, including sequencing and error control. Sequencing refers to the fact that, because all packets follow the same route, they arrive in the original order. Error control is a service that assures not only that packets arrive in proper sequence, but also that all packets arrive correctly. Another advantage is that packets should transit the network more rapidly with a virtual circuit; it is not necessary to make a routing decision for each packet at each node.
One advantage of the datagram approach is that the call setup phase is avoided. Thus, if a station wishes to send only one or a few packets, datagram delivery will be quicker. Another advantage of the datagram service is that, because it is more primitive, it is more flexible. For example, if congestion develops in one part of the network, incoming datagrams can be routed away from the congestion. With the use of virtual circuits, packets follow a predefined route, and thus it is more difficult for the network to adapt to congestion. A third advantage is that datagram delivery is inherently more reliable. With the use of virtual circuits, if a node fails, all virtual circuits that pass through that node are lost. With datagram delivery, if a node fails, subsequent packets may find an alternate route that bypasses that node. A datagram-style of operation is common in internetworks.

## Slide 26
Notes: There is a significant relationship between packet size and transmission time, as
shown in Figure 9.13. In this example, it is assumed that there is a virtual circuit
from station X through nodes a and b to station Y. The message to be sent comprises
40 octets, and each packet contains 3 octets of control information, which is placed
at the beginning of each packet and is referred to as a header. If the entire message
is sent as a single packet of 43 octets (3 octets of header plus 40 octets of data), then
the packet is first transmitted from station X to node a (Figure 9.13a). When the
entire packet is received, it can then be transmitted from a to b. When the entire
packet is received at node b, it is then transferred to station Y. Ignoring switching
time, total transmission time is 129 octet-times (43 octets Å~ 3 packet transmissions).
Suppose now that we break up the message into two packets, each containing
20 octets of the message and, of course, 3 octets each of header, or control information.
In this case, node a can begin transmitting the first packet as soon as it has
arrived from X, without waiting for the second packet. Because of this overlap in
transmission, the total transmission time drops to 92 octet-times. By breaking the
message up into five packets, each intermediate node can begin transmission even
sooner and the savings in time is greater, with a total of 77 octet-times for transmission.
However, this process of using more and smaller packets eventually results in
increased, rather than reduced, delay as illustrated in Figure 9.13d. This is because
each packet contains a fixed amount of header, and more packets mean more of
these headers. Furthermore, the example does not show the processing and queuing
delays at each node. These delays are also greater when more packets are handled
for a single message. However, we shall see in the next chapter that an extremely
small packet size (53 octets) can result in an efficient network design.

## Slide 27: External Network Interface
ITU-T standard for interface between host and packet switched network
Almost universal on packet switched networks and packet switching in ISDN
Defines three layers
Physical
Link
Packet
Notes: One technical aspect of packet-switching networks remains to be examined: the interface
between attached devices and the network. We have seen that a circuit-switching
network provides a transparent communications path for attached devices that makes
it appear that the two communicating stations have a direct link. However, in the case
of packet-switching networks, the attached stations must organize
their data into packets for transmission. This requires a certain level of cooperation between the network
and the attached stations. This cooperation is embodied in an interface standard. The
standard used for traditional packet-switching networks is X.25, which is described in
Appendix U. Another interface standard is frame relay, also discussed in Appendix U.

## Slide 28
Notes: Typically, standards for packet-switching network interfaces define a virtual
circuit service. This service enables any subscriber to the network to set up logical
connections, called virtual circuits, to other subscribers. An example is shown in
Figure 9.14 (compare Figure 9.1). In this example, station A has a virtual circuit
connection to C; station B has two virtual circuits established, one to C and one to
D; and stations E and F each have a virtual circuit connection to D.
In this context, the term virtual circuit refers to the logical connection between
two stations through the network; this is perhaps best termed an external virtual
circuit .Earlier, we used the term virtual circuit to refer to a specific preplanned route
through the network between two stations; this could be called an internal virtual
circuit . Typically, there is a one-to-one relationship between external and internal
virtual circuits. However, it is also possible to employ an external virtual circuit service
with a datagram-style network. What is important for an external virtual circuit is that
there is a logical relationship, or logical channel, established between two stations,
and all of the data associated with that logical channel are considered as part of a
single stream of data between the two stations. For example, in Figure 9.14, station D
keeps track of data packets arriving from three different workstations (B, E, F) on
the basis of the virtual circuit number associated with each incoming packet.

## Slide 29
Notes: A simple comparison of circuit switching and the two forms of
packet switching is provided in Figure 9.15. The figure depicts the transmission of a
message across four nodes, from a source station attached to node 1 to a destination
station attached to node 4. In this figure, we are concerned with three types of delay:
• Propagation delay: The time it takes a signal to propagate from one node to
the next. This time is generally negligible. The speed of electromagnetic signals
through a wire medium, for example, is typically 2 * 108m/s.
• Transmission time: The time it takes for a transmitter to send out a block of
data. For example, it takes 1 s to transmit a 10,000-bit block of data onto a
10-kbps line.
• Node delay: The time it takes for a node to perform the necessary processing
as it switches data.
For circuit switching, there is a certain amount of delay before the message
can be sent. First, a Call Request signal is sent through the network, to set up a
connection to the destination. If the destination station is not busy, a Call Accepted
signal returns. Note that a processing delay is incurred at each node during the call
request; this time is spent at each node setting up the route of the connection. On
the return, this processing is not needed because the connection is already set up.
After the connection is set up, the message is sent as a single block, with no noticeable
delay at the switching nodes.
Virtual circuit packet switching appears quite similar to circuit switching.
A virtual circuit is requested using a Call Request packet, which incurs a delay at
each node. The virtual circuit is accepted with a Call Accept packet. In contrast to the
circuit-switching case, the call acceptance also experiences node delays, even though
the virtual circuit route is now established. The reason is that this packet is queued at
each node and must wait its turn for transmission. Once the virtual circuit is established,
the message is transmitted in packets. It should be clear that this phase of the
operation can be no faster than circuit switching for comparable networks. This is
because circuit switching is an essentially transparent process, providing a constant
data rate across the network. Packet switching involves some delay at each node in
the path. Worse, this delay is variable and will increase with increased load.
Datagram packet switching does not require a call setup. Thus, for short
messages, it will be faster than virtual circuit packet switching and perhaps circuit
switching. However, because each individual datagram is routed independently, the
processing for each datagram at each node may be longer than for virtual circuit
packets. Thus, for long messages, the virtual circuit technique may be superior.
Figure 9.15 is intended only to suggest what the relative performance of the
techniques might be; actual performance depends on a host of factors, including the
size of the network, its topology, the pattern of load, and the characteristics of typical
exchanges.

## Slide 30
Table 9.1
Comparison
of Communication Switching Techniques
(Table can be found on page 315 in textbook)
Notes: Besides performance, there are a number of other
characteristics that may be considered in comparing the techniques we have been
discussing. Table 9.1 summarizes the most important of these. Most of these characteristics
have already been discussed. A few additional comments follow.
As was mentioned, circuit switching is essentially a transparent service. Once a
connection is established, a constant data rate is provided to the connected stations.
This is not the case with packet switching, which typically introduces variable delay,
so that data arrive in a choppy manner. Indeed, with datagram packet switching,
data may arrive in a different order than they were transmitted.
An additional consequence of transparency is that there is no overhead
required to accommodate circuit switching. Once a connection is established, the
analog or digital data are passed through, as is, from source to destination. For
packet switching, analog data must be converted to digital before transmission; in
addition, each packet includes overhead bits, such as the destination address.

## Slide 31: Asynchronous Transfer Mode (ATM)
A switching and multiplexing technology that employs small, fixed-length packets called cells
A fixed-size packet ensures function could be carried out efficiently, with little delay variation
Small cell size supports delay-intolerant interactive voice service with a small packetization delay
Designed to provide the performance of a circuit-switching network and the flexibility and efficiency of a packet-switching network
Standardization effort was to provide a powerful set of tools for supporting a rich QoS capability and a powerful traffic management capability
Notes: Asynchronous transfer mode is a switching and multiplexing technology that
employs small, fixed-length packets called cells . A fixed-size packet was chosen
to ensure that the switching and multiplexing function could be carried out efficiently,
with little delay variation. A small cell size was chosen primarily to support
delay-intolerant interactive voice service with a small packetization delay. ATM is a
connection-oriented packet-switching technology that was designed to provide the
performance of a circuit-switching network and the flexibility and efficiency of a
packet-switching network. A major thrust of the ATM standardization effort was to
provide a powerful set of tools for supporting a rich QoS capability and a powerful
traffic management capability. ATM was intended to provide a unified networking
standard for both circuit-switched and packet-switched traffic, and to support data,
voice, and video with appropriate QoS mechanisms. With ATM, the user can select
the desired level of service and obtain guaranteed service quality. Internally, the
ATM network makes reservations and preplans routes so that transmission allocation
is based on priority and QoS characteristics.

## Slide 32: ATM
Commonly used by telecommunications providers to implement wide area networks
Used by many DSL implementations
Used as a backbone network technology in numerous IP networks
Multiprotocol Label Switching (MPLS) has reduced the role for ATM
Notes: ATM was intended to be a universal networking technology, with much of the
switching and routing capability implemented in hardware, and with the ability to
support IP-based networks and circuit-switched networks. It was also anticipated
that ATM would be used to implement local area networks. ATM never achieved
this comprehensive deployment. However, ATM remains an important technology.
ATM is commonly used by telecommunications providers to implement wide area
networks. Many DSL implementations use ATM over the basic DSL hardware for
multiplexing and switching, and ATM is used as a backbone network technology in
numerous IP networks and portions of the Internet.
A number of factors have led to this lesser role for ATM. IP, with its many
associated protocols, provides an integrative technology that is more scalable and
less complex than ATM. In addition, the need to use small fixed-sized cells to
reduce jitter has disappeared as transport speeds have increased. The development
of voice and video over IP protocols has provided an integration capability
at the IP level.
Perhaps the most significant development related to the reduced role for ATM
is the widespread acceptance of Multiprotocol Label Switching (MPLS). MPLS is
a layer-2 connection-oriented packet-switching protocol that, as the name suggests,
can provide a switching service for a variety of protocols and applications, including
IP, voice, and video. We introduce MPLS in Chapter 23.

## Slide 33: Virtual Channel Connection (VCC)
Logical connection in ATM
Analogous to a virtual circuit
Basic unit of switching in an ATM network
Set up between two end users through the network, and a variable-rate, full duplex flow of fixed-size cells is exchanged over the connection
Also used for user-network exchange and network-network exchange
Notes: ATM is a packet-oriented transfer mode. It allows multiple logical connections to
be multiplexed over a single physical interface. The information flow on each logical
connection is organized into fixed-size packets called cells. Logical connections
in ATM are referred to as virtual channel connections (VCCs) . A VCC is analogous
to a virtual circuit; it is the basic unit of switching in an ATM network. A VCC is
set up between two end users through the network, and a variable-rate, full-duplex
flow of fixed-size cells is exchanged over the connection. VCCs are also used for
user–network exchange (control signaling) and network–network exchange (network
management and routing).
For ATM, a second sublayer of processing has been introduced that deals
with the concept of virtual path (Figure 9.16). A virtual path connection (VPC) is a
bundle of VCCs that have the same endpoints. Thus, all of the cells flowing over alof the VCCs in a single VPC are switched together.
The virtual path concept was developed in response to a trend in high-speed
networking in which the control cost of the network is becoming an increasingly
higher proportion of the overall network cost. The virtual path technique helps contain
the control cost by grouping connections sharing common paths through the
network into a single unit. Network management actions can then be applied to
a small number of groups of connections instead of a large number of individual
connections.
Several advantages can be listed for the use of virtual paths:
• Simplified network architecture: Network transport functions can be separated
into those related to an individual logical connection (virtual channel)
and those related to a group of logical connections (virtual path).
• Increased network performance and reliability: The network deals with fewer,
aggregated entities.
• Reduced processing and short connection setup time: Much of the work is
done when the virtual path is set up. By reserving capacity on a virtual path
connection in anticipation of later call arrivals, new virtual channel connections
can be established by executing simple control functions at the endpoints
For ATM, a second sublayer of processing has been introduced that deals
with the concept of virtual path (Figure 9.16). A virtual path connection (VPC) is a
bundle
of VCCs that have the same endpoints. Thus, all of the cells flowing over all
of the VCCs in a single VPC are switched together.
The virtual path concept was developed in response to a trend in high-speed
networking in which the control cost of the network is becoming an increasingly
higher proportion of the overall network cost. The virtual path technique helps contain
the control cost by grouping connections sharing common paths through the
network into a single unit. Network management actions can then be applied to
a small number of groups of connections instead of a large number of individual
connections.

## Slide 34
Notes: For ATM, a second sublayer of processing has been introduced that deals
with the concept of virtual path (Figure 9.16). A virtual path connection (VPC) is a
bundle of VCCs that have the same endpoints. Thus, all of the cells flowing over all
of the VCCs in a single VPC are switched together.
The virtual path concept was developed in response to a trend in high-speed
networking in which the control cost of the network is becoming an increasingly
higher proportion of the overall network cost. The virtual path technique helps contain
the control cost by grouping connections sharing common paths through the
network into a single unit. Network management actions can then be applied to
a small number of groups of connections instead of a large number of individual
connections.

## Slide 35: Virtual Path Advantages
Simplified network architecture
Network transport functions can be separated into those related to an individual logical connection and those related to a group of logical connections
Increased network performance and reliability
The network deals with fewer, aggregated entities
Reduced processing and short connection setup time
By reserving capacity on a virtual path connection, new virtual channel connections can be established by executing simple control functions at the endpoints of the virtual path connection
Enhanced network services
The virtual path is used internal to the network but is also visible to the end user; the user may define closed user groups or closed networks of virtual channel bundles
Notes: Several advantages can be listed for the use of virtual paths:
• Simplified network architecture: Network transport functions can be separated
into those related to an individual logical connection (virtual channel)
and those related to a group of logical connections (virtual path).
• Increased network performance and reliability: The network deals with fewer,
aggregated entities.
• Reduced processing and short connection setup time: Much of the work is
done when the virtual path is set up. By reserving capacity on a virtual path
connection in anticipation of later call arrivals, new virtual channel connections
can be established by executing simple control functions at the endpoints
of the virtual path connection; no call processing is required at transit nodes.
Thus, the addition of new virtual channels to an existing virtual path involves
minimal processing.
• Enhanced network services: The virtual path is used internal to the network
but is also visible to the end user. Thus, the user may define closed user groups
or closed networks of virtual channel bundles.

## Slide 36: Virtual Channel Characteristics
ITU-T Recommendation I.150 lists the following characteristics of VCCs:
Quality of service (QoS)
Specified by parameters such as cell loss ratio and cell delay variation
Switched and semipermanent VCCs
A switched VCC is an on-demand connection which requires a call control signaling for setup and tearing down
A semipermanent VCC is one that is of long duration and is set up by configuration or network management action
Cell sequence integrity
The sequence of transmitted cells within a VCC is preserved
Traffic parameter negotiation and usage monitoring
Traffic parameters can be negotiated between a user and the network for each VCC
The network monitors the input of cells to ensure that the negotiated parameters are not violated
Notes: ITU-T Recommendation I.150 lists the following as characteristics of virtual channel connections:
• Quality of service (QoS): A user of a VCC is provided with a QoS specified by
parameters such as cell loss ratio (ratio of cells lost to cells transmitted) and
cell delay variation.
• Switched and semipermanent virtual channel connections: A switched VCC
is an on-demand connection, which requires a call control signaling for setup
and tearing down. A semipermanent VCC is one that is of long duration and is
set up by configuration or network management action.
• Cell sequence integrity: The sequence of transmitted cells within a VCC is
preserved.
• Traffic parameter negotiation and usage monitoring: Traffic parameters can
be negotiated between a user and the network for each VCC. The network
monitors the input of cells to the VCC to ensure that the negotiated parameters
are not violated.
The types of traffic parameters that can be negotiated include average rate,
peak rate, burstiness, and peak duration. The network may need a number of strategies
to deal with congestion and to manage existing and requested VCCs. At the
crudest level, the network may simply deny new requests for VCCs to prevent congestion.
Additionally, cells may be discarded if negotiated parameters are violated
or if congestion becomes severe. In an extreme situation, existing connections might
be terminated.

## Slide 37: Virtual Path Characteristics
Quality of service (QoS)
Specified by parameters such as cell loss ratio and cell delay variation
Switched and semipermanent VPCs
A switched VPC is an on-demand connection which requires a call control signaling for setup and tearing down
A semipermanent VPC is one that is of long duration and is set up by configuration or network management action
Cell sequence integrity
The sequence of transmitted cells within a VPC is preserved
Traffic parameter negotiation and usage monitoring
Traffic parameters can be negotiated between a user and the network for each VPC
The network monitors the input of cells to ensure that the negotiated parameters are not violated
Virtual channel identifier restriction within a VPC
One or more virtual channel identifiers, or numbers, may not be available to the user of the VPC but may be reserved for network use
ITU-T Recommendation I.150 lists the following characteristics of VPCs:
Notes: I.150 also lists characteristics of VPCs. The first four characteristics listed are
identical to those for VCCs. That is, QoS; switched and semipermanentVPCs; cell
sequence integrity; and traffic parameter negotiation and usage monitoring are
all also characteristics of a VPC. There are a number of reasons for this duplication.
First, this provides some flexibility in how the network service manages the
requirements placed upon it. Second, the network must be concerned with the
overall requirements for a VPC, and within a VPC may negotiate the establishment
of virtual channels with given characteristics. Finally, once a VPC is set up, it is
possible for the end users to negotiate the creation of new VCCs. The VPC characteristics
impose a discipline on the choices that the end users may make.
In addition, a fifth characteristic is listed for VPCs:
• Virtual channel identifier restriction within a VPC: One or more virtual channel
identifiers, or numbers, may not be available to the user of the VPC but
may be reserved for network use. Examples include VCCs used for network
management.

## Slide 38: Control Signaling
VCCs
Semi-permanent VCCs may be used for user-to-user exchange
  No control signaling is required
If there is no preestablished call control signaling channel, then one must be set up
  Meta-signaling channel
The meta-signaling channel can be used to set up a VCC between the user and the network for call control signaling
  User-to-network signaling virtual channel
The meta-signaling channel can also be used to set up a user-to-user signaling virtual channel
  Such a channel must be set up within a preestablished VPC
VPCs
Can be established on a semi-permanent basis by prior agreement
  No control signaling is required
VPC establishment/release may be customer controlled
  The customer uses a signaling VCC to request the VPC from the network
VPC establishment/release may be network controlled
  The network establishes a VPC for its own convenience
  The path may be network-to-network, user-to-network, or user-to-user
Notes: In ATM, a mechanism is needed for the establishment and
release of VPCs and VCCs. The exchange of information involved in this process is
referred to as control signaling and takes place on separate connections from those
that are being managed.
For VCCs, I.150 specifies four methods for providing an establishment/release
facility. One or a combination of these methods will be used in any particular network:
1. SemipermanentVCCs may be used for user-to-user exchange. In this case, no
control signaling is required.
2. If there is no preestablished call control signaling channel, then one must
be set up. For that purpose, a control signaling exchange must take place
between the user and the network on some channel. Hence we need a permanent
channel, probably of low data rate, that can be used to set up VCCs that
can be used for call control. Such a channel is called a meta-signaling channel ,
as the channel is used to set up signaling channels.
3. The meta-signaling channel can be used to set up a VCC between the user and
the network for call control signaling. This user-to-network signaling virtual
channel can then be used to set up VCCs to carry user data.
4. The meta-signaling channel can also be used to set up a user-to-user signaling
virtual channel . Such a channel must be set up within a preestablished VPC. It
can then be used to allow the two end users, without network intervention, to
establish and release user-to-user VCCs to carry user data.
For VPCs, three methods are defined in I.150:
1. A VPC can be established on a semipermanent basis by prior agreement. In
this case, no control signaling is required.
VPC establishment/release may be customer controlled . In this case, the customer
uses a signaling VCC to request the VPC from the network.
VPC establishment/release may be network controlled . In this case, the
network establishes a VPC for its own convenience. The path may be network-
to-network, user-to-network, or user-to-user.

## Slide 39
Notes: ATM makes use of fixed-size cells, consisting of a 5-octet header and a 48-octet
information field. There are several advantages to the use of small, fixed-size cells.
First, the use of small cells may reduce queuing delay for a high-priority cell, because
it waits less if it arrives slightly behind a lower-priority cell that has gained access
to a resource (e.g., the transmitter). Second, fixed-size cells can be switched more
efficiently, which is important for the very high data rates of ATM. With fixed-size
cells, it is easier to implement the switching mechanism in hardware.
Figure 9.17a shows the cell header format at the user–network interface.
Figure 9.17b shows the cell header format internal to the network.
The Generic Flow Control (GFC) field does not appear in the cell header
internal to the network, but only at the user–network interface. Hence, it can be
used for control of cell flow only at the local user–network interface. The field could
be used to assist the customer in controlling the flow of traffic for different qualities
of service. In any case, the GFC mechanism is used to alleviate short-term overload
conditions in the network.
The virtual path identifier (VPI) constitutes a routing field for the network.
It is 8 bits at the user–network interface and 12 bits at the network–network interface.
The latter allows support for an expanded number of VPCs internal to the
network, to include those supporting subscribers and those required for network
management. The virtual channel identifier (VCI) is used for routing to and from
the end user.
The Payload Type (PT) field indicates the type of information in the information
field. A value of 0 in the first bit indicates user information (i.e., information from the next higher layer). In this
case, the second bit indicates whether congestion has been experienced; the third
bit, known as the Service Data Unit (SDU) type bit, is a one-bit field that can be
used to discriminate two types of ATM SDUs associated with a connection. The
term SDU refers to the 48-octet payload of the cell. A value of 1 in the first bit of
the Payload Type field indicates that this cell carries network management or maintenance
information. This indication allows the insertion of network-management
cells onto a user’s VCC without impacting the user’s data. Thus, the PT field can
provide inband control information.
The Cell Loss Priority (CLP) bit is used to provide guidance to the network
in the event of congestion. A value of 0 indicates a cell of relatively higher priority,
which should not be discarded unless no other alternative is available. A value
of 1 indicates that this cell is subject to discard within the network. The user might
employ this field so that extra cells (beyond the negotiated rate) may be inserted
into the network, with a CLP of 1, and delivered to the destination if the network
is not congested. The network may set this field to 1 for any data cell that is in
violation of an agreement concerning traffic parameters between the user and the
network. In this case, the switch that does the setting realizes that the cell exceeds
the agreed traffic parameters but that the switch is capable of handling the cell. At
a later point in the network, if congestion is encountered, this cell has been marked
for discard in preference to cells that fall within agreed traffic limits.
The Header Error Control (HEC) field is an 8-bit error code that can be used
to correct single-bit errors in the header and to detect double-bit errors. In the case
of most existing data link layer protocols, such as LAPD and HDLC, the data field
that serves as input to the error code calculation is in general much longer than the
size of the resulting error code. This allows for error detection. In the case of ATM,
there is also sufficient redundancy in the code to recover from certain error patterns.

## Slide 40
SDU = Service Data Unit
OAM = Operations, Administration, and Maintenance
Table 9.2
Payload Type (PT) Field Coding
Notes: Table 9.2 shows the interpretation of the PT bits.

## Slide 41: Summary
Switched communications networks
Circuit-switching networks
Circuit-switching concepts
  Space division switching
  Time-division switching
Softswitch architecture
Packet-switching principles
  Switching technique
  Packet size
  External network interface
  Comparison of circuit switching and packet switching
Asynchronous transfer mode
  ATM logical connections
  ATM cells
Notes: Chapter 9 summary.