## Slide 1: Data and Computer Communications
Tenth Edition
by William Stallings
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 13 “Wireless LANs”.

## Slide 2: Wireless LANs
Chapter 13
Notes: This chapter provides a survey of WLANs. We begin with an overview
that looks at the motivations for using WLANs and summarize the various
approaches in current use. The next section examines the three principal types
of wireless WLANs, classified according to transmission technology: infrared,
spread spectrum, and narrowband microwave.
The most prominent specification for WLANs was developed by the
IEEE 802.11 working group. This chapter focuses on this standard, and is
based on the 2012 version.

## Slide 3
Investigators have published numerous reports of birds taking turns vocalizing; the bird spoken to gave its full attention to the speaker and never vocalized at the same time, as if the two were holding a conversation.
Researchers and scholars who have studied the data on avian communication carefully write the (a) the communication code of birds such has crows has not been broken by any means; (b) probably all birds have wider vocabularies than anyone realizes; and (c) greater complexity and depth are recognized in avian communication as research progresses.
—The Human Nature of Birds,
Theodore Barber
Notes: In recent years, wireless LANs (WLANs) have come to occupy a significant
niche in the local area network market. Increasingly, organizations are finding
that WLANs are an indispensable adjunct to traditional wired LANs, to
satisfy requirements for mobility, relocation, ad hoc networking, and coverage
of locations difficult to wire.

## Slide 4
Notes: Figure 13.1 indicates a simple WLAN configuration that is typical of many environments.
There is a backbone wired LAN, such as Ethernet, that supports servers,
workstations, and one or more bridges or routers to link with other networks. In
addition, there is a control module (CM) that acts as an interface to a WLAN. The
control module includes either bridge or router functionality to link the WLAN
to the backbone. It includes some sort of access control logic, such as a polling or
token-passing scheme, to regulate the access from the end systems. Note that some
of the end systems are stand-alone devices, such as a workstation or a server. Hubs
or other user modules (UMs) that control a number of stations off a wired LAN
may also be part of the WLAN configuration.

## Slide 5
Notes: The configuration of Figure 13.1 can be referred to as a single-cell WLAN; all
of the wireless end systems are within range of a single control module. Another
common configuration, suggested by Figure 13.2, is a multiple-cell WLAN. In this
case, there are multiple control modules interconnected by a wired LAN. Each
control module supports a number of wireless end systems within its transmission
range. For example, with an infrared LAN, transmission is limited to a single
room; therefore, one cell is needed for each room in an office building that requires
wireless support.

## Slide 6
Notes: Figure 13.3 illustrates a different type of configuration, referred to as an
ad hoc network , from that shown in Figures 13.1 and 13.2. Typically, the WLAN
forms a stationary infrastructure consisting of one or more cells with a control
module for each cell. Within a cell, there may be a number of stationary end
systems. Nomadic stations can move from one cell to another. By contrast, there
is no infrastructure for an ad hoc network. Rather, a peer collection of stations
within a range of each other may dynamically configure themselves into a
temporary network.

## Slide 7: Wireless LAN Requirements
Throughput
Number of nodes
Connection to backbone LAN
Service area
Battery power consumption
Transmission robustness and security
Collocated network operation
License-free operation
Handoff/roaming
Dynamic configuration
Notes: A WLAN must meet the same sort of requirements typical of any LAN, including
high capacity, ability to cover short distances, full connectivity among attached
stations, and broadcast capability. In addition, there are a number of requirements
specific to the WLAN environment. The following are among the most important
requirements for WLANs:
• Throughput: The medium access control (MAC) protocol should make as efficient
use as possible of the wireless medium to maximize capacity.
• Number of nodes: WLANs may need to support hundreds of nodes across
multiple cells.
• Connection to backbone LAN: In most cases, interconnection with stations on
a wired backbone LAN is required. For infrastructure WLANs, this is easily
accomplished through the use of control modules that connect to both types of
LANs. There may also need to be accommodation for mobile users and ad hoc
wireless networks.
• Service area: A typical coverage area for a WLAN has a diameter of 100 to
300 m.
• Battery power consumption: Mobile workers use battery-powered workstations
that need to have a long battery life when used with wireless adapters.
This suggests that a MAC protocol that requires mobile nodes to monitor
access points constantly or engage in frequent handshakes with a base
station is inappropriate. Typical WLAN implementations have features
to reduce power consumption while not using the network, such as a
sleep mode.
• Transmission robustness and security: Unless properly designed, a WLAN
may be especially vulnerable to interference and network eavesdropping.
The design of a WLAN must permit reliable transmission even in a
noisy environment and should provide some level of security from
eavesdropping.
• Collocated network operation: As WLANs become more popular, it is quite
likely for two or more WLANs to operate in the same area or in some area
where interference between the LANs is possible. Such interference may
thwart the normal operation of a MAC algorithm and may allow unauthorized
access to a particular LAN.
• License-free operation: Users would prefer to buy and operate WLAN products
without having to secure a license for the frequency band used by the
LAN.
• Handoff/roaming: The MAC protocol used in the WLAN should enable
mobile stations to move from one cell to another.
• Dynamic configuration: The MAC addressing and network management
aspects of the WLAN should permit dynamic and automated addition, deletion,
and relocation of end systems without disruption to other users.

## Slide 8: Table 13.1 Key IEEE 802.11 Standards
(Table can be found on page 424 in the textbook)
Notes: In 1990, the IEEE 802 committee formed a new working group, IEEE 802.11, specifically
devoted to WLANs, with a charter to develop a MAC protocol and physical
medium specification. Since that time, the demand for WLANs, at different frequencies
and data rates, has exploded. Keeping pace with this demand, the IEEE 802.11
working group has issued an ever-expanding list of standards (Table 13.1).

## Slide 9: Table 13.2 IEEE 802.11 Terminology
(Table can be found on page 424 in the textbook)
Notes: Table 13.2 briefly defines key terms used in the IEEE 802.11 standard.

## Slide 10: Wi-Fi Alliance
There is always a concern whether products from different vendors will successfully interoperate
Wireless Ethernet Compatibility Alliance (WECA)
  Industry consortium formed in 1999
Renamed the Wi-Fi (Wireless Fidelity) Alliance
  Created a test suite to certify interoperability for 802.11 products
Notes: Although 802.11 products are all based on the same standards, there is always a
concern whether products from different vendors will successfully interoperate.
To meet this concern, the Wireless Ethernet Compatibility Alliance (WECA), an
industry consortium, was formed in 1999. This organization, subsequently renamed
the Wi-Fi (Wireless Fidelity) Alliance, created a test suite to certify interoperability
for 802.11 products.

## Slide 11
Notes: Figure 13.4 illustrates the model developed by the 802.11 working group. The
smallest building block of a WLAN is a basic service set (BSS) , which consists
of some number of stations executing the same MAC protocol and competing
for access to the same shared wireless medium. A BSS may be isolated or it may
connect to a backbone distribution system (DS) through an access point (AP) .
The AP functions as a bridge and a relay point. In a BSS, client stations do not
communicate directly with one another. Rather, if one station in the BSS wants to
communicate with another station in the same BSS, the MAC frame is first sent
from the originating station to the AP, and then from the AP to the destination
station. Similarly, a MAC frame from a station in the BSS to a remote station is
sent from the local station to the AP and then relayed by the AP over the DS
on its way to the destination station. The BSS generally corresponds to what is
referred to as a cell in the literature. The DS can be a switch, a wired network, or
a wireless network.
When all the stations in the BSS are mobile stations, with no connection to
other BSSs, the BSS is called an independent BSS (IBSS) . An IBSS is typically an
ad hoc network. In an IBSS, the stations all communicate directly, and no AP is
involved.
A simple configuration is shown in Figure 13.4, in which each station belongs
to a single BSS; that is, each station is within wireless range only of other stations
within the same BSS. It is also possible for two BSSs to overlap geographically, so
that a single station could participate in more than one BSS. Further, the association
between a station and a BSS is dynamic. Stations may turn off, come within range,
and go out of range.
An extended service set (ESS) consists of two or more BSSs interconnected by
a distribution system. Typically, the distribution system is a wired backbone LAN
but can be any communications network. The ESS appears as a single logical LAN
to the logical link control (LLC) level.
Figure 13.4 indicates that an AP is implemented as part of a station; the AP
is the logic within a station that provides access to the DS by providing DS services
in addition to acting as a station. To integrate the IEEE 802.11 architecture
with a traditional wired LAN, a portal is used. The portal logic is implemented
in a device, such as a bridge or router, that is part of the wired LAN and that is
attached to the DS.

## Slide 12: Table 13.3 IEEE 802.11 Services
Notes: IEEE 802.11 defines a number of services that need to be provided by the WLAN to
provide functionality equivalent to that which is inherent to wired LANs. Table 13.3
lists key services and indicates two ways of categorizing them.
1. The service provider can be either the station or the DS. Station services are
implemented in every 802.11 station, including AP stations. Distribution
services are provided between BSSs; these services may be implemented
in an AP or in another special-purpose device attached to the distribution
System.
2. Three of the services are used to control IEEE 802.11 LAN access and confidentiality.
Six of the services are used to support delivery of MAC service
data units (MSDUs) between stations. The MSDU is a block of data passed
down from the MAC user to the MAC layer; typically this is a LLC PDU. If
the MSDU is too large to be transmitted in a single MAC frame, it may be
fragmented and transmitted in a series of MAC frames.

## Slide 13: Distribution of Messages Within a DS
Integration service
Distribution service
Primary service used by stations to exchange MAC frames when frame must traverse the DS to get from a station in one BSS to a station in another BSS
If stations are in the same BSS, distribution service logically goes through the single AP of that BSS
Enables transfer of data between a station on an IEEE 802.11 LAN and a station on an integrated IEEE 802.x LAN
Takes care of any address translation and media conversion logic required for the exchange of data
Notes: The two services involved with the distribution
of messages within a DS are distribution and integration. Distribution is
the primary service used by stations to exchange MAC frames when the frame must
traverse the DS to get from a station in one BSS to a station in another BSS. For
example, suppose a frame is to be sent from station 2 (STA2) to STA7 in Figure 13.4.
The frame is sent from STA2 to STA1, which is the AP for this BSS. The AP gives
the frame to the DS, which has the job of directing the frame to the AP associated
with STA5 in the target BSS. STA5 receives the frame and forwards it to STA7. How
the message is transported through the DS is beyond the scope of the IEEE 802.11
standard.
If the two stations that are communicating are within the same BSS, then the
distribution service logically goes through the single AP of that BSS.
The integration service enables transfer of data between a station on an IEEE
802.11 LAN and a station on an integrated IEEE 802.x LAN. The term integrated
refers to a wired LAN that is physically connected to the DS and whose stations
may be logically connected to an IEEE 802.11 LAN via the integration service. The
integration service takes care of any address translation and media conversion logic
required for the exchange of data.

## Slide 14: Association-Related Services
DS requires information about stations within the ESS that is provided by the association-related services
Station must be associated before DS can deliver data to or accept data from it
3 mobility transition types:
No transition stationary or in single BSS
BSS transition between BSS in same ESS
ESS transition between BSS in different ESS
Notes: The primary purpose of the MAC layer is to
transfer MSDUs between MAC entities; this purpose is fulfilled by the distribution
service. For that service to function, it requires information about stations
within the ESS that is provided by the association-related services. Before the
distribution service can deliver data to or accept data from a station, that station
must be associated . Before looking at the concept of association, we need
to describe the concept of mobility. The standard defines three transition types,
based on mobility:
• No transition: A station of this type is either stationary or moves only within
the direct communication range of the communicating stations of a single BSS.
• BSS transition: This is defined as a station movement from one BSS to another
BSS within the same ESS. In this case, delivery of data to the station requires that
the addressing capability be able to recognize the new location of the station.
• ESS transition: This is defined as a station movement from a BSS in one ESS
to a BSS within another ESS. This case is supported only in the sense that
the station can move. Maintenance of upper-layer connections supported by
802.11 cannot be guaranteed. In fact, disruption of service is likely to occur.

## Slide 15: Association Related Services
DS needs to know the identity of the AP to which the message should be delivered
  Stations must maintain association with AP within current BSS
3 services relate to this requirement:
Association - establishes initial association between station and AP
Reassociation – enables an established association to be transferred from one AP to another
Disassociation – a notification from either a station or an AP that an existing association is terminated
Notes: To deliver a message within a DS, the distribution service needs to know
where the destination station is located. Specifically, the DS needs to know the
identity of the AP to which the message should be delivered in order for that message
to reach the destination station. To meet this requirement, a station must
maintain an association with the AP within its current BSS. Three services relate
to this requirement:
• Association: Establishes an initial association between a station and an AP.
Before a station can transmit or receive frames on a WLAN, its identity and
address must be known. For this purpose, a station must establish an association
with an AP within a particular BSS. The AP can then communicate this
information to other APs within the ESS to facilitate routing and delivery of
addressed frames.
• Reassociation: Enables an established association to be transferred from one
AP to another, allowing a mobile station to move from one BSS to another.
• Disassociation: A notification from either a station or an AP that an existing
association is terminated. A station should give this notification before leaving
an ESS or shutting down. However, the MAC management facility protects
itself against stations that disappear without notification.

## Slide 16: Medium Access Control
MAC layer covers three functional areas:
Reliable data delivery
Access control
Security
Notes: The IEEE 802.11 MAC layer covers three functional areas: reliable data delivery, access control, and security. This section covers the first two topics.

## Slide 17: Reliable Data Delivery
Can be dealt with at a higher layer
More efficient to deal with errors at MAC level
802.11 includes frame exchange protocol
  Station receiving frame returns acknowledgment (ACK) frame
  Exchange treated as atomic unit
  If no ACK within short period of time, retransmit
802.11 physical and MAC layers unreliable
  Noise, interference, and other propagation effects result in loss of frames
  Even with error-correction codes, frames may not successfully be received
Notes: As with any wireless network, a wireless LAN using the IEEE 802.11 physical and MAC layers is subject to considerable unreliability. Noise, interference, and other propagation effects result in the loss of a significant number of frames. Even with error correction codes, a number of MAC frames may not successfully be received. This situation can be dealt with by reliability mechanisms at a higher layer, such as TCP. However, timers used for retransmission at higher layers are typically on the order of seconds. It is therefore more efficient to deal with errors at the MAC level. For this purpose, IEEE 802.11 includes a frame exchange protocol. When a station receives a data frame from another station, it returns an acknowledgment (ACK) frame to the source station. This exchange is treated as an atomic unit, not to be interrupted by a transmission from any other station. If the source does not receive an ACK within a short period of time, either because its data frame was damaged or because the returning ACK was damaged, the source retransmits the frame.

## Slide 18: Four Frame Exchange
RTS alerts all stations within range of source that exchange is under way
CTS alerts all stations within range of destination
Other stations don’t transmit to avoid collision
RTS/CTS exchange is a required function of MAC but may be disabled
Can use four-frame exchange for better reliability
Source issues a Request to Send (RTS) frame
Destination responds with Clear to Send (CTS)
After receiving CTS, source transmits data
Destination responds with ACK
Notes: Thus, the basic data transfer mechanism in IEEE 802.11 involves an exchange of two frames. To further enhance reliability, a four-frame exchange may be used. In this scheme, a source first issues a Request to Send (RTS) frame to the destination. The destination then responds with a Clear to Send (CTS). After receiving the CTS, the source transmits the data frame, and the destination responds with an ACK. The RTS alerts all stations that are within reception range of the source that an exchange is under way; these stations refrain from transmission in order to avoid a collision between two frames transmitted at the same time. Similarly, the CTS alerts all stations that are within reception range of the destination that an exchange is under way. The RTS/CTS portion of the exchange is a required function of the MAC but may be disabled.

## Slide 19
Notes: The 802.11 working group considered two types of proposals for a MAC algorithm:
distributed access protocols, which, like Ethernet, distribute the decision
to transmit over all the nodes using a carrier sense mechanism; and centralized
access protocols, which involve regulation of transmission by a centralized decision
maker. A distributed access protocol makes sense for an ad hoc network of
peer workstations (typically an IBSS) and may also be attractive in other WLAN
configurations that consist primarily of bursty traffic. A centralized access
protocol is natural for configurations in which a number of wireless stations are
interconnected with each other and some sort of base station that attaches to a
backbone wired LAN; it is especially useful if some of the data is time sensitive
or high priority.
The end result for 802.11 is a MAC algorithm called DFWMAC (distributed
foundation wireless MAC) that provides a distributed access control mechanism
with an optional centralized control built on top of that. Figure 13.5 illustrates the
architecture. The lower sublayer of the MAC layer is the distributed coordination
function (DCF). DCF uses a contention algorithm to provide access to all traffic.
Ordinary asynchronous traffic directly uses DCF. The point coordination function
(PCF) is a centralized MAC algorithm used to provide contention-free service. PCF
is built on top of DCF and exploits features of DCF to assure access for its users.

## Slide 20: Distributed Coordination Function (DCF)
DCF sublayer uses CSMA algorithm
Does not include a collision detection function because it is not practical on a wireless network
Includes a set of delays that amounts as a priority scheme
If station has frame to send it listens to medium
If medium is idle, station may transmit
Else waits until current transmission is complete
Notes: The DCF sublayer makes use of a simple CSMA (carrier sense multiple access) algorithm. If a station has a MAC frame to transmit, it listens to the medium. If the medium is idle, the station may transmit; otherwise the station must wait until the current transmission is complete before transmitting. The DCF does not include a collision detection function (i.e., CSMA/CD) because collision detection is not practical on a wireless network. The dynamic range of the signals on the medium is very large, so that a transmitting station cannot effectively distinguish incoming weak signals from noise and the effects of its own transmission.
To ensure the smooth and fair functioning of this algorithm, DCF includes a set of delays that amounts to a priority scheme. Let us start by considering a single delay known as an interframe space (IFS). In fact, there are three different IFS values, but the algorithm is best explained by initially ignoring this detail.

## Slide 21
Notes: Using an IFS, the rules for CSMA access are as follows (Figure 13.6):
A station with a frame to transmit senses the medium. If the medium is idle, it waits to see if the medium remains idle for a time equal to IFS. If so, the station may transmit immediately.
2. If the medium is busy (either because the station initially finds the medium busy or because the medium becomes busy during the IFS idle time), the station defers transmission and continues to monitor the medium until the current transmission is over
3. Once the current transmission is over, the station delays another IFS. If the medium remains idle for this period, then the station backs off a random amount of time and again senses the medium. If the medium is still idle, the station may transmit. During the backoff time, if the medium becomes busy, the backoff timer is halted and resumes when the medium becomes idle.
4.If the transmission is unsuccessful, which is determined by the absence of an acknowledgement, then it is assumed that a collision has occurred.
To ensure that backoff maintains stability, binary exponential backoff, described in Chapter 12, is used. Binary exponential backoff provides a means of handling a heavy load. Repeated failed attempts to transmit result in longer and longer backoff times, which helps to smooth out the load. Without such a backoff, the following situation could occur: Two or more stations attempt to transmit at the same time, causing a collision. These stations then immediately attempt to retransmit, causing a new collision.

## Slide 22: Priority IFS Values
SIFS
(short IFS)
For all immediate response actions
PIFS
(point coordination function IFS)
Used by the centralized controller in PCF scheme when issuing polls
DIFS
(distributed coordination function IFS)
Used as minimum delay for asynchronous frames contending for access
Notes: The preceding scheme is refined for DCF to provide priority-based access by the simple expedient of using three values for IFS:
SIFS (short IFS): The shortest IFS, used for all immediate response actions, as explained in the following discussion
PIFS (point coordination function IFS): A midlength IFS, used by the centralized controller in the PCF scheme when issuing polls
DIFS (distributed coordination function IFS): The longest IFS, used as a minimum delay for asynchronous frames contending for access

## Slide 23
Notes: Figure 13.7a illustrates the use of these time values.

## Slide 24: SIFS
Any station using SIFS to determine transmission opportunity has the highest priority
Used in the following circumstances:
  Acknowledgment (ACK)
    Station responds with an ACK frame after waiting only for a SIFS gap
    Provides for efficient collision recovery
  Clear to Send (CTS)
    Station ensures data frame gets through by issuing RTS
  Poll response
Notes: Consider first the SIFS. Any station using SIFS to determine transmission opportunity has, in effect, the
highest priority, because it will always gain access in preference to a station waiting
an amount of time equal to PIFS or DIFS. The SIFS is used in the following
circumstances:
• Acknowledgment (ACK): When a station receives a frame addressed only
to itself (not multicast or broadcast), it responds with an ACK frame after
waiting only for an SIFS gap. This has two desirable effects. First, because
collision detection is not used, the likelihood of collisions is greater than with
CSMA/CD, and the MAC-level ACK provides for efficient collision recovery.
Second, the SIFS can be used to provide efficient delivery of an LLC protocol
data unit (PDU) that requires multiple MAC frames. In this case, the
following scenario occurs. A station with a multiframe LLC PDU to transmit
sends out the MAC frames one at a time. Each frame is acknowledged by the
recipient after SIFS. When the source receives an ACK, it immediately (after
SIFS) sends the next frame in the sequence. The result is that once a station
has contended for the channel, it will maintain control of the channel until it
has sent all of the fragments of an LLC PDU.
• Clear to Send (CTS): A station can ensure that its data frame will get through
by first issuing a small RTS frame. The station to which this frame is addressed
should immediately respond with a CTS frame if it is ready to receive. All
other stations receive the RTS and defer using the medium.
• Poll response: This is explained in the following discussion of PCF.
The next longest IFS interval is the PIFS. This is used by the centralized
controller in issuing polls and takes precedence over normal contention traffic.
However, those frames transmitted using SIFS have precedence over a PCF poll.
Finally, the DIFS interval is used for all ordinary asynchronous traffic.

## Slide 25: Point Coordination Function (PCF)
Alternative access method implemented on top of DCF
Polling by centralized polling master (point coordinator)
Uses PIFS when issuing polls
Point coordinator polls in round-robin to stations configured for polling
When poll issued, polled station may respond using SIFS
If point coordinator receives response, it issues another poll using PIFS
If no response during expected turnaround time, coordinator issues poll
Coordinator could lock out asynchronous traffic by issuing polls
Have a superframe interval defined
Notes: PCF is an alternative access method implemented on top of the DCF. The operation consists of polling by the centralized polling master (point coordinator). The point coordinator makes use of PIFS when issuing polls. Because PIFS is smaller than DIFS, the point coordinator can seize the medium and lock out all asynchronous traffic while it issues polls and receives responses.
As an extreme, consider the following possible scenario. A wireless network is configured so that a number of stations with time-sensitive traffic are controlled by the point coordinator while remaining traffic contends for access using CSMA. The point coordinator could issue polls in a round-robin fashion to all stations configured for polling. When a poll is issued, the polled station may respond using SIFS. If the point coordinator receives a response, it issues another poll using PIFS. If no response is received during the expected turnaround time, the coordinator issues a poll.
If the discipline of the preceding paragraph were implemented, the point coordinator would lock out all asynchronous traffic by repeatedly issuing polls. To prevent this, an interval known as the superframe is defined. During the first part of this interval, the point coordinator issues polls in a round-robin fashion to all stations configured for polling. The point coordinator then idles for the remainder of the superframe, allowing a contention period for asynchronous access.

## Slide 26
Notes: Figure 13.7b illustrates the use of the superframe. At the beginning of a superframe, the point coordinator may optionally seize control and issue polls for a given period of time. This interval varies because of the variable frame size issued by responding stations. The remainder of the superframe is available for contention-based access. At the end of the superframe interval, the point coordinator contends for access to the medium using PIFS. If the medium is idle, the point coordinator gains immediate access and a full superframe period follows. However, the medium may be busy at the end of a superframe. In this case, the point coordinator must wait until the medium is idle to gain access; this results in a foreshortened superframe period for the next cycle.

## Slide 27
Notes: Figure 13.8 shows the format of IEEE 802.11 frame, also known as the MAC protocol
data unit (MPDU). This general format is used for all data and control frames,
but not all fields are used in all contexts. The fields are as follows:
• Frame Control: Indicates the type of frame (control, management, or data)
and provides control information. Control information includes whether the
frame is to or from a DS, fragmentation information, and privacy information.
• Duration/Connection ID: If used as a duration field, indicates the time (in
microseconds) the channel will be allocated for successful transmission of a
MAC frame. In some control frames, this field contains an association, or connection,
identifier.
• Addresses: The number and meaning of the 48-bit address fields depend on
context. The transmitter address and receiver address are the MAC addresses
of stations joined to the BSS that are transmitting and receiving frames over
the WLAN. The service set ID (SSID) identifies the WLAN over which a
frame is transmitted. For an IBSS, the SSID is a random number generated at
the time the network is formed. For a WLAN that is part of a larger configuration,
the SSID identifies the BSS over which the frame is transmitted; specifically,
the SSID is the MAC-level address of the AP for this BSS (Figure 13.4).
Finally the source address and destination address are the MAC addresses of
stations, wireless or otherwise, that are the ultimate source and destination of
this frame. The source address may be identical to the transmitter address and
the destination address may be identical to the receiver address.
• Sequence Control: Contains a 4-bit fragment number subfield, used for fragmentation
and reassembly, and a 12-bit sequence number used to number
frames sent between a given transmitter and receiver.
• QoS Control: Contains information relating to the IEEE 802.11 quality of
service (QoS) facility. A discussion of this facility is beyond our scope.
• High Throughput Control: This field contains control bits related to the operation
of 802.11n, 802.11ac, and 802.11ad. A discussion of this field is beyond
our scope.
• Frame Body: Contains an MSDU or a fragment of an MSDU. The MSDU is a
LLC PDU or MAC control information.
• Frame Check Sequence: A 32-bit cyclic redundancy check.

## Slide 28: Control Frames
Power Save-Poll (PS-Poll)
Request AP transmit buffered frame when in power-saving mode
Request to Send (RTS)
First frame in four-way frame exchange
Clear to Send (CTS)
Second frame in four-way exchange
Acknowledgment (ACK)
Acknowledges correct receipt
Contention-Free (CF)-end
Announces end of contention-free period part of PCF
CF-End + CF-Ack:
Acknowledges CF-end to end contention-free period and release stations from associated restrictions
Notes: Control frames assist in the reliable delivery of data frames.
There are six control frame subtypes:
• Power Save-Poll (PS-Poll): This frame is sent by any station to the station that
includes the AP (access point). Its purpose is to request that the AP transmit
a frame that has been buffered for this station while the station was in powersaving
mode.
• Request to Send (RTS): This is the first frame in the four-way frame exchange
discussed under the subsection on reliable data delivery at the beginning of
this section. The station sending this message is alerting a potential destination,
and all other stations within reception range, that it intends to send a data
frame to that destination.
• Clear to Send (CTS): This is the second frame in the four-way exchange. It
is sent by the destination station to the source station to grant permission to
send a data frame.
• Acknowledgment: Provides an acknowledgment from the destination to the
source that the immediately preceding data, management, or PS-Poll frame
was received correctly.
• Contention-Free (CF)-end: Announces the end of a contention-free period
that is part of the point coordination function.
• CF-End + CF-Ack: Acknowledges the CF-end. This frame ends the contention-
free period and releases stations from the restrictions associated with that
period.

## Slide 29: Data Frames
Eight data frame subtypes
  Organized in two groups
    First four carry upper-level data
    Remaining do not carry any user data
Data
  Simplest data frame, contention or contention-free use
Data + CF-Ack
  Carries data and acknowledges previously received data during contention-free period
Data + CF-Poll
  Used by point coordinator to deliver data and request send
Data + CF-Ack + CF-Poll
  Combines Data + CF-Ack and Data + CF-Poll
Notes: There are eight data frame subtypes, organized into two
groups. The first four subtypes define frames that carry upper-level data from
the source station to the destination station. The four data-carrying frames are
as follows:
• Data: This is the simplest data frame. It may be used in both a contention
period and a contention-free period.
• Data + CF-Ack: May only be sent during a contention-free period. In addition
to carrying data, this frame acknowledges previously received data.
• Data + CF-Poll: Used by a point coordinator to deliver data to a mobile station
and also to request that the mobile station send a data frame that it may
have buffered.
• Data + CF-Ack + CF-Poll: Combines the functions of the Data + CF-Ack and
Data + CF-Poll into a single frame.
The remaining four subtypes of data frames do not in fact carry any user
data. The Null Function data frame carries no data, polls, or acknowledgments.
It is used only to carry the power management bit in the frame control field to
the AP, to indicate that the station is changing to a low-power operating state.
The remaining three frames (CF-Ack, CF-Poll, CF-Ack + CF-Poll) have the same
functionality as the corresponding data frame subtypes in the preceding list (Data
+ CF-Ack, Data + CF-Poll, Data + CF-Ack + CF-Poll) but without the data.

## Slide 30: Management Frames
Used to manage communications between stations and APs
Management of associations
Request, response, reassociation, dissociation, and authentication
Notes: Management frames are used to manage communications between stations and APs. Functions covered include management of associations (request, response, reassociation, dissociation, and authentication.

## Slide 31: Table 13.4 IEEE 802.11 Physical Layer Standards
(Table is on page 436 in textbook)
Notes: Since its introduction, the IEEE 802.11 standard has been expanded and revised
a number of times. The first version of the standard, simply called IEEE 802.11,
includes the MAC layer and three physical layer specifications, two in the 2.4-GHz
band (ISM) and one in the infrared, all operating at 1 and 2 Mbps. This version
is now obsolete and no longer in use. Table 13.4 summarizes key characteristics
of the subsequent revisions. In this section, we survey 802.11b, 802.11a, 802.11g,
and 802.11n. The following section deals with 802.11ac and 802.11ad, both of which
provide for data rates greater than 1 Gbps.

## Slide 32: IEEE 802.11b
Extension of 802.11 DSSS scheme
  Data rates of 5.5 and 11 Mbps
Chipping rate 11 MHz
  Same as original DSSS scheme
  Complementary Code Keying (CCK) modulation gives higher data rate with same bandwidth and chipping rate
  Packet Binary Convolutional Coding (PBCC) for future higher rate use
Notes: One of the original 802.11 standards, now obsolete, used direct sequence spread
spectrum (DSSS). It operates in the 2.4-GHz ISM band, at data rates of 1 Mbps
and 2 Mbps. In the United States, the FCC (Federal Communications Commission)
requires no licensing for the use of this band. The number of channels available
depends on the bandwidth allocated by the various national regulatory agencies.
IEEE 802.11b is an extension of the IEEE 802.11 DSSS scheme, providing
data rates of 5.5 and 11 Mbps in the ISM band. The chipping rate is 11 MHz, which is
the same as the original DSSS scheme, thus providing the same occupied bandwidth.
To achieve a higher data rate in the same bandwidth at the same chipping rate, a
modulation scheme known as complementary code keying (CCK) is used.

## Slide 33
Notes: The CCK modulation scheme is quite complex and is not examined in detail here. Figure 13.9 provides an overview of the scheme for the 11-Mbps rate. Input data are treated in blocks of 8 bits at a rate of 1.375 MHz (8 bits/symbol  1.375 MHz = 11 Mbps). Six of these bits are mapped into one of 64 codes sequences derived from a 64  64 matrix known as the Walsh matrix (discussed in Chapter 17). The output of the mapping, plus the two additional bits, forms the input to a QPSK modulator.
An optional alternative to CCK is known as packet binary convolutional coding (PBCC). PBCC provides for potentially more efficient transmission at the cost of increased computation at the receiver. PBCC was incorporated into 802.11b in anticipation of its need for higher data rates for future enhancements to the standard.

## Slide 34
Notes: IEEE 802.11b defines two physical-layer frame
formats, which differ only in the length of the preamble. The long preamble of 144
bits is the same as used in the original 802.11 DSSS scheme and allows interoperability
with other legacy systems. The short preamble of 72 bits provides improved
throughput efficiency. Figure 13.10b illustrates the physical-layer frame format with
the short preamble. The PLCP (physical layer conversion protocol) Preamble field
enables the receiver to acquire an incoming signal and synchronize the demodulator.
It consists of two subfields: a 56-bit Sync field for synchronization and a 16-bit start-of-
frame delimiter (SFD ). The preamble is transmitted at 1 Mbps using differential
BPSK and Barker code spreading.

## Slide 35: PLCP Header
Follows the preamble and is transmitted at 2 Mbps using DQPSK
Consists of the following subfields:
  Signal
    Specifies the data rate at which the MPDU portion of the frame is transmitted
  Service
    Only 3 bits of this 8-bit field are used in 802.11b
  Length
    Indicates the length of the MPDU field by specifying the number of microseconds necessary to transmit the MPDU
  CRC
    A 16-bit error-detection code used to protect the Signal, Service, and Length fields
Notes: Following the preamble is the PLCP Header , which is transmitted at 2 Mbps
using DQPSK. It consists of the following subfields:
• Signal: Specifies the data rate at which the MPDU (MAC protocol data unit)
portion of the frame is transmitted.
• Service: Only 3 bits of this 8-bit field are used in 802.11b. One bit indicates
whether the transmit frequency and symbol clocks use the same local oscillator.
Another bit indicates whether CCK or PBCC encoding is used. A third bit
acts as an extension to the Length subfield.
• Length: Indicates the length of the MPDU field by specifying the number of
microseconds necessary to transmit the MPDU. Given the data rate, the length of
the MPDU in octets can be calculated. For any data rate over 8 Mbps, the length
extension bit from the Service field is needed to resolve a rounding ambiguity.
• CRC: A 16-bit error-detection code used to protect the Signal, Service, and
Length fields.
The MPDU field consists of a variable number of bits transmitted at the data
rate specified in the Signal subfield. Prior to transmission, all of the bits of the physical-
layer PDU are scrambled (see Appendix 12B for a discussion of scrambling).

## Slide 36: IEEE 802.11a
Universal Networking Information Infrastructure (UNNI)
  UNNI-1 band (5.15 to 5.25 GHz) for indoor use
  UNNI-2 band (5.25 to 5.35GHz) for indoor or outdoor
  UNNI-3 band (5.725 to 5.825 GHz) for outdoor
  Advantages over IEEE 802.11b/g:
  IEEE 802.11a
  Utilizes more available bandwidth
  Provides much higher data rates
  Uses a relatively uncluttered frequency spectrum (5 GHz)
Notes: Although 802.11b achieved a certain level of success, its limited data rate results in limited appeal. To meet the needs for a truly high-speed LAN, IEEE 802.11a was developed.
IEEE 802.11a makes use of the frequency band called the Universal Networking Information Infrastructure (UNNI), which is divided into three parts. The UNNI-1 band (5.15 to 5.25 GHz) is intended for indoor use; the UNNI-2 band (5.25 to 5.35 GHz) can be used either indoor or outdoor, and the UNNI-3 band (5.725 to 5.825 GHz) is for outdoor use.
IEEE 80211.a has several advantages over IEEE 802.11b/g:
IEEE 802.11a utilizes more available bandwidth than 802.11b/g. Each UNNI band provides four nonoverlapping channels for a total of 12 across the allocated spectrum.
IEEE 802.11a provides much higher data rates than 802.11b and the same maximum data rate as 802.11g.
IEEE 802.11a uses a different, relatively uncluttered frequency spectrum (5 GHz).

## Slide 37: Physical-Layer Frame Structure
Primary purpose of layer is to transmit MAC protocol data units as directed by the 802.11 MAC layer
Signal field consists of:
  Rate
    Specifies the data rate at which the data field portion of the frame is transmitted
  r:
    Reserved for future use
  Length
    Number of octets in the MAC PDU
  P:
    An even parity bit for the 17 bits in the
    Rate, r, and Length subfields
  Tail
    Consists of 6 zero bits appended
    to the symbol to bring the convolutional
    encoder to zero state
Data field consists of four subfields:
Service
MAC PDU
Tail
Pad
Notes: The primary purpose of the physical layer
is to transmit MAC protocol data units as directed by the 802.11 MAC layer. The
PLCP sublayer provides the framing and signaling bits needed for the OFDM
transmission and the PMD sublayer performs the actual encoding and transmission
operation.
Figure 13.10a illustrates the physical-layer frame format. The PLCP Preamble
field enables the receiver to acquire an incoming OFDM signal and synchronize the
demodulator. Next is the Signal field, which consists of 24 bits encoded as a single
OFDM symbol. The Preamble and Signal fields are transmitted at 6 Mbps using
BPSK. The signal field consists of the following subfields:
• Rate: Specifies the data rate at which the data field portion of the frame is
transmitted
• r: Reserved for future use
• Length: Number of octets in the MAC PDU
• P: An even parity bit for the 17 bits in the Rate, r, and Length subfields
• Tail: Consists of 6 zero bits appended to the symbol to bring the convolutional
encoder to zero state
The Data field consists of a variable number of OFDM symbols transmitted
at the data rate specified in the Rate subfield. Prior to transmission, all of the bits
of the Data field are scrambled (see Appendix 12B for a discussion of scrambling).
The Data field consists of four subfields:
• Service: Consists of 16 bits, with the first 7 bits set to zeros to synchronize the
descrambler in the receiver and the remaining 9 bits (all zeros) reserved for
future use.
• MAC PDU: Handed down from the MAC layer. The format is shown in
Figure 13.8.
Tail: Produced by replacing the six scrambled bits following the MPDU end
with 6 bits of all zeros; used to reinitialize the convolutional encoder.
• Pad: The number of bits required to make the Data field a multiple of the
number of bits in an OFDM symbol (48, 96, 192, or 288).

## Slide 38: IEEE 802.11g
Higher-speed extension to 802.11b
Operates in 2.4GHz band
Compatible with 802.11b devices
Combinesphysical layer encoding techniques used in 802.11 and 802.11b to provide service at a variety of data rates
  ERP-OFDM for 6, 9, 12, 18, 24, 36, 48, 54Mbps rates
  ERP-PBCC for 22 and 33Mbps rates
Notes: IEEE 802.11g extends 802.11b to data rates above 20 Mbps, up to 54 Mbps. Like 802.11b, 802.11g operates in the 2.4-GHz range and thus the two are compatible. The standard is designed so that 802.11b devices will work when connected to an 802.11g AP, and 802.11g devices will work when connected to an 802.11b AP, in both cases using the lower 802.11b data rate.
EE 802.11g offers a wider array of data rate and modulation scheme options. IEEE 802.11g provides compatibility with 802.11 and 802.11b by specifying the same modulation and framing schemes as these standards for 1, 2, 5.5, and 11 Mbps. At data rates of 6, 9, 12, 18, 24, 36, 48, and 54 Mbps, 802.11g adopts the 802.11a OFDM scheme, adapted for the 2.4 GHz rate; this is referred to as ERP-OFDM, with ERP standing for extended rate physical layer. In addition, an ERP-PBCC scheme is used to provide data rates of 22 and 33 Mbps.

## Slide 39: Table 13.5 Estimated Distance (m) Versus Data Rate
Notes: The IEEE 802.11 standards do not include a specification of speed versus distance objectives. Different vendors will give different values, depending on environment.Table 13.5, based on [LAYL04] gives estimated values for a typical office environment.

## Slide 40: IEEE 802.11n
Has enhancements in three general areas:
  Multiple-input-multiple-output (MIMO) antenna architecture
    Most important enhancement
  Radio transmission scheme
    Increased capacity
  MAC enhancements
    Most significant change is to aggregate multiple MAC frames into a single block for transmission
Notes: With increasing demands being placed on wireless LANs, the 802.11 committee looked for ways to increase the data throughput and overall capacity of 802.11 networks. The goal of this effort is to not just increase the bit rate of the transmitting antennas but to increase the effective throughput of the network. Increasing effective throughput involves not only looking at the signal encoding scheme, but also at the antenna architecture and the MAC frame structure. The result of these efforts is a package of improvements and enhancements embodied in IEEE 802.11n. This standard is defined to operate in both the 2.4-GHz and the 5-GHz bands and can therefore be made upwardly compatible with either 802.11a or 802.11b/g.
IEEE 802.11n embodies changes in three general areas: use of MIMO, enhancements in radio transmission, and MAC enhancements. We briefly examine each of these.
Multiple-input-multiple-output (MIMO) antenna architecture is the most important of the enhancements provided by 802.11n. A discussion of MIMO is beyond our scope, so we content ourselves with a brief overview. In a MIMO scheme, the transmitter employs multiple antennas. The source data stream is divided into n substreams, one for each of the n transmitting antennas. The individual substreams are the input to the transmitting antennas (multiple input). At the receiving end, m antennas receive the transmissions from the n source antennas via a combination of line-of-sight transmission and multipath. The outputs from the m receiving antennas (multiple output) are combined with the signals from the other receive radios. With a lot of complex math, the result is a much better receive signal than can be achieved with either a single antenna or multiple frequency channels. 802.11n defines a number of different combinations for the number of transmitters and the number of receivers, from 2  1 to 4  4. Each additional transmitter or receiver in the system increases the SNR (signal-to-noise ratio).
In addition to MIMO, 802.11n makes a number of changes in the radio transmission scheme to increase capacity. The most significant of these techniques, known as channel bonding, combines two 20-MHz channels to create a 40-MHz channel. Using OFDM, this allows for twice as many subchannels, doubling the transmission rate.
Finally, 802.11 provides some MAC enhancements. The most significant change is to aggregate multiple MAC frames into a single block for transmission. Once a station acquires the medium for transmission, it can transmit long packets without significant delays between transmissions. The receiver sends a single block acknowledgement. Frame aggregation can result in significantly improved efficiency in the use of the transmission capacity.

## Slide 41
Notes: The 802.11n specification includes three forms of aggregation, illustrated
in Figure 13.11 [CISC12b]. For simplicity, the 4-octet MAC trailer field is not
shown. A-MSDU aggregation combines multiple MSDUs into a single MPDU.
Thus there is a single MAC header and single FCS for all of the MSDUs rather
than for each of the MSDUs. This provides a certain amount of efficiency because
the 802.11 MAC header is potentially quite lengthy. However, if a bit error
occurs in one of the MSDU, all of the aggregated MSDUs must be retransmitted.
A-MPDU aggregation combines multiple MPDUs in a single physical transmission.
Thus, as with A-MSDU, only a single physical-layer header is needed.
This approach is less efficient because each MPDU includes the MAC header
and FCS. However, if a bit error occurs in one of the MPDUs, only that MPDU
needs to be retransmitted. Finally, the two forms of aggregation can be combined
(A-MPDU of A-MSDU).

## Slide 42
Notes: Figure 13.12 gives an indication of the effectiveness of 802.11n compared to
802.11g [DEBE07]. The chart shows the average throughput per user on a shared
system. As expected, the more active users competing for the wireless capacity,
the smaller the average throughput per user. IEEE 802.11n provides a significant
improvement, especially for networks in which a small number of users are actively
competing for transmission time.

## Slide 43
Notes: IEEE 802.11ac operates in the 5-GHz band, as does 802.11a and 802.11n. It is
designed to provide a smooth evolution from 802.11n. The new standard achieves
much higher data rates than 802.11n by means of enhancements in three areas
(Figure 13.13):
• Bandwidth: The maximum bandwidth of 802.11n is 40 MHz; the maximum
bandwidth of 802.11ac is 160 MHz.
• Signal encoding: 802.11n uses 64 QAM with OFDM, and 802.11ac uses 256
QAM with OFDM. Thus, more bits are encoded per symbol. Both schemes
use forward error correction with a code rate of 5/6 (ratio of data bits to
total bits).
• MIMO: With 802.11n, there can be a maximum of 4 channel input and 4 channel
output antennas. 802.11ac increases this to 8 * 8.

## Slide 44: IEEE 802.11ac
Includes the option of multiuser MIMO (MU-MIMO)
  On the downlink the transmitter is able to use its antenna resources to transmit multiple frames to different stations, all at the same time and over the same frequency spectrum
  Each antenna of a MU-MIMO AP can simultaneously communicate with a different single-antenna device, such as a smartphone or tablet
Requires that every 802.11ac transmission be sent as an A-MPDU aggregate
Notes: Two other changes going from 802.11n to 802.11ac are noteworthy.
802.11ac includes the option of multiuser MIMO (MU-MIMO). This means that
on the downlink, the transmitter is able to use its antenna resources to transmit
multiple frames to different stations, all at the same time and over the same
frequency spectrum. Thus, each antenna of a MU-MIMO AP can simultaneously
communicate with a different single-antenna device, such as a smartphone
or tablet. This enables the AP to deliver significantly more data in many
environments.
Another difference is that 802.11ac requires that every 802.11ac transmission
to be sent as an A-MPDU aggregate. Briefly, this requirement is imposed
to guarantee efficient use of the channel. For a more extended explanation, see
[CISC12b].

## Slide 45: IEEE 802.11ad
A version of 802.11 operating in the 60-GHz frequency band
  Offers the potential for much wider channel bandwidth than the 5-GHz band
  Few devices operate in the 60-GHz which means communications would experience less interference than in the other bands used by 802.11
Undesirable propagation characteristics:
  Losses are much higher in this range than in the ranges used for traditional microwave systems
  Multipath losses can be quite high
  Millimeter-wave signals generally don’t penetrate solid objects
Notes: IEEE 802.11ad is a version of 802.11 operating in the 60-GHz frequency band. This
band offers the potential for much wider channel bandwidth than the 5-GHz band,
enabling high data rates with relatively simple signal encoding and antenna characteristics.
Few devices operate in the 60-GHz band, which means communications
would experience less interference than in the other bands used by 802.11.
However, at 60 GHz, 802.11ad is operating in the millimeter range, which has
some undesirable propagation characteristics:
1. Free space loss increases with the square of the frequency [Equation (4.3)];
thus losses are much higher in this range than in the ranges used for traditional
microwave systems.
2. Multipath losses can be quite high. Reflection occurs when an electromagnetic
signal encounters a surface that is large relative to the wavelength of the
signal; scattering occurs if the size of an obstacle is on the order of the wavelength
of the signal or less; diffraction occurs when the wavefront encounters
the edge of an obstacle that is large compared to the wavelength.
3. Millimeter-wave signals generally don’t penetrate solid objects.
For these reasons, 802.11ad is likely to be useful only within a single room.
Because it can support high data rates and, for example, could easily transmit
uncompressed high-definition video, it is suitable for applications such as replacing
wires in a home entertainment system, or streaming high-definition movies from
your cell phone to your television.

## Slide 46: 802.11ac and 802.11ad Differences
802.11ac
Supports a MIMO antenna configuration
802.11ad
Is designed for single-antenna operation
Has a huge channel bandwidth of 2160 MHz
Notes: There are two striking differences between 802.11ac and 802.11ad. Whereas
802.11ac supports a MIMO antenna configuration, 802.11ad is designed for single-antenna
operation. And 802.11ad has a huge channel bandwidth of 2160 MHz.

## Slide 47: Table 13.6 IEEE 802.11ad Modulation and Coding Schemes
BPSK = binary phase-shift keying
DBPSK = differential binary phase-shift keying
LDPC = low density parity check code
OFDM = orthogonal frequency-division multiplexing
OQPSK = offset quadrature phase-shift keying
QAM = quadrature amplitude modulation
QPSK = quadrature phase-shift keying
RS = Reed-Solomon
Notes: IEEE 802.11ad defines four physical layer modulation and coding schemes
(Table 13.6). Each type has a distinct purpose and supports a different range of data rates.
Control PHY (CPHY) is by far the most robustly coded (and consequently,
lowest throughput) mode, with a code rate of only 1/2. Its purpose is exclusively to
transmit control channel messages. The CPHY robustness is evident from its use of
differential encoding, code spreading, and BPSK modulation. Differential encoding
eliminates the need for carrier tracking, 32x spreading contributes a theoretical 15
dB gain to the link budget, and BPSK is very noise tolerant.
As with CPHY, single-carrier PHY (SCPHY) uses the powerful low-density
parity-check (LDPC) code for robust forward error correction and provides three
options for modulation. The set of options for code rate and modulation density allow
for a trade-off between throughput and robustness to be determined operationally.
OFDM PHY (OFDMPHY) employs multicarrier modulation, which can provide
higher modulation densities and hence higher data throughput than the single-carrier
options. As with SCPHY, OFDMPHY provides a choice of error protection
ratio and the depth of modulation applied to the OFDM data carriers, again to
provide operational control over the robustness/throughput trade-off. The choice
between SCPHY and OFDMPHY depends on several factors. OFDM modulation
will generally impose greater power requirements than SCPHY, but is more robust
in the presence of multipath distortion.
The LDPC error-correcting coding technique that is common to the CPHY,
SCPHY, and OFDMPHY is based on a common codeword length of 672 bits carrying
336, 504, 420, or 546 payload bits to achieve a code rate of 1/2, 3/4, 5/8, or 13/16
as required.
Low-power single carrier (LPSCPHY) employs single-carrier modulation to
minimize power consumption. It also uses either Reed–Solomon or Hamming block
codes, which require less IC area and hence less power than LDPC, at the expense
of less robust error correction. Small battery-powered devices could benefit from
the extra power savings.

## Slide 48: Access and Privacy Services - Authentication
Used to establish station identity
Wired LANs assume physical connection gives authority to use LAN
Not a valid assumption for wireless LANs
802.11 supports several authentication schemes
Does not mandate any particular scheme
From relatively insecure handshaking to public-key encryption
802.11 requires mutually acceptable, successful authentication before association
Notes: There are two characteristics of a wired LAN that are not inherent in a wireless LAN.
1.In order to transmit over a wired LAN, a station must be physically connected to the LAN. On the other hand, with a wireless LAN, any station within radio range of the other devices on the LAN can transmit. In a sense, there is a form of authentication with a wired LAN, in that it requires some positive and presumably observable action to connect a station to a wired LAN.
2.Similarly, in order to receive a transmission from a station that is part of a wired LAN, the receiving station must also be attached to the wired LAN. On the other hand, with a wireless LAN, any station within radio range can receive. Thus, a wired LAN provides a degree of privacy, limiting reception of data to stations connected to the LAN.
IEEE 802.11 defines three services that provide a wireless LAN with these two features:
Authentication: Used to establish the identity of stations to each other. In a wired LAN, it is generally assumed that access to a physical connection conveys authority to connect to the LAN. This is not a valid assumption for a wireless LAN, in which connectivity is achieved simply by having an attached antenna that is properly tuned. The authentication service is used by stations to establish their identity with stations they wish to communicate with. IEEE 802.11 supports several authentication schemes and allows for expansion of the functionality of these schemes. The standard does not mandate any particular authentication scheme, which could range from relatively unsecure handshaking to public-key encryption schemes. However, IEEE 802.11 requires mutually acceptable, successful authentication before a station can establish an association with an AP.

## Slide 49: Access and Privacy Services Deauthentication and Privacy
Deauthentication
  Invoked whenever an existing authentication is to be terminated
Privacy
  Used to prevent messages being read by others
  802.11 allows optional use of encryption
Original WEP security features were weak
Subsequently 802.11i and WPA alternatives evolved giving better security
Notes: Deauthentication: This service is invoked whenever an existing authentication is to be terminated.
Privacy: Used to prevent the contents of messages from being read by other than the intended recipient. The standard provides for the optional use of encryption to assure privacy.
The original 802.11 specification included a set of security features for privacy and authentication that, unfortunately, were quite weak. For privacy, 802.11 defined the Wired Equivalent Privacy (WEP) algorithm. The privacy portion of the 802.11 standard contained major weaknesses. Subsequent to the development of WEP, the 802.11i task group has developed a set of capabilities to address the WLAN security issues. In order to accelerate the introduction of strong security into WLANs, the Wi-Fi Alliance promulgated Wi-Fi Protected Access (WPA) as a Wi-Fi standard. WPA is a set of security mechanisms that eliminates most 802.11 security issues and was based on the current state of the 802.11i standard. As 802.11i evolves, WPA will evolve to maintain compatibility.

## Slide 50: Summary
Wireless LAN configurations
Wireless LAN requirements
IEEE 802.11 architecture and services
  The Wi-Fi alliance
  IEEE 802.11 architecture
  IEEE 802.11 services
IEEE 802.11 medium access control
  Reliable data delivery
  Medium access control
  MAC frame
IEEE 802.11 physical layer
  IEEE 802.11b
  IEEE 802.11a
  IEEE 802.11g
  IEEE 802.11n
Gigabit Wi-Fi
  IEEE 802.11ac
  IEEE 802.11ad
IEEE 802.11 security considerations
  Access and privacy services
  Wireless LAN security standards
Notes: Chapter 13summary.