Mobile Ad Hoc Networking Working Group                Charles E. Perkins

INTERNET DRAFT                                     Nokia Research Center

2 March 2001                                          Elizabeth M. Royer

University of California, Santa Barbara

Samir R. Das

University of Cincinnati

Ad hoc On-Demand Distance Vector (AODV) Routing

draft-ietf-manet-aodv-08.txt

Status of This Memo

This document is a submission by the Mobile Ad Hoc Networking Working

Group of the Internet Engineering Task Force (IETF).  Comments should

be submitted to the manet@itd.nrl.navy.mil mailing list.

Distribution of this memo is unlimited.

This document is an Internet-Draft and is in full conformance with

all provisions of Section 10 of RFC2026.  Internet-Drafts are working

documents of the Internet Engineering Task Force (IETF), its areas,

and its working groups.  Note that other groups may also distribute

working documents as Internet-Drafts.

Internet-Drafts are draft documents valid for a maximum of six months

and may be updated, replaced, or obsoleted by other documents at

any time.  It is inappropriate to use Internet-Drafts as reference

material or to cite them other than as "work in progress."

The list of current Internet-Drafts can be accessed at:

http://www.ietf.org/ietf/1id-abstracts.txt

The list of Internet-Draft Shadow Directories can be accessed at:

http://www.ietf.org/shadow.html.

Abstract

The Ad Hoc On-Demand Distance Vector (AODV) routing protocol is

intended for use by mobile nodes in an ad hoc network.  It offers

quick adaptation to dynamic link conditions, low processing and

memory overhead, low network utilization, and determines unicast

between sources and destinations.  It uses destination sequence

numbers to ensure loop freedom at all times (even in the face of

anomalous delivery of routing control messages), solving problems

(such as ``counting to infinity'') associated with classical distance

vector protocols.

Perkins, Royer, Das          Expires 2 September 2001           [Page i]

Internet Draft                     AODV                     2 March 2001

Contents

Status of This Memo                                                    i

Abstract                                                               i

1. Introduction                                                       1

2. Overview                                                           1

3. AODV Terminology                                                   2

4. Route Request (RREQ) Message Format                                3

5. Route Reply (RREP) Message Format                                  4

6. Route Error (RERR) Message Format                                  6

7. Route Reply Acknowledgment (RREP-ACK) Message Format               7

8. AODV Operation                                                     7

8.1. Maintaining Route Utilization Records . . . . . . . . . .    7

8.2. Generating Route Requests . . . . . . . . . . . . . . . .    7

8.2.1. Controlling Route Request broadcasts  . . . . . .    8

8.3. Forwarding Route Requests . . . . . . . . . . . . . . . .    9

8.3.1. Processing Route Requests . . . . . . . . . . . .    9

8.4. Generating Route Replies  . . . . . . . . . . . . . . . .   11

8.4.1. Route Reply Generation by the Destination   . . .   11

8.4.2. Route Reply Generation by an Intermediate Node  .   11

8.4.3. Generating Gratuitous RREPs . . . . . . . . . . .   12

8.5. Forwarding Route Replies  . . . . . . . . . . . . . . . .   13

8.6. Operation over Unidirectional Links . . . . . . . . . . .   14

8.7. Hello Messages  . . . . . . . . . . . . . . . . . . . . .   14

8.8. Maintaining Local Connectivity  . . . . . . . . . . . . .   15

8.9. Route Error Messages  . . . . . . . . . . . . . . . . . .   16

8.9.1. Local Repair  . . . . . . . . . . . . . . . . . .   17

8.10. Route Expiry and Deletion . . . . . . . . . . . . . . . .   18

8.11. Actions After Reboot  . . . . . . . . . . . . . . . . . .   19

8.12. Interfaces  . . . . . . . . . . . . . . . . . . . . . . .   19

9. AODV and Aggregated Networks                                      20

10. Using AODV with Other Networks                                    20

11. Extensions                                                        20

11.1. Hello Interval Extension Format . . . . . . . . . . . . .   21

Perkins, Royer, Das          Expires 2 September 2001          [Page ii]

Internet Draft                     AODV                     2 March 2001

12. Configuration Parameters                                          21

13. Security Considerations                                           23

14. Acknowledgments                                                   23

1. Introduction

The Ad Hoc On-Demand Distance Vector (AODV) algorithm enables

dynamic, self-starting, multihop routing between participating mobile

nodes wishing to establish and maintain an ad hoc network.  AODV

allows mobile nodes to obtain routes quickly for new destinations,

and does not require nodes to maintain routes to destinations that

are not in active communication.  AODV allows mobile nodes to respond

quickly to link breakages and changes in network topology.  The

operation of AODV is loop-free, and by avoiding the Bellman-Ford

``counting to infinity'' problem offers quick convergence when the

ad hoc network topology changes (typically, when a node moves in the

network).  When links break, AODV causes the affected set of nodes to

be notified so that they are able to invalidate the routes using the

broken link.

One distinguishing feature of AODV is its use of a destination

sequence number for each route entry.  The destination sequence

number is created by the destination for any route information it

sends to requesting nodes.  Using destination sequence numbers

ensures loop freedom and is simple to program.  Given the choice

between two routes to a destination, a requesting node always selects

the one with the greatest sequence number.

2. Overview

Route Requests (RREQs), Route Replies (RREPs), and Route Errors

(RERRs) are the message types defined by AODV. These message types

are handled by UDP, and normal IP header processing applies.  So, for

instance, the requesting node is expected to use its IP address as

the source IP address for the messages.  The range of dissemination

of broadcast RREQs can be indicated by the TTL in the IP header.

Fragmentation is typically not required.

As long as the endpoints of a communication connection have valid

routes to each other, AODV does not play any role.  When a route to

a new destination is needed, the node uses a broadcast RREQ to find

a route to the destination.  A route can be determined when the RREQ

reaches either the destination itself, or an intermediate node with

a 'fresh enough' route to the destination.  A 'fresh enough' route

is an unexpired route entry for the destination whose associated

Perkins, Royer, Das          Expires 2 September 2001           [Page 1]

Internet Draft                     AODV                     2 March 2001

sequence number is at least as great as that contained in the RREQ.

The route is made available by unicasting a RREP back to the source

of the RREQ. Since each node receiving the request caches a route

back to the source of the request, the RREP can be unicast back from

the destination to the source, or from any intermediate node that

is able to satisfy the request back to the source.  A RREQ can be

conditioned by requirements on the path to the destination, namely

bandwidth or delay bounds.

Nodes monitor the link status of next hops in active routes.  When a

link break in an active route is detected, a RERR message is used to

notify other nodes that the loss of that link has occurred.  The RERR

message indicates which destinations are now unreachable due to the

loss of the link.

AODV is a routing protocol, and it deals with route table management.

Route table information must be kept even for ephemeral routes, such

as are created to temporarily store reverse paths towards nodes

originating RREQs.  AODV uses the following fields with each route

table entry:

-  Destination IP Address

-  Destination Sequence Number

-  Interface

-  Hop Count (number of hops needed to reach destination)

-  Last Hop Count (described in subsection 8.2.1)

-  Next Hop

-  List of Precursors (described in Section 8.1)

-  Lifetime (expiration or deletion time of the route)

-  Routing Flags

3. AODV Terminology

This protocol specification uses conventional meanings [1] for

capitalized words such as MUST, SHOULD, etc., to indicate requirement

levels for various protocol features.  This section defines other

terminology used with AODV that is not already defined in [3].

active route

A routing table entry with a finite metric in the Hop Count

field.  A routing table may contain entries that are not active

(invalid routes or entries).  They have an infinite metric

Perkins, Royer, Das          Expires 2 September 2001           [Page 2]

Internet Draft                     AODV                     2 March 2001

in the Hop Count field.  Only active entries can be used to

forward data packets.  Invalid entries are eventually deleted.

forwarding node

A node which agrees to forward packets destined for another

destination node, by retransmitting them to a next hop which is

closer to the unicast destination along a path which has been

set up using routing control messages.

forward route

A route set up to send data packets from a source to a

destination.

reverse route

A route set up to forward a reply (RREP) packet back to the

source from the destination or from an intermediate node having

a route to the destination.

4. Route Request (RREQ) Message Format

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|     Type      |J|R|G|       Reserved          |   Hop Count   |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                         Broadcast ID                          |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                    Destination IP Address                     |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                  Destination Sequence Number                  |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                       Source IP Address                       |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                     Source Sequence Number                    |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

The format of the Route Request message is illustrated above, and

contains the following fields:

Type           1

J              Join flag; reserved for multicast.

R              Repair flag; reserved for multicast.

Perkins, Royer, Das          Expires 2 September 2001           [Page 3]

Internet Draft                     AODV                     2 March 2001

G              Gratuitous RREP flag; indicates whether a

gratuitous RREP should be unicast to the node

specified in the Destination IP Address field (see

sections 8.2, 8.4.3)

Reserved       Sent as 0; ignored on reception.

Hop Count      The number of hops from the Source IP Address to

the node handling the request.

Broadcast ID   A sequence number uniquely identifying the

particular RREQ when taken in conjunction with the

source node's IP address.

Destination IP Address

The IP address of destination for which a route is

desired.

Destination Sequence Number

The last sequence number received in the past by

the source for any route towards the destination.

Source IP Address

The IP address of the node which originated the

Route Request.

Source Sequence Number

The current sequence number to be used for route

entries pointing to (and generated by) the source

of the route request.

5. Route Reply (RREP) Message Format

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|     Type      |R|A|    Reserved     |Prefix Sz|   Hop Count   |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                     Destination IP address                    |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                  Destination Sequence Number                  |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                       Source IP address                       |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                           Lifetime                            |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Perkins, Royer, Das          Expires 2 September 2001           [Page 4]

Internet Draft                     AODV                     2 March 2001

The format of the Route Reply message is illustrated above, and

contains the following fields:

Type          2

R             Repair flag; used for multicast.

A             Acknowledgment required; see sections 7 and 8.5.

Reserved      Sent as 0; ignored on reception.

Prefix Size   If nonzero, the 5-bit Prefix Size specifies that the

indicated next hop may be used for any nodes with

the same routing prefix (as defined by the Prefix

Size) as the requested destination.

Hop Count     The number of hops from the Source IP Address to

the Destination IP Address.  For multicast route

requests this indicates the number of hops to the

multicast tree member sending the RREP.

Destination IP Address

The IP address of the destination for which a route

is supplied.

Destination Sequence Number

The destination sequence number associated to the

route.

Source IP Address

The IP address of the source node which issued the

RREQ for which the route is supplied.

Lifetime      The time for which nodes receiving the RREP consider

the route to be valid.

Note that the Prefix Size allows a Subnet Leader to supply a route

for every host in the subnet defined by the routing prefix, which

is determined by the IP address of the Subnet Leader and the Prefix

Size.  In order to make use of this feature, the Subnet Leader has to

guarantee reachability to all the hosts sharing the indicated subnet

prefix.  The Subnet Leader is also responsible for maintaining the

Destination Sequence Number for the whole subnet.

Perkins, Royer, Das          Expires 2 September 2001           [Page 5]

Internet Draft                     AODV                     2 March 2001

6. Route Error (RERR) Message Format

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|     Type      |N|          Reserved           |   DestCount   |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|            Unreachable Destination IP Address (1)             |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|         Unreachable Destination Sequence Number (1)           |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-|

|  Additional Unreachable Destination IP Addresses (if needed)  |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|Additional Unreachable Destination Sequence Numbers (if needed)|

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

The format of the Route Error message is illustrated above, and

contains the following fields:

Type        3

N           No delete flag; set when a node has performed a local

repair of a link, and upstream nodes should not delete

the route.

Reserved    Sent as 0; ignored on reception.

DestCount   The number of unreachable destinations included in the

message; MUST be at least 1.

Unreachable Destination IP Address

The IP address of the destination which has become

unreachable due to a link break.

Unreachable Destination Sequence Number

The last known sequence number, incremented by one,

of the destination listed in the previous Unreachable

Destination IP Address field.

The RERR message is sent whenever a link break causes one or more

destinations to become unreachable.  The unreachable destination

addresses included are those of all lost destinations which are now

unreachable due to the loss of that link.

Perkins, Royer, Das          Expires 2 September 2001           [Page 6]

Internet Draft                     AODV                     2 March 2001

7. Route Reply Acknowledgment (RREP-ACK) Message Format

0                   1

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|     Type      |   Reserved    |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Type        4

Reserved    Sent as 0; ignored on reception.

The RREP-ACK message may be used to acknowledge receipt of a RREP

message.  It is used in cases where the link over which the RREP

message is sent may be unreliable.

8. AODV Operation

This section describes the scenarios under which nodes generate

RREQs, RREPs and RERRs for unicast communication, and how the message

data are handled.

8.1. Maintaining Route Utilization Records

For each valid route maintained by a node (containing a finite Hop

Count metric) as a routing table entry, the node also maintains a

list of precursors that may be forwarding packets on this route.

These precursors will receive notifications from the node in the

event of detection of the loss of the next hop link.  The list of

precursors in a routing table entry contains those neighboring nodes

to which a route reply was generated or forwarded.

Each time a route is used to forward a data packet, its Lifetime

field is updated to be current time plus ACTIVE_ROUTE_TIMEOUT.

8.2. Generating Route Requests

A node broadcasts a RREQ when it determines that it needs a route

to a destination and does not have one available.  This can happen

if the destination is previously unknown to the node, or if a

previously valid route to the destination expires or is broken

(i.e., an infinite metric is associated with the route).  The

Destination Sequence Number field in the RREQ message is the last

known destination sequence number for this destination and is copied

from the Destination Sequence Number field in the routing table.  If

Perkins, Royer, Das          Expires 2 September 2001           [Page 7]

Internet Draft                     AODV                     2 March 2001

no sequence number is known, a sequence number of zero is used.  The

Source Sequence Number in the RREQ message is the node's own sequence

number.  The Broadcast ID field is incremented by one from the last

broadcast ID used by the current node.  Each node maintains only one

broadcast ID. The Hop Count field is set to zero.

A source node often expects to have bidirectional communications with

a destination node.  In such cases, it is not sufficient for the

source node to have a route to the destination node; the destination

must also have a route back to the source node.  In order for this

to happen as efficiently as possible, any generation of an RREP

by an intermediate node (as in section 8.4) for delivery to the

source node, should be accompanied by some action which notifies the

destination about a route back to the source node.  The source node

selects this mode of operation in the intermediate nodes by setting

the `G' flag.  See section 8.4.3 for details about actions taken by

the intermediate node in response to a RREQ with the `G' flag set.

After broadcasting a RREQ, a node waits for a RREP. If the RREP is

not received within NET_TRAVERSAL_TIME milliseconds, the node MAY

rebroadcast the RREQ, up to a maximum of RREQ_RETRIES times.  Each

rebroadcast MUST increment the Broadcast ID field.

Data packets waiting for a route (i.e., waiting for a RREP after RREQ

has been sent) SHOULD be buffered.  The buffering SHOULD be FIFO. If

a RREQ has been rebroadcast RREQ_RETRIES times without receiving any

RREP, all data packets destined for the corresponding destination

SHOULD be dropped from the buffer and a Destination Unreachable

message delivered to the application.

8.2.1. Controlling Route Request broadcasts

To prevent unnecessary network-wide broadcasts of RREQs, the

source node SHOULD use an expanding ring search technique as an

optimization.  In an expanding ring search, the source node initially

uses a TTL = TTL_START in the RREQ packet IP header and sets the

timeout for receiving a RREP to 2 * TTL * NODE_TRAVERSAL_TIME

milliseconds.  Upon timeout, the source rebroadcasts the RREQ with

the TTL incremented by TTL_INCREMENT. This continues until the

TTL set in the RREQ reaches TTL_THRESHOLD, beyond which a TTL =

NET_DIAMETER is used for each rebroadcast.  Each time, the timeout

for receiving a RREP is calculated as before.  Each rebroadcast

increments the Broadcast ID field in the RREQ packet.  The RREQ

can be rebroadcast with TTL = NET_DIAMETER up to a maximum of

RREQ_RETRIES times.

When a RREP is received, the Hop Count used in the RREP packet is

remembered as Last Hop Count in the routing table.  When a new route

Perkins, Royer, Das          Expires 2 September 2001           [Page 8]

Internet Draft                     AODV                     2 March 2001

to the same destination is required at a later time (e.g., upon route

loss), the TTL in the RREQ IP header is initially set to this Last

Hop Count plus TTL_INCREMENT. Thereafter, following each timeout the

TTL is incremented by TTL_INCREMENT until TTL = TTL_THRESHOLD is

reached.  Beyond this TTL = NET_DIAMETER is used as before.

As a further optimization, timeouts MAY be determined dynamically via

measurements, instead of using a statically configured value related

to NODE_TRAVERSAL_TIME. To accomplish this, the RREQ may carry the

timestamp via an extension field as defined in Section 11 to be

carried back by the RREP packet (again via an extension field).  The

difference between the current time and this timestamp will determine

the route discovery latency.  The timeout may be set to be a small

factor times the average of the last few route discovery latencies

for the concerned destination.  These latencies may be recorded as

additional fields in the routing table.

If the optimizations described in this section are used, an expired

routing table entry SHOULD NOT be expunged before DELETE_PERIOD.

Otherwise, the soft state corresponding to the route (e.g., Last Hop

Count) will be lost.  In such cases, a longer routing table entry

expunge time may be specified.  Any routing table entry waiting for a

RREP should not be expunged before RREP_WAIT_TIME.

8.3. Forwarding Route Requests

When a node receives a broadcast RREQ, it first checks to determine

whether it has received a RREQ with the same Source IP Address

and Broadcast ID within at least the last BROADCAST_RECORD_TIME

milliseconds.  If such a RREQ has been received, the node silently

discards the newly received RREQ. The rest of this subsection

describes actions taken for RREQs that are not discarded.

8.3.1. Processing Route Requests

When a node receives a RREQ, the node checks to determine whether it

has an active route to the destination.  If the node does not have

an active route, it rebroadcasts the RREQ from its interface(s) but

using its own IP address in the IP header of the outgoing RREQ. The

Destination Sequence Number in the RREQ is updated to the maximum

of the existing Destination Sequence Number in the RREQ and the

destination sequence number in the routing table (if an entry exists)

of the current node.  The TTL or hop limit field in the outgoing IP

header is decreased by one.  The Hop Count field in the broadcast

RREQ message is incremented by one, to account for the new hop

through the intermediate node.

Perkins, Royer, Das          Expires 2 September 2001           [Page 9]

Internet Draft                     AODV                     2 March 2001

If the node, on the other hand, does have an active route for the

destination, it compares the destination sequence number for that

route with the Destination Sequence Number field of the incoming

RREQ. If the existing destination sequence number is smaller than

the Destination Sequence Number field of the RREQ, the node again

rebroadcasts the RREQ just as if it did not have an active route to

the destination.

The node generates a RREP (as discussed further in section 8.4) if

either:

(i)       it has an active route to the destination, and the

node's existing destination sequence number is greater

than or equal to the Destination Sequence Number of the

RREQ, or

(ii)      it is itself the destination.

The node always creates or updates a reverse route to the Source IP

Address in its routing table.  If a route to the Source IP Address

already exists, it is updated only if either

(i)       the Source Sequence Number in the RREQ is higher than

the destination sequence number of the Source IP Address

in the route table, or

(ii)      the sequence numbers are equal, but the hop count as

specified by the RREQ is now smaller than the existing

hop count in the routing table.

When a reverse route is created or updated, the following actions are

carried out:

1. the Source Sequence Number from the RREQ is copied to the

corresponding destination sequence number;

2. the next hop in the routing table becomes the node broadcasting

the RREQ (it is obtained from the source IP address in the IP

header and is often not equal to the Source IP Address field in

the RREQ message);

3. the hop count is copied from the Hop Count in the RREQ message;

4. the lifetime of the route is the higher of its current lifetime

(for an active route) and current time plus REV_ROUTE_LIFE.

Even if the route is not updated because the existing route has a

higher destination sequence number, but if it is scheduled to expire

Perkins, Royer, Das          Expires 2 September 2001          [Page 10]

Internet Draft                     AODV                     2 March 2001

before REV_ROUTE_LIFE, its lifetime is still updated to be current

time plus REV_ROUTE_LIFE.

This reverse route would be needed in case the node receives an

eventual RREP back to the node which originated the RREQ (identified

by the Source IP Address).

8.4. Generating Route Replies

If a node receives a route request for a destination, and either

has a fresh enough route to satisfy the request or is itself the

destination, the node generates a RREP message and unicasts it back

to the node indicated by the Source IP Address field of the received

RREQ. The node generating the RREP message copies the Source and

Destination IP Addresses in RREQ message into the corresponding

fields in the RREP message which is to be sent back toward the

source of the RREQ. Additional operations are slightly different,

depending on whether the node is itself the requested destination, or

instead if it is an intermediate node with an admissible route to the

destination.

As the RREP is forwarded to the source, the Hop Count field is

incremented by one at each hop.  Thus, when the RREP reaches the

source, the Hop Count represents the distance, in hops, of the

destination from the source.

8.4.1. Route Reply Generation by the Destination

If the generating node is the destination itself, it uses a

destination sequence number at least equal to a sequence number

generated after the last detected change in its neighbor set and at

least equal to the destination sequence number in the RREQ. If the

destination node has not detected any change in its set of neighbors

since it last incremented its destination sequence number, it MAY use

the same destination sequence number.  The destination node places

the value zero in the Hop Count field of the RREP.

The destination node copies the value MY_ROUTE_TIMEOUT into

the Lifetime field of the RREP. Each node MAY make a separate

determination about its value MY_ROUTE_TIMEOUT.

8.4.2. Route Reply Generation by an Intermediate Node

If node generating the RREP is not the destination node, but

instead is an intermediate hop along the path from the source to the

Perkins, Royer, Das          Expires 2 September 2001          [Page 11]

Internet Draft                     AODV                     2 March 2001

destination, it copies the last known destination sequence number in

the Destination Sequence Number field in the RREP message.

The intermediate node places its distance in hops from the

destination (indicated by the hop count in the routing table) plus

one in the Hop Count field in the RREP.

When the intermediate node updates its route table for the source

of the RREQ, it puts the last hop node (from which it received the

RREQ, as indicated by the source IP address field in the IP header)

into the precursor list for the forward path route entry -- i.e., the

entry for the Destination IP Address.  Furthermore, the intermediate

node puts the next hop towards the destination in the precursor list

for the reverse route entry -- i.e., the entry for the Source IP

Address field of the RREQ message data.

The intermediate node calculates the Lifetime field of the RREP by

subtracting the current time from the expiration time in its route

table entry.

8.4.3. Generating Gratuitous RREPs

When a node receives a RREQ and responds with a RREP, it does not

forward the RREQ any further.  If all incarnations of a single

RREQ are replied to by intermediate nodes, the destination does

not receive any copies of the RREQ. Hence, it does not learn of a

route to the source node.  This can be problematic if the source is

attempting to establish a TCP session.  In order that the destination

learn of routes to the source node, the source node SHOULD set the

gratuitous RREP ('G') flag in the RREQ if the session is going to be

run over TCP, or if the destination should receive the gratuitous

RREP for any other reason.  Intermediate nodes receiving a RREQ

with the 'G' flag set and responding with a RREP SHOULD unicast a

gratuitous RREP to the destination node.

The RREP that is sent to the source of the RREQ is the same as

before.  The gratuitous RREP that is to be sent to the desired

destination contains the following values in the RREP message fields:

Hop Count  The Hop Count as received in the RREQ

Destination IP Address

The IP address of the node that generated the RREQ

Destination Sequence Number

The Source Sequence Number from the RREQ

Perkins, Royer, Das          Expires 2 September 2001          [Page 12]

Internet Draft                     AODV                     2 March 2001

Source IP Address

The IP address of the destination node

Lifetime   The remaining lifetime of the route towards the

destination node, as known by the intermediate node.

The gratuitous RREP is then sent to the next hop along the path to

the destination node.

8.5. Forwarding Route Replies

When a node receives a RREP message, it first compares the

Destination Sequence Number in the message with its own copy of

destination sequence number for the Destination IP Address in the

RREP message.  The forward route for this destination is created or

updated only if (i) the Destination Sequence Number in the RREP is

greater than the node's copy of the destination sequence number, or

(ii) the sequence numbers are the same, but the route is no longer

active or the Hop Count in RREP is smaller than the hop count in

route table entry.  If a new route is created or the old route is

updated, the next hop is the node from which the RREP is received,

which is indicated by the source IP address field in the IP header;

the hop count is the Hop Count in the RREP message plus one; the

expiry time is the current time plus the Lifetime in the RREP

message; the destination sequence number is the Destination Sequence

Number in the RREP message.

The current node can now begin using this route to send data packets

to the destination.

If the current node is not the source node as indicated by the Source

IP Address in the RREP message AND a forward route has been created

or updated as described before, the node consults its route table

entry for the source node to determine the next hop for the RREP

packet, and then forwards the RREP towards the source with its Hop

Count incremented by one.

When any node generates or forwards a RREP, the precursor list for

the corresponding destination node is updated by adding to it the

next hop node to which the RREP is forwarded.  Also, at each node the

(reverse) route used to forward a RREP has its lifetime changed to

current time plus ACTIVE_ROUTE_TIMEOUT.

If a node forwards a RREP over a link that is likely to have errors

or be unidirectional, the node MAY set the `A' flag to require that

the recipient of the RREP acknowledge receipt of the RREP by sending

a RREP-ACK message back.

Perkins, Royer, Das          Expires 2 September 2001          [Page 13]

Internet Draft                     AODV                     2 March 2001

8.6. Operation over Unidirectional Links

When unidirectional links are present, it is possible that a RREP

transmission may fail.  Such failure can be detected via the absence

of a link-layer or network-layer acknowledgment (e.g., RREP-ACK). If

no other RREP generated from the same route request broadcast reaches

the source, the source will redo the broadcast after a timeout (see

section 8.2).  However, the same scenario will repeat, and no route

will be discovered even after repeated retries.  This is possible

even when bidirectional routes between source and destination do

exist.  This happens because a RREQ transmission may occur over a

unidirectional link.  Link layers using broadcast transmissions for

RREQ will not be able to detect the presence of such unidirectional

links.  Also, in AODV any node acts on only the first RREQ with

the same broadcast ID and ignores any subsequent RREQs.  It is

possible that the first RREQ arrives along a path that has one or

more unidirectional link(s).  However, a subsequent RREQ may arrive

via a bidirectional path (assuming such paths exist), but it will be

ignored.

To prevent this problem, a node that fails to transmit a RREP

remembers the next-hop of the failed RREP in a ``blacklist'' set.  A

node ignores all RREQs received from any node in its blacklist set.

Nodes are removed from the blacklist set after a BLACKLIST_TIMEOUT

period.  This period should be set to the upper bound of the time it

takes to perform the allowed number of route request retry attempts

as described in section 8.2.

8.7. Hello Messages

A node MAY offer connectivity information by broadcasting local

Hello messages as follows.  Every HELLO_INTERVAL milliseconds, the

node checks whether it has sent a broadcast (e.g., a RREQ or an

appropriate layer 2 message) within the last HELLO_INTERVAL. If it

has not, it MAY generate a broadcast RREP with TTL = 1, called a

Hello message, with the message fields set as follows:

Destination IP Address

The node's IP address.

Destination Sequence Number

The node's latest sequence number.

Hop Count   0

Lifetime    ALLOWED_HELLO_LOSS * HELLO_INTERVAL

Perkins, Royer, Das          Expires 2 September 2001          [Page 14]

Internet Draft                     AODV                     2 March 2001

A node MAY determine connectivity by listening for packets from

its set of neighbors.  If it receives no packets for more than

ALLOWED_HELLO_LOSS * HELLO_INTERVAL milliseconds, the node SHOULD

assume that the link to this neighbor is currently broken.  When this

happens, the node SHOULD proceed as in Section 8.9.

8.8. Maintaining Local Connectivity

Each forwarding node SHOULD keep track of its active next hops (i.e.,

which next hops have been used to forward packets towards some

destination within the last ACTIVE_ROUTE_TIMEOUT milliseconds).  This

is done by updating the Lifetime field of a routing table entry used

to forward data packets to current time plus ACTIVE_ROUTE_TIMEOUT

milliseconds.  For purposes of efficiency, each node may try to learn

which of these active next hops are really in the neighborhood at the

current time using one or more of the available link or network layer

mechanisms, as described below.

-  Any suitable link layer notification, such as those provided by

IEEE 802.11, can be used to determine connectivity, each time

a packet is transmitted to an active next hop.  For example,

absence of a link layer ACK or failure to get a CTS after sending

RTS, even after the maximum number of retransmission attempts,

will indicate loss of the link to this active next hop.

-  Passive acknowledgment can be used when the next hop is expected

to forward the packet, by listening to the channel for a

transmission attempt made by the next hop.  If transmission is

not detected within NEXT_HOP_WAIT milliseconds or the next hop is

not a forwarding node (and thus is never supposed to transmit the

packet) one of the following methods should be used to determine

connectivity.

*  Receiving an ICMP ACK message from the next hop.  The ICMP

ACK message SHOULD be sent to a forwarding node by a next hop

which is also the destination as in the in the IP header of

the packet.  This should be done only when this destination

has not sent any packets to the concerned forwarding node

within the last HELLO_INTERVAL milliseconds.

*  A RREQ unicast to the next hop, asking for a route to the

next hop.

*  An ICMP Echo Request message unicast to the next hop.

If a link to the next hop cannot be detected by any of these methods,

the forwarding node SHOULD assume that the link is broken, and take

corrective action by following the methods specified in Section 8.9.

Perkins, Royer, Das          Expires 2 September 2001          [Page 15]

Internet Draft                     AODV                     2 March 2001

8.9. Route Error Messages

A node initiates a RERR message in three situations:

(i)       if it detects a link break for the next hop of an active

route in its routing table, or

(ii)      if it gets a data packet destined to a node for which it

does not have an active route, or

(iii)     if it receives a RERR from a neighbor for one or more

active routes.

For cases (i) and (ii), the destination sequence numbers in the

routing table for the unreachable destination(s) are incremented by

one.  Then RERR is broadcast with the unreachable destination(s) and

their incremented destination sequence number(s) included in the

packet.  For case (i), the unreachable destinations are the broken

next hop, and any additional destinations which are now unreachable

due to the loss of this next hop link.  These additional destinations

are those that also use the lost link as next hop in the routing

table.  For case (ii), there is only one unreachable destination,

which is the destination of the data packet that cannot be delivered.

The DestCount field of the RERR packet indicates the number of

unreachable destinations included in the packet.

For cases (i) and (ii), for each unreachable destination the node

copies the value in the Hop Count route table field into the Last

Hop Count field, and marks the Hop Count for this destination as

infinity, and thus invalidates the route.

For case (iii) when a node receives a RERR message, for each

unreachable destination included in the packet, the node determines

whether the source node (as indicated by the source IP address in the

IP header) forwarding the RERR packet is its own next hop used to

reach this destination.  If so, the node takes the following actions:

(a)       updates the corresponding destination sequence number

with the Destination Sequence Number in the packet, and

(b)       marks the Hop Count for this destination as infinity,

and thus invalidates the route.  The old value of Hop

Count is copied into the Last Hop Count field.

(c)       checks the precursor list for this destination for

emptiness.  If one or more of the precursor lists for

the unreachable destinations are non-empty, the node

creates a RERR message, including as unreachable each

destination with a non-empty precursor list.  It also

Perkins, Royer, Das          Expires 2 September 2001          [Page 16]

Internet Draft                     AODV                     2 March 2001

includes their destination sequence numbers, and then

broadcasts this RERR message.

When a node broadcasts a RERR message, it always deletes the

precursor list of each unreachable destination included in the

message.

When a node invalidates a route to a neighboring node, it must also

delete that neighbor from any precursor lists for routes to other

nodes.  This prevents precursor lists from containing stale entries

of neighbors with which the node is no longer able to communicate.

The node should inspect the precursor list of each destination entry

in its routing table, and delete the lost neighbor from any list in

which it appears.

8.9.1. Local Repair

When a link break in an active route occurs, the node upstream of

that break MAY choose to repair the link locally if the destination

is no farther than MAX_REPAIR_TTL hops away.  To repair the link

break itself, it increments the sequence number for the destination

and then broadcasts a RREQ for that destination.  The TTL of the RREQ

should initially be set to the following value:

max(MIN_REPAIR_TTL, 0.5 distance to source) + LOCAL_ADD_TTL      .

Thus, local repair attempts should never be visible to the source

node, and will always have minimum TTL equal to MIN_REPAIR_TTL

+ LOCAL_ADD_TTL. The node initiating the repair then waits the

discovery period to receive RREPs in response to the RREQ. If, at

the end of the discovery period, it has not received a RREP for that

destination, it proceeds as described in Section 8.9 by creating a

RERR message for that destination.

On the other hand, if the nodes does receive one or more RREPs during

the discovery period, the node proceeds as described in Section 8.5,

creating a route table entry for that destination.  It then compares

the hop count of the new route with the value in the last hop count

route table entry for that destination.  If the hop count of the

newly determined route to the destination is greater than the hop

count of the previously known route, as recorded in the last hop

count field, the node MAY create a RERR message for the destination

and send this message to the source node.  The node sets the 'N' flag

of the RERR, and then broadcasts this message if it has one or more

precursor nodes for this route table entry.

A node which receives a RERR message with the 'N' flag set MUST

NOT delete the route to that destination.  The only action taken

should be the retransmission of the message, if the RERR arrived

from the next hop along that route, and if there are one or more

Perkins, Royer, Das          Expires 2 September 2001          [Page 17]

Internet Draft                     AODV                     2 March 2001

precursor nodes for that route to the destination.  When the source

node receives a RERR message with the 'N' flag set, if this message

came from its next hop along its route to the destination then the

source node MAY choose to reinitiate route discovery, as described in

Section 8.2.

Local repair of link breaks in active routes sometimes results in

increased path lengths to those destinations.  Repairing the link

locally is likely to increase the number of data packets which are

able to be delivered to the destinations, since data packets will not

be dropped as the RERR travels to the source node.  Sending a RERR

to the source node after locally repairing the link break allows the

source to find a fresh route to the destination which is more optimal

based on current node positions.  However, it does not require the

source node to rebuild the route, as the source may be done, or

nearly done, with the data session.

When a link breaks along an active route, there are often multiple

destinations which become unreachable.  The node which is upstream

of the broken link tries an immediate local repair for only the one

destination towards which the packet was traveling.  Other routes

using the same link MUST be marked as broken, but the node handling

the local repair MAY flag each such newly broken route as locally

repairable; this local repair flag in the route table MUST be reset

when the route times out (i.e., after the route has been not been

active for ACTIVE_ROUTE_TIMEOUT). Before the timeout occurs, these

other routes will be repaired as needed when packets arrive for the

other destinations.  Alternatively, depending upon local congestion,

the node MAY begin the process of establishing local repairs for the

other routes, without waiting for new packets to arrive.

8.10. Route Expiry and Deletion

If the Lifetime of an active routing entry expires, the following

actions are taken.

1. The entry is invalidated by copying the Hop Count to the Last Hop

Count field and then making the Hop Count infinity.

2. The destination sequence number of this routing entry is

incremented by one.

3. The Lifetime field is updated to current time plus DELETE_PERIOD.

Before this time, the entry MUST NOT be deleted.

Note that the Lifetime field plays dual role -- for an active route

it is the expiry time, and for an invalid route it is the deletion

time.

Perkins, Royer, Das          Expires 2 September 2001          [Page 18]

Internet Draft                     AODV                     2 March 2001

These actions are also taken whenever a route entry is invalidated

for any reason, for example, for link breakage or receiving a RERR.

If a data packet is received for an invalid route, the Lifetime

field is always updated to current time plus DELETE_PERIOD. The

determination of DELETE_PERIOD is discussed in Section 12

8.11. Actions After Reboot

A node participating in the ad hoc network must take certain

actions after reboot as it will have lost its prior sequence number

and as well as its last known sequence numbers for various other

destinations.  However, there may be neighboring nodes which are

using this node as an active next hop.  This can potentially create

routing loops.  To prevent this possibility, each node on reboot

waits for DELETE_PERIOD. In this time, it does not respond to

any routing packets.  However, if it receives a data packet, it

broadcasts a RERR as described in subsection 8.9 and resets the

waiting timer to expire after current time plus DELETE_PERIOD.

It can be shown that by the time the rebooted node comes out of

the waiting phase and becomes an active router again, none of its

neighbors will be using it as an active next hop any more.  Its own

sequence number gets updated once it receives a RREQ from any other

node, as the RREQ always carries the maximum destination sequence

number seen en route.

8.12. Interfaces

Because AODV should operate smoothly over wired, as well as wireless,

networks, and because it is likely that AODV will also be used with

multi-homed radios, the interface over which packets arrive must

be known to AODV whenever a packet is received.  This includes the

reception of RREQ, RREP, and RERR messages.  Whenever a packet is

received from a new neighbor, the interface on which that packet was

received is recorded into the route table entry for that neighbor,

along with all the other appropriate routing information.  Similarly,

whenever a route to a new destination is learned, the interface

through which the destination can be reached is also recorded into

the destination's route table entry.

When multiple interfaces are available, a node receiving and

rebroadcasting a RREQ message rebroadcasts that message on all

interfaces.  When a node needs to transmit a RERR, it should only

broadcast it on those interfaces which have precursor nodes for that

route.

Perkins, Royer, Das          Expires 2 September 2001          [Page 19]

Internet Draft                     AODV                     2 March 2001

9. AODV and Aggregated Networks

AODV has been designed for use by mobile nodes with IP addresses

that are not necessarily related to each other, to create an ad hoc

network.  However, in some cases a collection of mobile nodes MAY

operate in a fixed relationship to each other and share a common

subnet prefix, moving together within an area where an ad hoc network

has formed.  Call such a collection of nodes a ``subnet''.  In this

case, it is possible for a single node within the subnet to advertise

reachability for all other nodes on the subnet, by responding with

a RREP message to any RREQ message requesting a route to any node

with the subnet routing prefix.  Call the single node the ``subnet

router''.  In order for a subnet router to operate the AODV protocol

for the whole subnet, it has to maintain a destination sequence

number for the entire subnet.  In any such RREP message sent by the

subnet router, the Prefix Size field of the RREP message MUST be

set to the length of the subnet prefix.  Other nodes sharing the

subnet prefix SHOULD NOT issue RREP messages, and SHOULD forward RREQ

messages to the subnet leader.

10. Using AODV with Other Networks

In some configurations, an ad hoc network may be able to provide

connectivity between external routing domains that do not use AODV.

If the points of contact to the other networks can act as subnet

routers (see Section 9) for any relevant networks within the external

routing domains, then the ad hoc network can maintain connectivity to

the external routing domains.  Indeed, the external routing networks

can use the ad hoc network defined by AODV as a transit network.

In order to provide this feature, a point of contact to an external

network (call it an Infrastructure Router) has to act as the subnet

router for every subnet of interest within the external network for

which the Infrastructure Router can provide reachability.  This

includes the need for maintaining a destination sequence number for

that external subnet.

If multiple Infrastructure Routers offer reachability to the same

external subnet, those Infrastructure Routers have to cooperate (by

means outside the scope of this specification) to provide consistent

AODV semantics for ad hoc access to those subnets.

11. Extensions

RREQ and RREP messages have extensions defined in the following

format:

Perkins, Royer, Das          Expires 2 September 2001          [Page 20]

Internet Draft                     AODV                     2 March 2001

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|     Type      |    Length     |     type-specific data ...

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

where:

Type     1

Length   The length of the type-specific data, not including the

Type and Length fields of the extension.

Extensions with types between 128 and 255 may NOT be skipped.  The

rules for extensions will be spelled out more fully, and conform with

the rules for handling IPv6 options.

11.1. Hello Interval Extension Format

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|     Type      |    Length     |       Hello Interval ...      |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

| ... Hello Interval, continued |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Type     2

Length   4

Hello Interval

The number of milliseconds between successive

transmissions of a Hello message.

The Hello Interval extension MAY be appended to a RREP message with

TTL == 1, to be used by a neighboring receiver in determine how long

to wait for subsequent such RREP messages (i.e., Hello messages; see

section 8.7).

12. Configuration Parameters

This section gives default values for some important values

associated with AODV protocol operations.  A particular mobile

node may wish to change certain of the parameters, in particular

the NET_DIAMETER, NODE_TRAVERSAL_TIME, MY_ROUTE_TIMEOUT,

Perkins, Royer, Das          Expires 2 September 2001          [Page 21]

Internet Draft                     AODV                     2 March 2001

ALLOWED_HELLO_LOSS, RREQ_RETRIES, and possibly the HELLO_INTERVAL. In

the latter case, the node should advertise the HELLO_INTERVAL in its

Hello messages, by appending a Hello Interval Extension to the RREP

message.  Choice of these parameters may affect the performance of

the protocol.

Parameter Name           Value

----------------------   -----

ACTIVE_ROUTE_TIMEOUT     3,000 Milliseconds

ALLOWED_HELLO_LOSS       2

BLACKLIST_TIMEOUT        RREQ_RETRIES * NET_TRAVERSAL_TIME

BROADCAST_RECORD_TIME    2 * NET_TRAVERSAL_TIME

DELETE_PERIOD            see note below

HELLO_INTERVAL           1,000 Milliseconds

LOCAL_ADD_TTL            2

MAX_REPAIR_TTL           0.3 * NET_DIAMETER

MIN_REPAIR_TTL           see note below

MY_ROUTE_TIMEOUT         2 * ACTIVE_ROUTE_TIMEOUT

NET_DIAMETER             35

NEXT_HOP_WAIT            NODE_TRAVERSAL_TIME + 10

NODE_TRAVERSAL_TIME      40

REV_ROUTE_LIFE           NET_TRAVERSAL_TIME

NET_TRAVERSAL_TIME       3 * NODE_TRAVERSAL_TIME * NET_DIAMETER / 2

RREQ_RETRIES             2

TTL_START                1

TTL_INCREMENT            2

TTL_THRESHOLD            7

The MIN_REPAIR_TTL should be the last known hop count to the

destination.

DELETE_PERIOD should be an upper bound on the time for which an

upstream node A can have a neighbor B as an active next hop for

destination D, while B has invalidated the route to D. Beyond this

time B can delete the route to D. The determination of the upper

bound somewhat depends on the characteristics of the underlying link

layer.  For example, if the link layer feedback is used to detect

loss of link DELETE_PERIOD must be at least ACTIVE_ROUTE_TIMEOUT.

If there is no feedback and hello messages must be used,

DELETE_PERIOD must be at least maximum of ACTIVE_ROUTE_TIMEOUT

and ALLOWED_HELLO_LOSS * HELLO_INTERVAL. If hello messages are

received from a neighbor but data packets to that neighbor are

lost, (due to temporary link asymmetry, e.g.)  we have to make more

concrete assumptions about the underlying link layer.  We assume

that such asymmetry cannot persist beyond a certain certain time,

say, a multiple K of ALLOWED_HELLO_LOSS * HELLO_INTERVAL. In other

words, it cannot not be the case that a node receives K subsequent

Perkins, Royer, Das          Expires 2 September 2001          [Page 22]

Internet Draft                     AODV                     2 March 2001

hello messages from a neighbor, while that same neighbor fails to

receive any data packet from the node in this period.  Covering all

possibilities,

DELETE_PERIOD = K * max (ACTIVE_ROUTE_TIMEOUT,

ALLOWED_HELLO_LOSS * HELLO_INTERVAL) (K = 5 is recommended).

NET_DIAMETER measures the maximum possible number of hops between

two nodes in the network.  NODE_TRAVERSAL_TIME is a conservative

estimate of the average one hop traversal time for packets and should

include queueing delays, interrupt processing times and transfer

times.  ACTIVE_ROUTE_TIMEOUT SHOULD be set to a longer value (at

least 10,000 milliseconds) if link-layer indications are used to

detect link breakages such as in IEEE 802.11 [2] standard.  TTL_START

should be set to at least 2 if Hello messages are used for local

connectivity information.  Performance of the AODV protocol is

sensitive to the chosen values of these constants, which often depend

on the characteristics of the underlying link layer protocol, radio

technologies etc.  BLACKLIST_TIMEOUT should be suitably increased

if expanding ring search is used.  In such cases, it should be

(TTL_THRESHOLD - TTL_START)/TTL_INCREMENT + 1 + RREQ_RETRIES. This is

to account for possible additional route discovery attempts.

13. Security Considerations

Currently, AODV does not specify any special security measures.

Route protocols, however, are prime targets for impersonation

attacks, and must be protected by use of authentication techniques

involving generation of unforgeable and cryptographically strong

message digests or digital signatures.  It is expected that, in

environments where security is an issue, that IPSec authentication

headers will be deployed along with the necessary key management to

distribute keys to the members of the ad hoc network using AODV.

14. Acknowledgments

We acknowledge with gratitude the work done at University of

Pennsylvania within Carl Gunter's group, as well as at Stanford and

CMU, to determine some conditions (especially involving reboots and

lost RERRs) under which previous versions of AODV could suffer from

routing loops.  Contributors to those efforts include Karthikeyan

Bhargavan, Joshua Broch, Dave Maltz, Madanlal Musuvathi, and

Davor Obradovic.  The idea of a DELETE_PERIOD, for which expired

routes (and, in particular, the sequence numbers) to a particular

destination must be maintained, was also suggested by them.

Perkins, Royer, Das          Expires 2 September 2001          [Page 23]

Internet Draft                     AODV                     2 March 2001

We also acknowledge the comments and improvements suggested by SJ Lee

(especially regarding local repair) and Mahesh Marina.

References

[1] S. Bradner.  Key words for use in RFCs to Indicate Requirement

Levels.  Request for Comments (Best Current Practice) 2119,

Internet Engineering Task Force, March 1997.

[2] IEEE 802.11 Committee, AlphaGraphics #35, 10201 N.35th Avenue,

Phoenix AZ 85051.  Wireless LAN Medium Access Control MAC and

Physical Layer PHY Specifications, June 1997.  IEEE Standard

802.11-97.

[3] Charles E. Perkins.  Terminology for Ad-Hoc Networking (work in

progress).  draft-ietf-manet-terms-00.txt, November 1997.

Perkins, Royer, Das          Expires 2 September 2001          [Page 24]

Internet Draft                     AODV                     2 March 2001

Author's Addresses

Questions about this memo can be directed to:

Charles E. Perkins

Communications Systems Laboratory

Nokia Research Center

313 Fairchild Drive

Mountain View, CA 94303

USA

+1 650 625 2986

+1 650 691 2170 (fax)

charliep@iprg.nokia.com

Elizabeth M. Royer

Dept. of Computer Science

University of California, Santa Barbara

Santa Barbara, CA 93106

+1 805 893 3411

+1 805 893 8553 (fax)

eroyer@cs.ucsb.edu

Samir R. Das

Department of Electrical and Computer Engineering

& Computer Science

University of Cincinnati

Cincinnati, OH 45221-0030

+1 513 556 2594

+1 513 556 7326 (fax)

sdas@ececs.uc.edu

Perkins, Royer, Das          Expires 2 September 2001          [Page 25]